## Slide 1: Progress with System Integration of the CBM Silicon Tracking Detector
Johann M. Heuser, GSI Helmholtz Center for Heavy Ion Research, Darmstadt, Germany
for the CBM Collaboration
DPG Frühjahrstagung, Münster, Germany, 27 March 2017

## Slide 2: STS - Task & integration challenges
STS ladder arrangement
pile-up free track point determination in high-rate collision environment:
  105  107/s (A+A), up to 109/s (p+A), track multiplicities up to 700/collision
  momentum resolution p/p  1-2%
physics aperture : 2.5    25
8 tracking stations: 0.3 m  z  1.0 m
  material :  0.3 % – 1% X0 per station
  896 detector modules , 106 ladders
double-sided silicon microstrip sensors
  hit spatial resolution  25 µm
  operation at T = -5 C (radiation field)
1.8 million r/o channels, 14 000 r/o ASICs
  time-stamp resolution  5 ns
  power dissipation:  40 kW

## Slide 3: STS - Task & integration challenges
STS ladder arrangement
pile-up free track point determination in high-rate collision environment:
  105  107/s (A+A), up to 109/s (p+A), track multiplicities up to 700/collision
  momentum resolution p/p  1-2%
physics aperture : 2.5    25
8 tracking stations: 0.3 m  z  1.0 m
  material :  0.3 % – 1% X0 per station
  896 detector modules , 106 ladders
double-sided silicon microstrip sensors
  hit spatial resolution  25 µm
  operation at T = -5 C (radiation field)
1.8 million r/o channels, 14 000 r/o ASICs
  time-stamp resolution  5 ns
  power dissipation:  40 kW
Challenges:
precision assembly of modules, ladders, stations
cooling of front-end electronics
cold sensors – thermal enclosure
routing of cables/cooling tubes
installation into dipole magnet

## Slide 4: Integration – from modules to stations
front-end board in cooling block
896 modules
8 tracking stations
18 mechanical half-units
C-frame
ultra-thin r/o cables
sensor
read-out + power boards
106 ladders
8-10 modules

## Slide 5: Progress with module assembly
GSI-Detector Lab
Work flow, per side:
TAB bonding of microcables to ASICs
TAB bonding of microcables to silicon sensor
die- and wire-bonding of ASICs to FEB
gluing of shielding layers and spacers

## Slide 6: Progress with module assembly
dummy modules produced during set-up of assembly line

## Slide 7: Detector ladders
silicon sensors
carbon ladder
ladder holder
fixed bearing side
floating bearing side
Beampipe cut-out for central ladders
sensor mounting with “L-legs”

## Slide 8: Carbon fiber ladders
hub from Al, 130 cm long
carbon fiber structure dimensions:
  base: 6.1 cm
  height: 2.0 cm
  length: 120 cm
  tube supports: 1.5/0.5 mm 
hub
prototypes made in aerospace industry, Germany

## Slide 9: Progress with ladder assembly
concept tool
sensor 1
sensor 2

## Slide 10: Progress with ladder assembly
concept tool
sensor 1
sensor 2

## Slide 11: Progress with ladder assembly
concept tool
sensor 1
sensor 2
placement accuracy < 100 m
optical survey
position refinement with tracks < 10 m

## Slide 12: STS in Dipole Magnet
Runner block
Cryogenic pipe
Rail
Rail support
Baseplate
8mm
bottom magnet coil
Thermal
insulation box
top magnet coil
20mm
300 cm
144 cm

## Slide 13: Progress with STS CAD model
Sandwich concept:
Lightweight and stiff
Parameters depend on filler material
Versatile configuration
Further development requires:
Thermal testing
Requirement summary
Coordination with industrial manufacturers
Design concept:
Cable routing
Unit disassembly
Integrated design
Thickness: 40mm
CF composite
Filler material/structure
Peripheral cabling design
Cable Stacks
Further CAD development:
Finalize cabling concept
Schematic cable routing
Integrated design

## Slide 14: Construction of a mock-up STS
Demo coolers
¼ Unit 07 – detailed CAD:
Cooling pipes
C-Frame integration
CNC pin Al bearing
CNC pin Ceramic bearing
Dowel pin Al bearing
Ruby ball Fiberglas bearing
Status:
CAD finished
Assembly ongoing
Final parts manufacturing
  FEB dummies
  ROB/POB dummies
Testing of different types of ladder bearings:
Set-up to study thermal management of FEE
water cooling  CO2 cooling

## Slide 15: Development of ladder handling tool
Longitudinal bearing fixture
Lateral bearing fixture
FEB Box fixture
Holding area
Design issues:
Stress free ladder handling
Variable length for multiple ladder types
Mounting and dismounting from Master jig to C-Frame
Sufficient precision
Easy handling
Status
First prototype assembled
Tests ongoing
Mounting of Mock-up ladders planned
[Square rail and brackets from IGUS]

## Slide 16: LV/HV powering scheme
Sensor bias: ± 200 V, common ground
FEE floating
ASIC powering: ~ 2.2 V, ca. 4 A (per FEB) by a FEAST DC/DC converter
Two LDOs convert to 1.8 V (digital) and 1.2 V (analog)
12 V, ca. 1 A, and HV are delivered from outside STS

## Slide 17: Summary
Challenges of CBM-STS system integration:
  precision assembly and mounting of its components, to yield the final spatial resolution
  fast front-end electronics requires efficient cooling (CO2)
  cold operation of sensors requires thermal enclosure
  routing of services
  installation in dipole magnet
Module assembly: fully developed, dummy modules produced.
  FEB under development for functional modules
Ladder assembly: procedure and tooling under development
System integration:
  CAD well advanced, in concept and detail
  ¼ unit demonstrator and cooling demonstrators under construction
  electronics & powering components being produced
  open topic: beam pipe section in STS
Aim to advance system integration towards production readiness in 2018.

## Slide 18
STS assembly and integration flow

## Slide 19: Key project institutes:
GSI-FAIR, Darmstadt, Germany
JINR, Dubna, Russia
Univ. Tübingen, Germany
KIT, Karlsruhe, Germany
AGH, Cracow, Poland; JU, Cracow, Poland; WUT, Warsaw, Poland
Assembly Centers: GSI-FAIR, JINR -VBLHEP