## Slide 1
Outline:
Introduction
CBM TOF requirements
Tof wall arrangements
Ceramics RPC and the central region of the ToF wall
Beam-time @ SPS Nov. 2015
Beam-time @ SPS Nov. 2016
TOF Project timeline
TOF FAIR Phase 0 project
Summary and Outlook
Ingo Deppner for the CBM-TOF Group
Physikalisches Institut der Uni. Heidelberg
DPG – Frühjahrstagung 2017
The CBM Time-of-Flight wall

## Slide 2
Introduction
1 ns
TRD
TOF
ECAL
RICH
Dipole magnet
PSD
MVD & STS
MUCH
The Compressed Baryonic Matter Experiment
CBM overview talk: HK30.1 Group reports: 6 Short reports: 41 Poster: 8
Tracking acceptance: 2 < Lab < 25
Free streaming DAQ
Software based event selection
Rint = 10 MHz (Au + Au)
High net-baryon densities

## Slide 3
Incident particle flux
URQMD simulated charged particle flux from Au + Au events for an interaction rate of 10 MHz
Flux ranging from 0.1 to 100 kHz/cm2
At different regions Time-of-Flight detectors with different rate capabilities are needed
kHz/cm2
kHz/cm2

## Slide 4
Requirements
80 W
120 W
1 ns
RPC
twisted pair cabe
twisted pair cabe
feed through gas box
CBM-ToF Requirements
Full system time resolution sT ~ 80 ps
Efficiency > 95 %
Rate capability  30 kHz/cm2
Polar angular range 2.5° – 25°
Active area of 120 m2
Occupancy < 5 %
Low power electronics
(~120.000 channels)
Free streaming data acquisition
Charged hadron identification is provided by Time-of-Flight (ToF) measurement
Multi-gap Resistive Plate Chambers (MRPC) are the most suitable ToF detectors fulfilling our requirements

## Slide 5
TDR ToF wall layout
6 types of modules (M1 – M6) only
A module contains several MRPC counters
Region containing counters equipped with float glass
Region containing counters equipped with low resistive glass
Region containing counters equipped with ceramic material

## Slide 6
Ceramic RPCs for BFTC
1200 mm
24 mm
400 mm
1 module
400 RPCs
BFT0C = 8 modules
1 RPC
3 cells
1 cell
2 gaps
Important scopes of High Energy Heavy Ion experiments are the start-time and the reaction-plane determination. For CBM the use of RPC for the Beam Fragmentation T0 Counter (BFT0C) with low resistive radiation hard ceramics electrodes and small chess-board like single cells is under consideration.

## Slide 7
4  109 Ωcm: most suitable resistivity order for our aims
electrodes
RPC
Ceramic RPCs for BFTC

## Slide 8
Resistive Glass Development
Resistive glass for high-rate MRPCs is developed in Beijing, China
Aging tests
Raw resistive glass material for 400 m2

## Slide 9
About 1100 channels
20 MRPC
CBM TOF module
Beam-time @ SPS North Area in Nov. 2015
Beam: Lead @ 30A GeV Target: Lead 1 mm
Intensity: 107 / spill
Spill length: 8 s
Rates: few 100 Hz/cm2 - 1 kHz/cm2
Energy close to SIS300 conditions
Upper setup
Lower setup
Beam
 = 3.5
 = 6
Beam-time @ SPS in Nov. 2015

## Slide 10
Alternative solution with Pad-MRPCs is available
Beam-time @ SPS in Nov. 2015

## Slide 11
Beam-time @ SPS in Nov. 2015
Counter time resolution about 46 ps
Efficiency about 97 %
Cluster size > 2
Particle flux only a few hundred Hz/cm2

## Slide 12
Module M5
Beam-time @ SPS in Nov. 2015

## Slide 13
Beam-time @ SPS in Nov. 2015
Counter time resolution about 60 ps
Efficiency about 97 %
Cluster size about 1.5
MRPC3a prototypes

## Slide 14
80 W
1 ns
Beam-time @ SPS in Nov. 2016
Beam
Target
Beam-time @ SPS North Area in Nov. 2016
Beam: Lead @ 158A GeV Target: 4 mm Pb (+ 10 cm Fe)
Rates: few 200 Hz/cm2 - 1 kHz/cm2
Target
Fe
Fe
Pb
Diamond
Event Display
two multiplicity 8 tracks found

## Slide 15
80 W
1 ns
Beam-time @ SPS in Nov. 2016
~ 500 Channels with the new “CLOSE TO FINAL” Free-streaming Readout-Chain:
PADI / GET4 / AFCK / FLIB => DAQ was running stable

## Slide 16
80 W
1 ns
Beam-time @ SPS in Nov. 2016
Mostly epoch markers!

## Slide 17
Module M5
0.28
13
12
140
Beam-time @ SPS in Nov. 2016

## Slide 18
80 W
1 ns
Backup Slides
Dut: 911
Mref: 910
Bref: 500
Sel2: 921
Efficiency about 93%
Cuts: 2(Dut-Mref) = 10 2(Mref-Sel2) = 3 Selected Mref area 0.5
System time resolution
MRPC3b
Beam-time @ SPS in Nov. 2016
Analysis ongoing

## Slide 19
Time line
Full-size demonstrator end 2012
TDR approved mid. 2015
Full-size modules mid. 2015
Full-size modules with ‘final’ electronics mid. 2016
Construction of the modules 2017- 2020
Integration in STAR@RHIC@BNL 2017- 2018
eTOF ready for beam 01.01.2019
Integration in CBM@SIS100@FAIR 2019- 2021
ToF ready for beam 01.06.2023
RPC type | res. material | efficiency | time resolution | rate capability
Ceramic MRPC | Ceramic |  90 % |  100 ps |  150 kHz/cm2
MRPC1/2 | sem. glass | > 95 % |  50 ps | > 30 kHz/cm2
MRPC3a | sem. glass | > 95 % |  60 ps | > 30 kHz/cm2
MRPC3b | float glass | > 95 % |  50 ps |  1.5 kHz/cm2
The prototype MRPC counters fulfill the CBM TOF requirements
ToF – Project Timeline

## Slide 20
The TOF FAIR Phase 0 program
Particle flux < 45 Hz/cm2, Multi-hit probability < 7.4%
Location of CBM eTOF modules

## Slide 21
Benefit for STAR:
providing critical TOF coverage for BES II
- PID extension to y = 1.2 in collider mode
- access to energies from 4.5 to 7.7 GeV in the fixed target program
Benefit for CBM:
providing a large-scale integration test of the CBM TOF system, including PID and calibration of the detectors (hardware and software)
preparation for day one experiment at SIS 100
Benefit for CBM-TOF group members:
participation in the analysis of the physics data provided by the CBM TOF detectors, including authorship of any publications from this data.
The TOF FAIR Phase 0 program

## Slide 22
Summer 2016 shipping a real size module to BNL and installing it on the east side pole of STAR
Feb. 2017 1st system integration test with one module by participating in the Run17 beam time in STAR
Fall 2017 shipping and installation of one sector
Feb. 2018 2nd system integration test with one sector by participating in the Run18 beam time in STAR
Summer 2018 shipping all 36 modules including infrastructure (gas system, LV-, HV-power supply) to BNL
Fall 2018 Installation and commissioning
Feb 2019 Start of the BES II campaign
Summer 2021 Decommissioning and shipping of all modules including infrastructure to FAIR
Milestones
The TOF FAIR Phase 0 program

## Slide 23
Open module
Module fixed at the pole-tip
Module installation in Oct. 2016
The TOF FAIR Phase 0 program
about 100 Hz/cm2
Running (Mar. 2017)

## Slide 24
Summary and outlook
80 W
1 ns
CBM TOF started system performance tests under realistic load conditions
Counters maintain their performance so far
Preproduction about to start (QC, QA procedures initiated)
R&D for BFTC ongoing
FAIR phase 0 started - looking forward to physics

## Slide 25
Thank you for your attention
Contributing institutions:
Tsinghua Beijing,
NIPNE Bucharest,
GSI Darmstadt,
IRI Frankfurt
USTC Hefei,
PI Heidelberg,
ITEP Moscow,
HZDR Rossendorf,
CCNU Wuhan,
Special thanks go to:
Norbert Herrmann

## Slide 26
Backup
80 W
1 ns
Backup Slides

## Slide 27
Backup Slides
CBM Physics topics
Deconfinement / phase transition at high ρB
QCD critical endpoint
The equation-of-state at high ρB
chiral symmetry restoration at high ρB
Observables
excitation function and flow of strangeness and charm
collective flow of hadrons
particle production at threshold energies
excitation function of event-by-event fluctuations
excitation function of low-mass lepton pairs
in-medium modifications of hadrons (ρ,ω,φ → e+e-(µ+µ-), D)
non twisted part
connector
p
p
K
D. Kresan Au + Au @ 25GeV
Kaon acceptance depends critically on TOF resolution

## Slide 28
PID capability
80 W
1 ns

## Slide 29
Working principle of an RPC
E0 = 120 kV/cm
E. Cerron Zeballos et al., Nucl.Instrum.Meth. A374 (1996) 132-136
Time resolution:
Efficiency:
: incident ch. particle flux, : electrode bulk resistivity, d: electrode thickness
How to increase the rate capability?
First Multi-gap RPC 1996
E. Cerron Zeballos et al., Nucl.Instrum.Meth. A374 (1996) 132-13
  3x1012 cm
  1010 cm

## Slide 30
Engineering design of the CBM experiment
TOF
TRD
RICH
Magnet
Nominal ToF position is between 6 m and 10 m from the target
Movable design allows for optimization of the detection efficiency of weakly decaying particles (Kaons)
Backup Slides

## Slide 31
Backup Slides

## Slide 32
Backup Slides

## Slide 33
Backup Slides

## Slide 34
80 W
1 ns
Freeze the design by March. Start counter assembly from April.
Produce 10 MRPC3a/b as “Pre-mass production”.
Check the performance and use for summer installation @ STAR.
Finish production by November.
Send to Heidelberg in three batches.
Production Readiness Review

## Slide 35
1 Track (blue) with hit multiplicity 8
2 Tracks (green) with hit multiplicity 7
1 Track (light blue) hit with multiplicity 6
1 Track (pink) with hit multiplicity 5
Event display after position calibration
The opportunity to reconstruct tracks offers new possibilities to analyze and study the counters in much greater detail: multi hit response, 2d position dependencies
Beam-time @ SPS in Nov. 2015
RPC Hits
RPC layers
Tracks