## Slide 1: Finalizing the CBM-MVD Geometry: CAD and Simulation
Philipp Klaus on behalf of the CBM-MVD Collaboration
klaus@physik.uni-frankfurt.de
81. Jahrestagung der DPG und DPG-Frühjahrstagung, Münster
30. März 2017, HK 53.7, 18:30
This work has been supported by BMBF (05P15RFFC1), GSI and HIC for FAIR

## Slide 2: Outline
  Updated sensor dimensions
  Geometries of the MVD: Mechanics & Simulation
  Comparison Cad2Root ⇿ Scripting in Root
  New MVD Geometry via Scripting
  Summary

## Slide 3: Need for Geometry Change due to Update of Sensor Dimensions
Preliminary
Previous (assumed) sensor:
“3x FSBB”
New (assumed) sensor:
“MIMOSIS-1”
30mm
13mm
10mm
Pixel Matrix (sensitive) 1024x504 pixel
Readout Part (insensitive)
31mm
16mm
13mm

## Slide 4: Plot Legend
Quadrant acceptance of previously assumed 3xFSBB quadrant composition
(PhD Thesis of Tobias Tischler)
Quadrant acceptance with new (assumed) MIMOSIS-1
sensor dimensions, if same sensor arrangement to be used as in
PhD Thesis of Tobias Tischler
Overlap area of sensors on front and back side of the carrier with new sensor dimensions

## Slide 5: Plot Legend
Nominal CBM
acceptance limits:
2.5 degrees
25 degrees
Actual inner CBM-MVD acceptance limit:
Begin of acceptance
Fully established acceptance
Resulting beam hole

## Slide 6: Acceptance Coverage: Station 0

## Slide 7: Acceptance Coverage: Station 1

## Slide 8: Acceptance Coverage: Station 2

## Slide 9: Acceptance Coverage: Station 3

## Slide 10: Result of Updated Sensor Dimensions
  For some stations, the new sensor dimensions allow to reduce the integration complexity by removing some rows of sensors.
  The MVD geometries for engineering and simulation need to be updated.
      This is where the problems started…

## Slide 11: Geometry Status of the MVD up to now
→ Geometry for Engineering / Mechanics
→ Geometry for CbmRoot Simulations
←software: same→
← look: similar →
← still: quite different →
← required: consistency →
Where they differ, there should be a justified reason such as:
Simulation Speed
Simplicity
Particle distributions
Parametric feature based modelling (“CAD”) with Autodesk Inventor

## Slide 12: Workflow of the “Cad2Root ” Conversion Approach For CbmRoot Geometries
Export to STEP →
[Autor: Dr. Tobias Stockmanns, FZ Jülich]
Material Map
Cad2Root
↓
https://panda-wiki.gsi.de/foswiki/bin/view/Computing/CadConverter
ROOT File with Geometry
→
→
Simulation w/ CbmRoot
Dependencies
(OpenCascade)
↓

## Slide 13: Cad2Root Conversion Aspects
New geometry will be scripted in a ROOT macro instead of being created with Cad2Root.
Using Parametric feature based modelling (“CAD”) with Autodesk Inventor
Why good / Pros:
Creating the geometry can be done very quickly if experienced with CAD software
Work can be offloaded if you have an engineering department
Component interferences can be checked and visually inspected nicely
Interferences with other detectors can be checked well, if also created with CAD software.
Better UI than ROOT.
Why bad / Cons:
Many dependencies for the conversion:
  Cad2Root, FairROOT, OpenCascade
More difficult to track changes to the geometry (no text file in version control)
Bigger workflow for changes
Small userbase of Cad2Root / maintenance needed to keep up to date

## Slide 14: Previous Approaches to CAD ↔ ROOT Conversion (for completeness)
STEP-to-ROOT – from CAD to Monte Carlo Simulation Tobias Stockmanns 2012 J. Phys.: Conf. Ser. 396 022050 DOI: https://doi.org/10.1088/1742-6596/396/2/022050
Development and application of CATIA-GDML geometry builder S Belogurov et al 2014 J. Phys.: Conf. Ser. 513 022003 DOI: http://iopscience.iop.org/article/10.1088/1742-6596/513/2/022003
TGeoCad: an Interface between ROOT and CAD Systems C Luzzi and F Carminati 2014 J. Phys.: Conf. Ser. 523 012017 DOI: https://doi.org/10.1088/1742-6596/523/1/012017
“Cad2Root”
STEP → ROOT
CATIA ↔ ROOT
ROOT → STEP

## Slide 15: Scripting a new Geometry in Root
Documentation
Root User Guide (v5.34) chapter ”The Geometry Package”: https://root.cern.ch → Documentation → User’s Guides → User’s Guides (all formats and series) → HTML – Geometry
FairRoot HowTo “Detector Geometry and Media”: https://fairroot.gsi.de → HowTo → Detector Geometry and Media
In short:
Define Materials, Media, Shapes, Volumes, Volume Assemblies, and instances of the Volumes positioned in a mother volume using a transformation Matrix.
TGeoMaterial
TGeoMedium
TGeoShape
TGeoVolume
TGeoBBox
TGeoVolumeAssembly
TGeoNode
TGeoMatrix
Relevant classes in Root:

## Slide 16: Structure of the New, Scripted CBM-MVD Geometry
Preliminary
Legend (Root Classes):

## Slide 17: Current Status - Scripted Geometry
Preliminary
An impression in 3D
(station position in z-direction streched)
  A success so far.
  Up next: MVD Digitizer to be adapted to work with the new geometry.

## Slide 18: Current Status - Scripted Geometry Stations 0 and 1
Height: identical for all 4 stations
S0
S1
y
x
z
Preliminary
23.1 cm
31.1 cm

## Slide 19: Current Status - Scripted Geometry Stations 2 and 3
Last station:
Heatsink fully quadratic
Height: identical for all 4 stations
S2
S3
y
x
z
Preliminary
34.34 cm
37.7 cm

## Slide 20: Summary
  Changed sensor dimensions require an update of the MVD geometry
  Move away from Cad2Root → geometry scripted in Root
  Goals for the scripted geometry:
    First step: reproduce current v15a MVD geometry
    Next step: update for the changed sensor dimensions
    Next next step: evaluate additional station configurations of the MVD to cover more physics cases
    Thank you for your attention! If you are interested in the slides, write to: klaus@physik.uni-frankfurt.de
→ simulation →
feedback
sensor
design