## Slide 1
Muon System Digital Electronics
(prototype design)
N.Zhuravlev, JINR/Dubna
Novosibirsk, September, 2017

## Slide 2
Electronics for PANDA Muon System
Simplified Block diagram of the data stream
- The total number of readout channels in Muon System is about 100000
- The time resolution of the mini-drift tubes - 100÷200ns
- The average hit rate from Muon System is about 30 hits/interaction
- The expected data rate for Muon System is about 19 Gbps
- Digital unit operates as an input register (so called “Latch mode”).
- The most-effective solution for Digital Electronics is the use of FPGA architecture
- The design Digital unit on the basis of Xilinx FPGA XC7A200 (Artix 7 Family) is in progress
The purpose is to test efficiency of this chip
- The unit will be functionally analogous to COMPASS digital R/O unit on the basis of TDC F1

## Slide 3
Simplified Block-diagram of Xilinx FPGA Prototype R/O Module (192ch) (to be tested with Range System Prototype at CERN; if the results will be positive, the Artix 7 chip may be regarded as the basis for the final PANDA/DAQ)

## Slide 4
DIGITAL 6U VME R/O UNIT STRUCTURE
Mezzanine board
Motherboard
(FPGA/Artix 7)
96 ch
LVDS
Threshold
Analog Electronics
LVDS
3
Threshold
96 ch
LVTTL
96
3
Interface board
USB -> JTAG
Remote Config
Interface
JTAG
CONFIG.
DATA
Programming Module
for Xilinx FPGA (DIGILENT)
RS-485
DAQ
3
Consists of 3 boards:
S
SMT1
(192 channel, VME 6U, double width)
(stand Config)

## Slide 5
Approximate view of Prototype Digital Module (to be tested with prototype at CERN)
DAQ Interface
Micro USB
RJ-45
RS-485 In
RS-485 Out
USB-JTAG
RJ-45
RJ-45
RJ-45
USB
RJ-45
Interface board
FPGA
Artix 7
P1
P2
will be removed: 6 F1(192 ch.), Initialization card, RJ-45
Will be installed: FPGA, Interface card (connected via P2 VME connector)
COMPASS digital unit (MWDB) is taken as basis
(crossed elements will be removed)
FPGA based digital module

## Slide 6
µController
(STM32F4xx)
Secure Digital
memory Card
(SD)
Switch (ID)
Interface
RS-485
Host PC
MUX
(CPLD)
USB to stand PC
FPGA
Firmware
JTAG
JTAG-SMT1
JTAG
DAQ Interface
DAQ Interface
Hit data
INTERFACE CARD BLOCK DIAGRAM (under discussion)
FPGA
900Kb/s –MOXA
2.8Mb/s – Home-made
0.45/1.4/24 Mb/s
96 Mb/s
MOXA/Home-made/SD
30Mb/s
3 variants for Firmware loading: - Stand (local) PC -> JTAG-SMT programming module -> FPGA
- Host PC -> RS-485 Interface -> µController -> FPGA
- SD -> µController -> FPGA

## Slide 7
VME crate #1
M1
M10
Rt
Interface board
RS-485
(900 Kbps)
FPGA
FPGA
JTAG
Twisted pair cable
VME crate #xx
M1
M10
Rt
Interface board
Port 1
Port8/16
Rackmount serial device server (industrial )
MOXA NPORT 5630-8/16
Home-made device server (2.8 Mbps)
Port 1
Ethernet
Up to 100Mbps
V.1
V.2
FPGA reloding System Structure ( view from back side of VME crate)
- The loading of crates – in parallel
- The loading inside crate – sequentially
- The loading from SD – all modules in
parallel by a broadcast command
Estimated loading time
for the whole PANDA Muon System:
10 sec ÷ 60 min depending on
the loading source (SD/Home-made
server/ MOXA device server)
Host PC

## Slide 8
Status of Muon System Digital Electronics
(prototype design)
The development of the double width VME 6U module on the basis of
Artix 7 Family FPGA is in progress
- Motherboard card circuit diagram is ready for 75%
Mezzanine card circuit diagram is ready for 80%
Interface card circuit diagram is under discussion (block diagram is developed)
The structure of firmware loading system was selected
Plans:
To finish design of the circuit diagrams of the Motherboard and Mezzanine cards,
at the end of the 2017, and to start PCB design
To produce the prototype of Interface card in the first half of 2018
To start tests of the digital VME module with Range System prototype at CERN in 2018
Manpower:
1 student, 1 PhD expert, 1 technician, 1 colleaque from the Moscow State University
(according to the agreement with the University)
- Increasing of manpower is possible depending on available budget