## Slide 1: CRYRING@ESR INTRODUCTION AND OVERVIEW. Operators training.
Svetlana Fedotova

## Slide 2: Agenda
Origin and location of CRYRING@ESR.
Purposes of CRYRING@ESR facility
Injection into CRYRING@ESR
CRYRING ring assembly
CRYRING@ESR commissioning status and future plans

## Slide 3: Origin and location of CRYRING@ESR.
Manne-Siegbahn Laboratory (MSL), Stockholm
1992-2010
GSI, Darmstadt
2013- present
Heavy ion storage ring:
Stores, cooles, accelerates and decelerates heavy HCI.

## Slide 4: Origin and location of CRYRING@ESR.
11 MeV/u
UNILAC
SIS
400 MeV/u
ESR
FRS
4 MeV/u
CRYRING@ESR
17 m
ESR
Local
ion source
E-cooler
RF cavity
Extraction
Target
section
Circumference | 54.17 m (ESR/2)
Vacuum pressure | 10-11-10-12 mbar
Ion energy | < 300 keV/u - 14 MeV/u
Rigidity for ions | 0.054 - 1.44 Tm
Magnet ramping | 1 T/s (4 T/s, 7 T/s)
Stand-alone operation | local ion beam (300 keV/u, q/A > 0.25)
Beam injection | multiturn and fast
Beam extraction | slow and fast
Main CRYRING@ESR characteristics

## Slide 5: Purposes of CRYRING@ESR facility
CRYRING@ESR is a prototype for FAIR
Tests of novel detectors and beam diagnostics systems
Tests of FAIR accelerator control system
Tests of FAIR safety and radiation protection access systems
Standalone operation during commissioning
Training of personnel on new control system
Scientific Opportunities
Heavy HCI (up to U92+ ) at low energy 100 keV/u -10 MeV/u: covers the energy gap between the ESR (> 4 MeV/u) and HITRAP (<10 keV/u)
Exotic short-lived ions: Fast ramping (~1s)
Atomic, nuclear, biophysics, materials research
Photonic, electronic and atomic collisions, extraction towards downstream experiments
  Research may continue even during major shutdowns (at limited ion ranges).

## Slide 6
Strong Field QED in Helium-like Ions
Accurate measurements of binding energies of K-electron in
H- and He-like ions (<1 eV) highest sensitivity to high-order QED corrections
Measurement of X-rays emitted during
K-shell radiative recombination employing
X-ray microcalorimeters
6

## Slide 7
Nuclear Reaction Rates
(p,γ) reactions in novae for g-ray astronomy
DSSD to be used in CRYRING
M. Lestinsky et al. “Physics Book: CRYRING@ESR”
Critical rate for abundance of g-rays
Proof of principle:
96Ru(p,g)97Rh
Mei et al. PRC92 (2015)35803
Notes: With dwarfs of One type develop into novae, want to measure 33Cl p, gamma 34 Argon
Referenz zum Test im ESR Rh cross sections

## Slide 8: Laser Experiments - CRYRING@ESR
x-ray cell?
x-ray cell?
Dielectronic recombination assisted laser spectroscopy
Preparation of polarized ion beams in a storage ring
…
Start with
  24,25Mg+
  9Be+
  …
  H and Li like Pr, Pb, and Bi
Laser lab infrastructure ready
Design of laser beam line ongoing
Detection chamber in production
Development of ion source ongoing

## Slide 9: Ultra High Vacuum & Beam Life Time
V. Shevelko, priv. comm.
Ion pumps
  ~ 10
Cryopumps
NEG pumps
  ~ 100
0.3
15
3 s
15 min
First bake out cycle finished
Mean pressure along the ring 8 x 10-11 mbar
2 min
0.4 s

## Slide 10: Injection into CRYRING@ESR
Injection
Ion source
ESR
E-cooler
RF-cavity
Extraction

## Slide 11: Injection into CRYRING@ESR
Transfer line from ESR towards CRYRING: GTT1VV1T – GHTBMU1
Injection line up to CRYRING ring: GHTBMU1 – YR01MP1I
ESR ion beams: from He (Z=1) to U (Z=92)
Injection energy at CRYRING: from 4 MeV/u to 14 MeV/u
Repetition rate: 1 per 60 s
Pulse length: 4 μs
Beam intensity: 107 -108 particle per pulse

## Slide 12
Injection into CRYRING@ESR
Injection septum magnet
PULSED
Injection kicker magnet
PULSED
Injection from ESR
Fast injection mode: pulsed injection septum magnet + pulsed kicker magnet
ESR

## Slide 13: Injection into CRYRING@ESR
Local injection line from the ion source up to the ring:
YRT1IN – YR01MP1
Local ion beams after RFQ: q/A > 0.25: 2H21+, D1+,18Ar1+
Injection energy: 300 keV/u
Repetition rate: 1 Hz
Pulse length: 1 μs – 1 ms
Beam intensity: max 10 μA (6*107 part per 1μs pulse)

## Slide 14
Injection into CRYRING@ESR
Injection septum magnet
DC
Injection bumper
PULSED
Injection from the local ion source
Multiturn injection mode: pulsed electrostatic bumper
Ion source

## Slide 15: CRYRING ring assembly

## Slide 16: CRYRING ring assembly: magnet straight sections
12 Dipoles: ramped
Bending angle 30°
Max field 1.2T
Nom current 1097A
18 Quadrupoles: ramped
12 Focusing
6 Defocusing
Max field 5 T/m
Nom current 336 A
12 Sextupoles:
6 Focusing
6 Defocusing
Max field 27 T/m2
Nom current 10 A
12 Correction dipoles:
6 Vertical
6 Horizontal
Max field 0.03 T
Nom current 10 A

## Slide 17: CRYRING ring assembly
E-cooler:
~20 voltage and current supplies:
7 Guiding magnets for e- beam
Superconducting gun solenoid
Compensation solenoid
2 Correctors + 2 dipols backleg windings
10 Steering coils
RF driven drift tube:
Slow ramping mode (1 T/s)
RF frequency 40 kHz- 2.4 MHz
RF voltage 0-1000Vp-p

## Slide 18: CRYRING ring assembly: Diagnostics
Faraday cups
Screens (MCP, Cromox)
Beam position monitors (BPM)
Schottky pickup
Ionization profile monitors (IPM)
Current transformers (AC, DC)
 For details about the diagnostics see presentation of H. Bräuning

## Slide 19: CRYRING ring assembly

## Slide 20: Local Ion Source
Typical gases so far – H2, D2, Ar
Typical intensities of beam for injection – 40 mA, has been improved starting at 1 mA
Uninterrupted operation time –improved from a few days to weeks
Second version built for fast change over
Other source types (e.g. EBIT) and upgrade of RF Power discussed or already scheduled

## Slide 21: Status of Commissioning
Many turns and RF bunching
Multi turn injection (improving)
Stored Beam Lifetime Measurement in Schottky
0.5 s

## Slide 22: CRYRING@ESR Control room
Cave B
Entrance
TH.1.023
way to CRYRING control room

## Slide 23: CRYRING@ESR Control room
TH.2.034

## Slide 24: CRYRING operations in 2017-2019
AUGUST-SEPTEMBER, 2017
Commissioning with UHV
Operators training
NOVEMBER-DECEMBER, 2017
Commissioning with UHV
First experiment
Operators training
2018-2019
Ready to accept ESR beam
Scheduled dry runs and beam time
For dates, look into plan of accelerator operations and a beam time schedule by S. Reimann