## Slide 1: Lecture on Particle Detectors and Electronic Readout 5th International FAIR School Riva del Sole Castiglione della Pescaia Sept. 4 – 10, 2017
Christian J. Schmidt,
GSI Darmstadt

## Slide 2
Very Large Structures
Engineering
Electronics
Services, Cooling
Finally  Resolution limits are still defined by the fundamental detector physics processes …
ALICE
ATLAS
CBM@FAIR

## Slide 3: Plan
Ionization Detectors
Charged particle tracks, interaction and energy loss
Electronic detection and the detection process
Signal formation on electrodes
Fluctuations in energy loss

## Slide 4: Detection of Radiation
Methods:
Position-sensitive detectors  direction and position of momentum vector
Bending in magnetic field  magnitude of p
Absorption in calorimeter  energy
Cherenkov radiation, time of flight  velocity b
Transition radiation  g
Energy loss  b, g
Characteristic decay of a particle,
detection of secondaries  m
Goal: Measurement of 4-momentum and position in space of particles
Detection by interaction with detector material:
electromagnetic interaction with DE<<E
interaction with DE~E (calorimtery)
[Claus Grupen, Particle Detectors, Cambridge, 1996]

## Slide 5
Cloud Chamber, C.T.R. Wilson 1910
Charges act as condensation nuclei in supersaturated water vapor
Alphas, Philipp 1926
Positron discovery, Carl Andersen 1933
V- particles, Rochester and Wilson, 1940ies

## Slide 6
Nuclear Emulsion, M. Blau 1930`ies
C. Powell, Discovery of muon and pion, 1947
Kaon Decay into 3 pions, 1949
Cosmic Ray Composition
Charges initiate a chemical reaction that blackens the emulsion (photographic film)

## Slide 7
Bubble Chamber, D. Glaser 1952
Charges create bubbles in superheated liquid, e.g. propane or Hydrogen (Alvarez)
Discovery of the f- in 1964
Neutral Currents 1973
Charmed Baryon, 1975

## Slide 8
Spark Chamber, 1960ies
Charges create ‘conductive channel’ which initiates a spark in case HV is applied.
Discovery of the Muon Neutrino 1960ies

## Slide 9
Electric Registration of Geiger Müller Tube Signals
Charges create a discharge in a cylinder with a thin wire set to HV. The charge is measured with a electronics circuit consisting of tubes  electronic signal.
W. Bothe, 1928
B. Rossi, 1932
Cosmic Ray Telescope 1930ies

## Slide 10: ... more modern: collect signals as electronic charges
electronic signals can be read out electronically  computers
can go to higher...
  granularity (millions of very small pixels)
  faster and faster signal readout  higher intensities reveal rarest effects
Gaseous detector, e.g. Ar/CO2:
q ~ 100 e-/cm (MIP)
internal amplification necessary
quencher gas necessary
Solid state detector  Silicon, Diamond etc.:
q~10000 e-/100 mm (MIP)
detectable with low-noise amplifier
What do we need to make a detector?

## Slide 11
Z2 electrons, q=-e0
Interaction with atomic electrons. The incoming particle loses energy and the atoms are excited or ionized.
Interaction with atomic nucleus. The particle is deflected (scattered) causing multiple scattering of the particle in the material. During this scattering a Bremsstrahlung photon can be emitted.
In case the particle’s velocity is larger than the velocity of light in the medium, the resulting EM shockwave manifests itself as Cherenkov Radiation. When the particle crosses the boundary between two media, there is a probability of the order of 1% to produced and X ray photon, called Transition radiation.
Electromagnetic Interaction of Particles with Matter
M, q=Z1 e0

## Slide 12
Charged particles leave a trail of primary and secondary charges (and excited atoms) along their path:
Electron-Ion pairs in gases and liquids, electron hole pairs in solids.
The produced charges can be registered  Position measurement  Time measurement  Tracking Detectors ....
Cloud Chamber: Charges create drops  photography.
Bubble Chamber: Charges create bubbles  photography.
Emulsion: Charges ‘blacken’ film.
Spark Chamber: Charges produce a conductive channel that creates a discharge  photography
Particle Detection based on Ionization

## Slide 13: Electronic Detection of Ionization
Detector material:
gas  fast collection of e- and ions, e.g. Ne, Ar
liquid  higher density, e.g. liquid Ar
solid  higher density, self-supporting, e.g. semiconductor
Gaseous and Solid State Detectors:
Moving Charges (electric fields) induce electronic signals on
metallic electrodes that can be read by dedicated electronics.
In solid state detectors the charge created by the incoming particle is sufficient for detection.
In gaseous detectors (e.g. wire chamber, GEM-chamber) charges are internally multiplied in order to provide a measurable signal.

## Slide 14: Statistics of Electron-Ion Pair Creation
Encounters with gas atoms are purely random, probability small
 Poisson distribution of number k of ionizing collisions over length L
L/l = mean number of ionizing collisions in L
= mean number of primary e--ion pairs nP
Total number of e--ion pairs: primary and secondary ionization
x = 1st term of Bethe-Bloch equation
D = mean energy loss in thickness L
W = effective average energy to produce one e--ion pair,
usually W>I, since part of energy lost by excitation,
empirical determination
= 1/
~
~
the total number is larger than the number of primary charges
s = cross section for ionization
n = number density
Characteristic length: mean free path between ionizing collisions
efficiency of gaseous detector allows to find l and thus si

## Slide 15: Properties of Gases
Gas | Z | A | d | Eex | Ei | I | W | dE/dx |  | nP | nT
 |  |  | (g/cm3) | (eV) | (eV) | (eV) | (eV) | (MeV/g cm-2) | (keV/cm) | (ip/cm) | (ip/cm)
He | 2 | 4 | 1.66E-4 | 19.8 | 24.5 | 24.6 | 41 | 1.94 | 0.32 | 5.9 | 7.8
N2 | 14 | 28 | 1.17E-3 | 8.1 | 16.7 | 15.5 | 35 | 1.68 | 1.96 | (10) | 56
Ne | 10 | 20.2 | 8.39E-4 | 16.6 | 21.5 | 21.6 | 36 | 1.68 | 1.41 | 12 | 39
Ar | 18 | 39.9 | 1.66E-3 | 11.6 | 15.7 | 15.8 | 26 | 1.47 | 2.44 | 29.4 | 94
CO2 | 22 | 44 | 1.86E-3 | 5.2 | 13.7 | 13.7 | 33 | 1.62 | 3.01 | (34) | 91
CH4 | 10 | 16 | 6.70E-4 |  | 15.2 | 13.1 | 28 | 2.21 | 1.48 | 16 | 53
[F. Sauli, CERN 77-09 (1977)]
Properties of some Semiconductors and solid materials
Si 2,3 3,6
Ge 5,3 2,8
Diamond 3,5 5,8
W = mean energy for electron-hole pair

## Slide 16: Energy Loss of Charged Particles
Inelastic collisions
 statistical process (quantum mechanics!)
 mostly small energy losses (< 100 eV in 90% of all collisions)
 rare events with large single-collision energy loss e.g. delta electrons
 total energy loss fluctuates!
Number of collisions per macroscopic path length large
 fluctuations in total energy loss small
 characteristic parameter: average energy loss per unit pathlength
“stopping power”

## Slide 17: towards dE/dx
Wish to know, how a charged ionizing particle interacts with detector.
Photo-Absorption Ionization model: PAI model
What is the energy loss dE in an infinitesimally thin disk of detector material dx? (dx is typically a mass density dx = rdz)
[W.W.M Allison, J.H. Cobb, Ann. Rev. Nucl. Part. Sci. 30, 253 (1980)]

## Slide 18: Bethe-Bloch Formula for Mean Energy Loss dE/dx
independent of mass of incident particle
depends only on velocity of inc. particle
and on I, the mean exitation energy
 main parameter
low energies 
minimum at bg ≈ 3.5 : “MIP” dE/dx|min ~ 1,5 MeV cm2/g
high energies  : relativistic rise
mass stopping power:
 almost independent of material
density effect: polarization of atoms along track
 partly compensates relativistic rise
[K. Nakamura et al. (PDG), J. Phys. G 37, 075021 (2010)]

## Slide 19: Mean Excitation Energy
[Review of Particle Physics, S. Eidelmann et al., Phys. Lett. B 592, 1 (2004)]
I = Z 10eV

## Slide 20: dE/dx can be used for particle ID if plotted vs E or p

## Slide 21: Detection process
Primary interaction of ionizing particle with detector material
Second: charges drift in electric fields towards electrodes and create (very small) induced signals
  drift velocity for electrons in gas at decent drift fields ~ 1 to 6 cm/µs
  drift velocity for ions ~ 1 cm/ms, smaller by four orders of magn.
Drift time can be used for resolution enhancement
  Drift chamber: invented by A. Walenta, J. Heintze, 1970 at Phys. Inst. U. Heidelberg (NIM 92 (1971) 373)
Some charges trapped along drift path
  solid state detectors  impurities, lattice defects, radiation damage
  gaseous detectors  loss by electron attachment on electro-negative atoms  Oxygen, SF6 contamination
High field region may be employed for final gain boost (wire chamber, GEM chamber)

## Slide 22: Need signal amplification: Proportional Wire Counter
Charge gain:
Typical values:
Proportional wire counter:
G~104-106
GEM: G~103-105
Amplification starts at r~5a
 negligible spatial dependence of pulse height
Notes: Overcomes drawbacks of planar detector:
very high voltages required to obtain gas amplification
size of avalanche depends on location of charge creation => loss of proportionality!
high electric field in complete detector => risk of breakdown!

## Slide 23: I-U Characteristics
Recombination during drift
Collection of all created e--ion
pairs: ionization chamber
Avalanche creation:
proportional counter
Distortion of electric field around
anode
 screening of electric field
 loss of proportionality
Propagation of avalanche over full
length of anode (photon emission)
 electric discharge
 saturation of output current
Termination: quench gas or lower U
Continuous breakdown even
without radiation
III
IV
V
VI
Modes of operation of gas detectors
(after F. Sauli 1977, lecture notes )

## Slide 24: PANDA Straw Tracker, one submodule
Straws are of 20µm Coated Polyimide Foil, pressurized to 2bar.

## Slide 25: Charpak´s Multi-Wire Proportional Chamber MWPC
G. Charpak et al. NIM 62 (1968) 202
Nobel prize 1992, Rev. Mod. Phys. 65 (1993) 591

## Slide 26: Anton Oed´s MSGC (Microstructured Gas Chamber)
On resistive glas substrate

## Slide 27: Microstructured Amplification Stages: GEM, InGrid
70 mm
GEM: Gas Electron Multiplier
[F. Sauli, NIM A386, 531 (1997)]
Photolithography: ~ 10.000 holes/cm2
[J. Timmermans, VCI 2007]
amplified charge clouds rain onto readout pixels
Microstructures: Ions travel very short  rate capability

## Slide 28: Choice of Detector gas
Noble gases: Energy dissipation
mainly through ionization
Deexcitation through photon emission
Polyatomic molecules:
Absorption of
photons in
broad energy
range
[O.K. Allkofer, Spark Chambers, Thiemig, München, 1969]
Ar + polyatomic gases
Polyatomic quencher gas essential for stable operation!

## Slide 29: Aging
Let us take a three minute break!

## Slide 30: Electronic Signal Formation
Moving charges induce current in electrodes. Currents proportional to drift velocity.
Simple case: Ionization chamber, no gain

## Slide 31: Varying Signal Formation
I
t
xo
d
xo/vel
(d-xo)/vion
I
t
d
xo/vel
(d-xo)/vion
holes in semicond.
ions in gas

## Slide 32: localized charge injection: one charge carrier only
I
t
I
t
d/vel
a
Anode
Cathode
a
Anode
Cathode
 realized to study mobility and drift velocity
More complicated detector geometries need Ramo´s Theorem

## Slide 33: Mostly focus on fast, electron component
Charge sensitive amplifier integrates signal current to measure the full signal charge
 (electronically low pass filter, integrate onto capacitor)
Ion drift in multi wire proportional chambers creates a long 1/(t + to) tail which leads to signal pile-up. A following shaper amplifier has high-pass filter characteristic that removes slow, ion-drift components
Ion tail nevertheless limits rate capability

## Slide 34
Since charge clusters need to drift to anode for amplification, time delay
proportional to drift distance  Drift chamber

## Slide 35: Modern Experiments Comprise a Detector System
Beam
g
e±
m
p±,p
n
Target
Magnet
Tracking
chamber
Electromagn.
calorimeter
Hadron
calorimeter
Muon
chamber
Different components, measuring different aspects of reaction products:
track, charge, energy, momentum, particle type, ...
The tracking detector is to see everything.....
.....but consist of nothing

## Slide 36: Time Projection Chamber, the Queen of Trackers
100 m3 gas

## Slide 37: HADES- The GSI Dilepton Spectrometer

## Slide 38: CBM Silicon Tracking System STS

## Slide 39: Very Small: Single Crystal- CVD Diamond Detectors
Particle Identification by Time of Flight
exceptional radiation hardness properties
time resolution better 50ps
identify particles by speed
HADES @ GSI

## Slide 40: Radiation hard material (scCVD diamond)
  3.04 x 1011 Au ions / mm2  total absorbed dose: 87 MGy !!!!
suffered amplitude reduction but still good timing < 70ps
Jerzey Pietrasco et al. at GSI for HADES

## Slide 41
Ionization Chambers, Wire Chambers, Solid State Detectors
!The movement of charges in electric fields induces signals on readout electrodes (No discharge, there is no charge flowing from cathode to Anode) !
Central Au+Au collision at 25 AGeV (UrQMD + GEANT4)
160 p 400 - 400 + 44 K+ 13 K-

## Slide 42
Signals induced on grounded electrodes:
S. Ramo, Currents induced by electron motion, Proc. IRE 27 (1939)
W. Shockley, 1938, Currents to Conductors Induced by a Moving Point Charge, Journal of Applied Physics, vol. 9 (1938) 635
Signals induced on electrodes connected by impedance elements:
E. Gatti, G. Padovini and V. Radeka, Signal evaluation in multielectrode radiation detectors by means of a time dependent weighting vector, Nucl. Instr. and Meth. 193 (1982) 651
Signals induced on electrodes embedded in materials with finite conductivity and connected with arbitrary impedance elements:
W. Riegler, Extended theorems for signal induction in particle detectors, Nucl. Instr. and Meth. A 535 (2004) 287.
Signals induced in Detectors by moving Charges

## Slide 43
The Principle of Signal Induction on Metal Electrodes by Moving Charges

## Slide 44
A point charge q at a distance z0 above a grounded metal plate ‘induces’ a surface charge.
Induced Charges
q
z0
+
-
-
-
-
-
-
-
-
-

## Slide 45
Electrostatics, things we know
Poisson Equation:
Gauss Law:
Metal Surface: Electric Field perpendicular to surface.
Charges are only on the surface, no electric field in the conductor.
Surface Charge Density s and electric E field on the surface are related by
E
Perfect Conductor
A
E
E=0
s
A
s

## Slide 46
Induced Charges
In order to find the charge induced on an electrode we therefore have to
Solve the Poisson equation with boundary condition that j = 0 on the conductor surface.
Calculate the electric field E on the surface of the conductor
Integrate e0E over the electrode surface.
q
z0
+
-
-
-
-
-
-
-
-
-

## Slide 47
q
The solution for the field of a point charge in front of a metal plate is equal to the solution of the charge together with a (negative) mirror charge at z=-z0.
Induced Charges
+
z0
-
-
-
-
-
-
-
-
-
=
q
+
-
z0
z0
E
E
The field on the electrode surface (z=0) is therefore

## Slide 48
q
We therefore find a surface charge density of
And therefore a total induced charge of
Induced Charges
z0
+
-
-
-
-
-
-
-
-
-

## Slide 49
q
The total charge induced by a point charge q on an infinitely large grounded metal plate is equal to –q, independent of the distance of the charge from the plate.
The surface charge distribution does however depend on the distance z0 of the charge q.
Induced Charges
z0
+
-
-
-
-
-
-
-
-
-
-q

## Slide 50
q
q
Moving the point charge closer to the metal plate, the surface charge distribution becomes more peaked, the total induced charge is however always equal to –q.
-q
-q
I=0
Induced Charges

## Slide 51
q
If we segment the grounded metal plate and if we ground the individual strips, the surface charge density doesn’t change with respect to the continuous metal plate.
-q
-q
V
I1(t) I2(t) I3(t) I4(t)
The charge induced on the individual strips does now depend upon the position z0 of the charge.
If the charge is moving there are currents flowing between the strips and ground.
 The movement of the charge induces a current.
Signal Induction by Moving Charges

## Slide 52
a little more general, more practical
In a real particle detector, the electrodes (wires, cathode strips, silicon strips, plate electrodes …) are not grounded but they are connected to readout electronics and interconnected by other discrete elements and kept at different potentials.
We want to answer the question:
What are the voltages induced on metal electrodes by a charge q moving along a trajectory x(t), in case these metal electrodes are connected by arbitrary linear impedance components ?

## Slide 53
solution in two steps
We first calculate the currents induced on grounded electrodes.
We then insert the currents as ideal current sources,
shrink the electrodes to nodes and add all the inter-node impedances.
=
+
The second step is typically performed by using an analog circuit simulation program. We will focus on the induced currents.

## Slide 54
Signal Polarity Definition
I(t)
The definition of I = -dQ/dt states that the positive current is pointing away from the electrode.
The signal is positive if:
Positive charge is moving from electrode to ground or
Negative charge is moving from ground to the electrode
The signal is negative if:
Negative charge is moving from electrode to ground or
Positive charge is moving from ground to the electrode
+q
-
-
-
-
-
-q
+
+
+
+
+
I(t)
+q
-
-
-
-
-
-q
+
+
+
+
+
Positive Signal
Negative Signal

## Slide 55
Signal Polarity Definition
By this we can guess the signal polarities:
In a wire chamber, the electrons are moving towards the wire, which means that they attract positive charges that are moving from ground to the electrode. The signal of a wire that collects electrons is therefore negative.
I(t)
+q
-
-
-
-
-
-q
+
+
+
+
+
I(t)
+q
-
-
-
-
-
-q
+
+
+
+
+
Positive Signal
Negative Signal

## Slide 56
The current induced on a grounded electrode n by a moving point charge q is given by
Where the weighting field En is defined by removing the point charge, setting the electrode in question to potential Vw and keeping the other electrodes grounded.
Removing the charge means that we just have to solve the Laplace equation and not the Poisson equation !
Induced Current, Ramo Shockley Theorem
the general, arbitrary electrode case
0

## Slide 57
Parallel Plate Chamber
q
D
z0
Plate 1
Plate 2
q2
q1
I2(t)
I1(t)
Weighting field E1 of plate 1: Remove charge, set plate1 to Vw and keep plate2 grounded
Weighting field E2 of plate 2: Remove charge, set plate2 to Vw and keep plate1 grounded
So we have the induced currents
v

## Slide 58
What are the signals induced by a moving charge on electrodes that are connected with arbitrary linear impedance elements ?
1) Calculate the particle trajectory in the ‘real’ electric field.
2) Remove all the impedance elements, connect the electrodes to ground and calculate the currents induced by the moving charge on the grounded electrodes.
The current induced on a grounded electrode by a charge q moving along a trajectory x(t) is calculated the following way (Ramo Theorem):
Weighting Field En:
Remove q from the setup, set the electrode to voltage V0 while keeping all other electrodes grounded. This results in an electric field En(x), the Weighting Field
3) These currents are then placed as ideal current sources on a circuit where the electrodes are ‘shrunk’ to simple nodes and the mutual electrode capacitances are added between the nodes. These capacitances are calculated from the weighting fields by
Signal Calclulation in 3 Steps

## Slide 59
Careful design of multi-electrode, highly segmented Germanium Crystal Detectors
and full understanding of the signals along Ramo, Shockley and the Weighting field
were the basis for AGATA Gamma Tracking  Lecture by Andreas Heinz

## Slide 60
The following relations hold for the induced currents:
1) The charge induced on an electrode through a charge moving from a point x0 to a point x1 is
and is independent of the actual path.
2) Once ALL charges have arrived at the electrodes, the total induced charge in the electrodes is equal to the charge that has ARRIVED at the particular electrode.
3) If there is one electrode enclosing all the others, the sum of all induced currents is zero at any time.
General Signal Theorems
take a 3 min break

## Slide 61
Wire Chamber Signals
People sometimes picture detector signals as ‘the charge entering the electrode and flowing through the amplifier’.
This is very misleading and gives incorrect results – once the moving charges have arrived at the electrodes the signal is over.
The shape of the signal is determined by the movements of the charges in between the electrodes.
b
b
a
Wire
Werner Riegler, CERN

## Slide 62: Consequences on wire chamber readout
Primary charges become visible through avalanche amplification at the anode wire
negative signals at anode
induced positive signals at cathodes
 localized avalanche

## Slide 63: Cathode Pad Response Function Po(l) in MWPC
Electrons in avalanche do not travel far
 surface charge distribution does not change for the fast, electron induced signals
Signal factorizes into Icathode(t) x Pad Response Function
I1(t) I2(t) I3(t) I4(t)
q
z0
-q

## Slide 64: Further Example: Double Sided Silicon Strip Detector
p-side
n-side
CBM-STS
silicon strip detector
58µm pitch, 300µm thick
7.5° stereo angle

## Slide 65: Further Example: Double Sided Silicon Strip Detector
Weighting Potential
strip positions

## Slide 66: Weighting Potential gives Total Charge Detected

## Slide 67
Conclusion on Signals
The principle of signal generation is identical for Solid State Detectors, Gaseous Detectors and Liquid Detectors.
The signals are due to charges (currents) induced on metal electrodes by moving charges.
The easiest way to calculate signals induced by moving charges on metal electrodes is the use of Weighting fields (Ramo – Shockley theorem) for calculation of currents induced on grounded electrodes.
These currents can then be placed as ideal current sources on an equivalent circuit diagram representing the detector.
An extended version of the theorem applies to detectors containing any resistive materials.

## Slide 68: Conclusion on Ramo Shockley Theorem
With the Ramo Shockley prescription we can fully understand signal formation
... even in an arbitrary detector volume with arbitrarily shaped electrodes
Cannot be inverted i.e. from knowledge of all signals in all electrodes, the charge distribution cannot necessarily be reconstructed, but a hypothesis may be tested
Prerequisit is the measurement of the actual signal shapes

## Slide 69: Fluctuations in Energy Loss
Bethe-Bloch formula  mean energy loss,
i.e. statistical average over many collisions
Important quantity to understand the response of a detector:
probability distribution of energy loss D in material of thickness x,
determined by
cross section ds/dT
nex
Calculation of energy loss distribution: two approaches
Convolution method
Laplace transform method
[Allison, Cobb, Ann. Rev. Nucl. Part. Sc., 253 (1980)]

## Slide 70: Landau Distribution
Properties of f(l):
asymmetric: tail up to Tmax
Maximum at l= - 0.223
FWHM = 4.02
numerical evaluation
Universal Landau distribution:
Landau distribution in ROOT:
x is the scaling factor for the energy loss

## Slide 71
Analytical approximation: Moyal distribution [Moyal 1955]:
Moyal:
Fit to Landau
coarse shape correct
tail too low!
The Moyal tends to zero exponentially while the (correct, physical) Landau distribution decays as 1/E2.
Since the long tail of the Landau distribution has significant impact on detector resolution it is a very bad idea to use it – it is simply incorrect and gives wrong predictions ….
People worry a lot about the details of the energy deposit spectrum around the most probable value, but forget the long tail by cutting at low values – which will give very wrong predictions.

## Slide 72
[H. Bichsel, Rev. Mod. Phys. 60, 663 (1988)]
Landau Distribution does not follow Central Limit Theorem
The tail does not vanish with increasing detector depth!
Mean and Variance of Landau distribution are infinite even though it is normalized!

## Slide 73: Small signal extend, read-out by single electrode: Position Resolution
Resolution = Sqrt(Variance signal distribution)
Gausian of width s has the same variance
readout
scan
x
signal
w
xm
Statistics of the cylinder hat distribution...
same as digitization error

## Slide 74: Enhancement of Resolution
spatial extension of induced cathode signals allow for high precision  the center of pad response function can be determined
typical gaseous detector resolution ~ 150µm << pad size (~cm)
Similarly: lateral diffusion enhances resolution on TPC with finite granularity
 Detector granularity does not limit resolution as long as cluster sizes are larger than pad size.

## Slide 75: Detector Simulation Tools available from CERN
Garfield (Rob Veenhof)
  electric fields, particle drift, induced signals, electronics ….
Magboltz (Steve Biagi)
  transport properties of gas mixtures, driftvelocity, diffusion
Heed (Igor Smirnov)
  charge deposit of fast particles in gas mixtures with PAI model
Very reliable simulation of all the chamber and signal processes

## Slide 76
Short introduction to CBM tracking

## Slide 77
 10 million Au+Au reactions/sec
 determination of (displaced) vertices (σ  50 m)
 identification of leptons and hadrons
 fast and radiation hard detectors
 free-streaming readout electronics
high speed data acquisition and high performance
computer farm for online event selection
 4-D event reconstruction
Central Au+Au collision at 25 AGeV (UrQMD + GEANT4):
160 p 400 - 400 + 44 K+ 13 K-
CBM technological challenges

## Slide 78: ASICs - Pre-Amplifier Microchips made for FAIR
Testpulse Release
Slow Shaper: Energy
Fast Shaper: Timestamp
Discriminator Output
FAIR-CBM
STS-XYTER 2013
AGH Krakow, Poland
n-XYTER 2006 built for neutrons
analogue signal sequence
128 amplifiers and signal
digitizers on
one chip
Self triggered, free streaming data generated with detector front-end chips

## Slide 79: Game industry supplies computing power for physics!
...Computer graphics relies on ray-tracing
particle tracking is not
much different!
For the experiments:
At 1000 Gbyte/s, there is
no time to store the data!
At FAIR, on-line event reconstruction will be realized by means of many thousands of Graphics-Chips operating in parallel!

## Slide 80: Work at the GSI Detectorlab