## Slide 1: The Silicon Tracking System of CBM
Project
System Integration
Read-out Electronics, Data Acquisition Chain
Low-mass module components
The Silicon Tracking System
pile-up free track point determination in high-rate collision environment: 105  107/s (A+A), up to 109/s (p+A)
8 tracking stations
double-sided silicon microstrip sensors
self-triggering front-end electronics
time-stamp resolution  5 ns
material budget:  0.3% – 1% X0 per station
momentum resolution: p/p  1.8% (p > 1 GeV/c, 1 Tm field)
Longitudinal cut – Silicon Tracking System in Dipole Magnet
2013 – Technical Design Report*
2017-2018 – Production Readiness (Sensors, Electronics, System Integration)
Detector construction until 2021 *GSI Report 2013-4 (Aug. 2013)
Timeline:
GSI-FAIR, Darmstadt, Germany;
JINR, Dubna, Russia;
Univ. Tübingen, Germany;
KIT, Karlsruhe, Germany;
AGH, Cracow, Poland;
JU, Cracow, Poland;
WUT, Warsaw, Poland.
Key Project Institutes:
Activities at GSI:
Current development activities
front-end boards
8 stations
C-frame
ultra-thin r/o cables
sensor
read-out + power boards
Module assembly: TAB-bonding of Al-polyimide cables between ASICs and sensor
Radiation hardness of sensors
Quarter-unit demonstrator
ladder mounting
mechanical stability
electronics cooling
cable routing
powering
connectivity
Neutron-irradiated sensors tested in the laboratory and with proton beam. Sensors retain >70% charge collection efficiency after 2x lifetime fluence.
Component QA: sensors, microcables, readout electronics
Detector module assembly QA
Ladder assembly and QA
Mechanical integration
Full CBM06
sensor family
half-unit
ladder
Ultra-thin readout cables: 0.228 X0 per cable stack (equivalent to 213 µm Si)
Carbon fiber support structures
Self-triggering front-
end electronics
FPGA based hardware for free streaming data acquisition chain
High performance
compute nodes
Custom STS-XYTER ASIC
Data processing board
Assembly centers:
GSI-FAIR
JINR –VBLHEP
KIT
18 half-units
106 ladders
896 modules
Notes: 1