## Slide 1: CBM-MUCH-RPC Electronics
J. Saini, VECC Kolkata

## Slide 2: Readout Chain for the RPC detector
RPC Detector
PADI Electronics
GET4 ASIC
FEE Board
ROB-3 (GBTx Board)
Beam Hall
Green Cube
CRI Board
PC/Computing
Node

## Slide 3: CSA (MUCH-XYTER) option as compared to Current sensitive PADI
Charge output of RPC ~ 1PC and above
CSA available in ASIC with CBM DAQ chain is STS/MUCH-XYTER
Dynamic range of MUCH-XYTER ~60FC
Attenuation required more then 50 times and general capacitive attenuator will introduce large noise as capacitor to ground will be 50 times large.
Active attenuation required where PADI itself can act as the attenuator.

## Slide 4: COSY Test Beam preparation with PADI
PADI doesn't have pulse stretcher at the digital output stage hence LVDS to other logic conversion circuits were not responding to low level signals from RPC.
As timing ASIC GET4 was unavailable for the Beam time, we decided to make PADI specific discriminator to convert output LVDS to NIM pulse.

## Slide 5: Present Lab setup of RPC-PADI
RPC Detector
PADI Electronics
Discriminator with NIM signal out
Coincidence
4 Fold
Sint1
Sint2
Sint3
Scaler
Coincidence
3 Fold

## Slide 6: Picture of the setup
RPC Detector
PADI-Electronics
Scaler and other
Conventional Electronics
Discriminator
Scintillators
Used THS4520 from NINO
FEE board for spark protection

## Slide 7: Results from the setup
We could get efficiency of ~ 94% at 10600 V from RPC-PADI combination.
These logic pulses can be inserted to STS-XYTER with some attenuation and series capacitance
Test beam setup is prepared without using GET4 and can be used for any other TEST-Beam using discriminator and STS/MUCH-XYTER chain.
With this results, we can say that PADI can be easy used along with RPC’s

## Slide 8: Number of pad calculation
At 300cms of station-3, at 5.7 degree the radius of innermost pat is 29.35cms
Pad size per degree is 5.22mm
 | 1 degree | 2 degree | 5 degree
Size of first pad | 5.2mm | 10.4mm | 26.1mm
No of pads per plane | ~28,080 | Not calculated | ~1,500

## Slide 9: Total number of channels for 1 degree and price estimate for RPC electronics
With 5 degree pads, total approx
  Channels per layer = 28000
  Channels per station = 84000
  Channels in two stations = 1,68,000
Cost estimate
  Cost per channel (with CRI) = 12Euro
  Total cost =20,21,000Euro
  Too much for pad….even PCB not possible

## Slide 10: Total number of channels for 5 degree and price estimate for RPC electronics
With 5 degree pads, total approx
  Channels per layer = 1500
  Channels per station = 4500
  Channels in two stations = 9000
Cost estimate
  Cost per channel (with CRI) = 12Euro
  Total cost =1,08,000Euro
  PCB possible in 2-layer….Cost reasonable may be

## Slide 11: Conclusion
PADI can be used along with RPC detector for station 3 & 4
STS/MUCH-XYTER based chain can also be used provided some active attenuator along with pulse stretcher is introduce in between

## Slide 12: Thanks for attention…!!!