## Slide 1: CBM Electronics
Christian J. Schmidt CBM-India Meeting
Feb. 15-17, 2018, Falta, India

## Slide 2
 determination of (displaced) vertices (σ  50 m)
 identification of leptons and hadrons
 fast and radiation hard detectors
 free-streaming readout electronics
high speed data acquisition and high performance
computer farm for online event selection
 4-D event reconstruction
CBM technological challenges
fixed target configuration makes 10MHz Au+Au interaction rate feasible at FAIR
Notes: 2
2
2

## Slide 3: CBM-Silicon Tracking System
~ 4 sqm active sensor area
double sided strips 7.5°, 58µm pitch
8 Stations,
106 ultra-light carbon ladders
896 Sensor modules
STS
2.5°
25°
beam
target
Low-mass micro cables from sensor to FEE
1.8 Mio channels, cooling power ~ 40 kW
selftriggering ASIC readout
x/X0 [%]
material budget per station

## Slide 4
Assembly of double sided strip detector modules, a collaborative effort
prototyping ongoing
Topical workshop on radiation induced surface effects in silicon detectors, Oct. 2016 at KIT

## Slide 5: Silicon microstrip sensors
300 µm thick, n-type silicon
double-sided segmentation
2nd metal routing lines
1024 strips of 58 µm pitch
strip length 2/4/6/12 cm
angle front/back: 7.5/0 deg
read-out from top edge
rad. tol. up to 1014 neq/cm2
C.J. Schmidt, CBM-India Meeting 2018, Falta, India

## Slide 6
the Silicon-Sensor-Module
STS-module-components:
double-sided silicon
microstrip sensor
signal transmission cable
front-end-boards

## Slide 7
Module Electronics Allocated on Cooling Shelves
Front-end Electronics Boards
Read-out Boards, Power Boards
Cooling plate
bi-phase CO2 cooling system
STS electronics total: 42 kW

## Slide 8: Read-out cables 32000 analogue cables of 64ch needed
cable stack: thickness 0.230 % X0
spacer layer
signal layer: 64 Al lines of 116 µm pitch, 10 µm thick on 14 µm polyimide, lengths up to 55 cm
64 traces per cable
challenge: production yield of upto 50cm long cables  low yield = uncalculable project duration
Important: cable capacitance < 500fF per cm
C.J. Schmidt, CBM-India Meeting 2018, Falta, India

## Slide 9: Micro Cable Technology with TAP-Bonding
double cable layer bonded onto chip

## Slide 10
assembly-step 2: TAB-bonding of chip cables to the silicon sensor
fixing of the microcables with vacuum and alignment
TAB-bonding of 16 microcables to the sensor (two rows at 8 microcables)
protection of the TAB-bonds with Globtop after QA-measurements

## Slide 11
Die- and wirebonding of readout chips to the PCB-rows
wire-bonded STS-XYTER-ASIC
die-bonding of four ASIC´s for the 2nd row
wire-bonding of the STS-YTER-ASIC´s
application of Globtop
after QA-measurements

## Slide 12
optimization of alignment jigs

## Slide 13
version 2: Copper-based microcables/
KIT-IPE (Dr. Thomas Blank & team)
Signal Transmission Cable, Version 2
Benefits of Copper:
well known in PCB-Flexboard technology
offers interconnected multilayer solutions
one cable with two layers (bottom & top) and vias instead of two single Al-cables
As an alternative to the Aluminum-microcables a R&D-project has been
started that investigates Copper-based cables.

## Slide 14
interconnection technology for version 2: Au-stud bumps + flip-chip
Au-Stud bumps on STSXter-Testchip
reliable and fast process
Ball-Wedge-Bonder
Interconnect of alternative signal cable

## Slide 15
Module-Components: Front-End-Boards
STS-XYTER-ASIC
with 128 channels and pitch of 116 µm
(same as the sensor bond pad pitch)
8-STS-XYTER-board
(dummy-PCB with power and signal connectors)
MUCH will employ a similar FEB with 2 STS-XYTER Chips

## Slide 16: STS-Module Front-End Board
very dense (101 x 31mm2)
cooling challenges (~ 10W)
floating at biasing potential
upto 40 x 320Mbps data transfer
in-board chip LDOs
point of load skimming regulation
powered by CERN Feast-based DC/DC converters

## Slide 17
QA-measurement tools: Pogo-Pin Sockets
testsocket for the ASIC-TAB-bonds
testsocket for the sensor-TAB-bonds
Pogo-pin

## Slide 18: Dicing precision successful: 100µm Pogo-Pins match!

## Slide 19: CBM-related Chip Developments and Options
CBM MuCH XYTER
E. Atkin et al, MEPhI
CBM STS-XYTER/MuCH-XYTER
AGH Krakow, R. Szczygiel et al
SPADIC for TRD
ZiTi Heidelberg, P. Fischer et al
SPADIC 2.0 with e-link interface
PADI for Diamond
M. Ciobanu, ISS
PADI for TOF
M. Ciobanu, ISS
Bucharest
GET-4 TDC (TOF)
H. Flemming, H. Deppe, GSI
CBM-GBTx
Chipset ordered from CERN
GBTx
FPGA emulation for
VECC and JINR
Rad tolerant LDOs
SCL Chandigarh, India

## Slide 20: Fully digital Read-out ASIC “STS-XYTER”
STS-XYTER ASIC
purely data driven read-out
time-stamped data elements
250kHz per channel
channels | 128, polarity +/-
noise | < 1000 e- under load
ADC range | 16 fC, 5 bit
clock | 160 MHz
power | < 10 mW/channel
timestamp | < 5 ns resolution
out interface | 5 × 320 Mbit/s LVDS
for every channel:
fast branch: time-stamp
slow branch: signal height digitization (energy)
noise minimization in self-triggering system:
effective two-level discrimination
trigger to the timestamp latch vetoed if ADC-LSB generated no signal
CBM-NET
(v1.0 )
GBT (V2.0)
LSB veto
ts = 30 ns
ts = 80 ns
r/o logic
Design Team:
R. Szczygiel et al. at AGH Krakow/Poland
UMC 180 nm CMOS

## Slide 21: Analog Front End - overview
Switchable
(90ns – 280ns)
in 4 steps
Switchable gain
(5x smaller for MUCH)
+ trimming 2 bit

## Slide 22: STS-XYTER R. Szczygiel et al. AGH Krakow
Submission Review in Feb. 2015: Noise is an issue 
system issue, optimization with complete system perspective, extensive architectural studies  goal < 1000 ENC
Submission Review in Oct. 2015  full go for submission
STS-XYTER 2.0: adaptation to GBTx-eLink-readout, STS-r/o protocol
   all architectural elements included!
in 2018: STS-XYTER 2.1: fix of minor bugs prior to large scale production
STS-XYTER turns into MuCH-XYTER via Gain Switch

## Slide 23: STS-XYTER 2.0 Submission Mai 2016
STS-XYTER 2.0  yield 930 chips for STS- and MUCH-prototyping
TOF readout ASICs, Volume production for operation at STAR
  Get4-TDC in two versions:
    Bug-fix version
    Version for robust operation at 40MHz
  PADI – fast 8-channel TOF pre-amp
SPADIC V2  prototype run with CBM compatible e-link interface
...evolved to a grand CBM-Joined 6-Chip Submission

## Slide 24: Unpacking was solemn like X-mas

## Slide 25: The Readout-ASIC STS-XYTER
Switchable
(90ns – 280ns)
in 4 steps
Switchable gain
(5x smaller for MUCH)
+ trimming 2 bit
The moment of truth: Testing, a joined AGH, WUT, VECC and GSI effort  workshop on STS-XYTER testing Feb. 2017 in India
All results cumulate now in a final prototyping iteration: STS/MUCH-XYTER 2.1 submission 2018

## Slide 27: SCL realizes radiation tolerant LDOs for CBM
Sensitivity to Total Ionizing Dose evaluated by VECC Kolkata  OK for CBM
Sensitivity to Single Event Upset evaluated by GSI at COSY, FZJ  OK for CBM
Semi–Conductor Laboratory
Department of Space, Government of India
180nm Tower Jazz Process
STS-XYTER single ended cascode
very sensitive to supply noise

## Slide 28: CBM-TRD: Spadic 2.0 in two versions being tested
32-channel signal digitizer 8bit at 16 MHz
self triggered
forced next neighbor trigger
e-link interface
Readout chip for CBM Transition Radiation Detector (allows to tell electrons from pions)

## Slide 29: PADI, the one proven design, is available in large numbers now
Designer: Mircea Ciobanu

## Slide 30: GET4 TDC s~20ps
Designer: H. Flemming, H. Deppe GSI/EE

## Slide 31: Summary
Big technological challenges tackled with CBM detectors and their signal rates
The STS- and MUCH-XYTER ASIC is a dedicated readout chip for the silicon tracker and the MUCH detector system alike
Careful full system design needed and done for adequate and dedicated customization of readout electronics
Outlook: We will be diving into our production phase