Next focusing lens
for the Barrel DIRC
Carsten Schwarz, GSI

---
Measured pattern
view from back
Observed Cherenkov rings
are folded
p, 3 GeV/c

---
Don't forget the lens...
hit pattern for 3-layer lens
7 GeV/c, 50 degree
no lens

---
Radiation hardness
DPM background generator

---
Optical software: Spherical lens
Geant
Zemax
Dispersing +
focusing lens
for flat focal plane

---
Lens design aimed for a focal plane
matching the flat photon detector plane
Radiation level ~ 400 Rad
(CUA 1% / 100Rad @420nm x-ray)
PbF2 is radiation hard,  ~ 100 kR
Other optical radiation resistant glasses?
Important for EIC
SiO2
LaK33

---
Barrel DIRC baseline design: three radiators per prism

---
GEANT
Roman Dzhygadlo
Green: one solid piece of SiO2 ?

---
Companies need drawings in accordance with ISO 10110

---
Summary
Several iteration of lenses
Simple lens with air gap → too much photon loss
Lens group: One bended surface → bended focal plane
Lens group: Two bended surfaces → flat focal plane
Lens group system: Lens combination (new, awaiting offer)
→ close to final version