## Slide 1
ICASiPM 2018 - Schwetzingen
Techniques for Characterizing Light Source Emission Statistics at Single-Photon Level
Paolo TRAINA
(In collaboration with Ivo P. Degiovanni)

## Slide 2
ICASiPM 2018 - Schwetzingen
OUTLINE
Intro: g(2)(t) function
The Grangier parameter α
Generalization to n-th order
Working conditions
Applications
Conclusions

## Slide 3
Single photon sources (SPS)
Deterministic and on-demand: 100% photon emission probability at any time decided by the user (emission rate arbitrarily high);
Subsequent photons completely indistinguishable;
Two-photon emission probability: 0%.
Ideal SPS:
Real single photon emitters
NV
FWM
SPDC
Heralded sources
Notes: SPS necessaria per estendere la catena di riferibilità delle grandezze radiometriche (misura di p ottica per principio di sost elettrica con rad crio)
al regime di fotoconteggio tipico delle qtech. caratteristiche. Equivqale a stato di Fock, non classico e non presente in natura.

## Slide 4
The second order intensity correlation function (or Glauber function) is defined as:
No classical description
Classical description is possible…
SPS!
(Antibunching)
Single mode laser
(coherent, Poissonian)
Chaotic source
(bunching, thermal)
“g(2)”: Introduction

## Slide 5
“g(2)” vs “α” parameter
Assuming low photon flux, g(2)(0) is equivalent to Grangier’s “α” parameter*:
CC
DA
DB
The value of α is independent of:
the total efficiencies (ηA, ηB) of individual channels
Splitting ratio of the BS
Hanbury-Brown & Twiss
(HBT)
ICASiPM 2018 - Schwetzingen
*P. Grangier, G. Roger, and A. Aspect, Europhys. Lett. 11, 173-179 (1986).

## Slide 6
On/Off Detectors:
“Geiger mode”
(Intermission)
Breakdown Voltage
Reverse Bias
Forward Bias

## Slide 7: On/Off vs SiPM
PNR
Single-photon sensitivity
Cross-talk
ICASiPM 2018 - Schwetzingen

## Slide 8
( = quantum efficiency)
BS
BS
BS
With four detectors in tree configuration, it is possible to measure up to the 4th-order Glauber’s self-correlation function:
Detector tree configuration
Manifold g-function...How to?
Post-selection system:
Time-tagging instrumentation;
Post-selection software.
4 On/Off detectors
3 pigtailed 50%:50% beam splitters
ICASiPM 2018 - Schwetzingen

## Slide 9: g(n) as a resource
Proving non-classical emission (SPS)
Characterizing optical fields
Applications in Sensing (superresolution)

## Slide 10: Working conditions(I)
ICASiPM 2018 - Schwetzingen
Pclick<0.1
1 thermal field
2 thermal fields
1 thermal +
1 Poissonian
Log10[thermal]
Log10[thermal]
Log10[thermal]
g(2)(0)
g(2)(0)
g(2)(0)
For high photon flux, g(2)(0) collapses to «1» anyway!

## Slide 11: Working conditions(II)
ICASiPM 2018 - Schwetzingen
…but SNR must be high!
1 thermal +
1 Poissonian
1 «fixed»Thermal field
+ dark counts
x=Log10[DCR]
g(2)(0)
Pclick<0.1
For low SNR, the statistics is governed by DCR (Poissonian)

## Slide 12: HBT vs SiPM
ICASiPM 2018 - Schwetzingen
The architecture of SiPM in principle allows direct g(n) measurement but…
…it requires pre-characterization of the device (efficiency, cross-talk, etc)
It is advisable to use SiPM like «overpowered» On/Off Detectors!

## Slide 13: Applications!
ICASiPM 2018 - Schwetzingen

## Slide 14
Emitter: single NV center in diamond, pulsed excitation
International comparison: g(2)(0) Measurement in the VISIBLE
(EMPIR 14IND05 MIQC2)
To provide a snapshot of the measurement capabilities of European National Metrology Institutes (NMI) in the area of photon counting detection, a joint measurement of g(2)(0) among three NMIs been hosted at INRIM
INRIM, Torino, October 16th - 29th 2017
Goal: To allow the participants and the scientific community to better understand the technical challenges and resources required to move from research projects to more standard measurement service
The Setup
Participants: INRIM (Host), NPL, PTB

## Slide 15
Emitter: single NV center in diamond, pulsed excitation
International comparison: g(2)(0) Measurement in the VISIBLE
(EMPIR 14IND05 MIQC2)
To provide a snapshot of the measurement capabilities of European National Metrology Institutes (NMI) in the area of photon counting detection, a joint measurement of g(2)(0) among three NMIs been hosted at INRIM
INRIM, Torino, October 16th - 29th 2017
Goal: To allow the participants and the scientific community to better understand the technical challenges and resources required to move from research projects to more standard measurement service
The Setup
Participants: INRIM (Host), NPL, PTB
(In preparation)

## Slide 16: Joint measurement of the of a “noiseless” heralded SPS @1550 nm
The Optical Switch works as an electro-optical shutter, open for a short time (topen) only when a heralded photon arrives, to suppress the “noise” photons: no need for post-selection!
topen
The Control Electronics waits a custom (greater than the measuring device dead time) before accepting a second heralding: no dead-time effects affecting the measurements!
Noiseless Heralded SPS: APL 101 221112 (2012)
(In preparation)

## Slide 17
We experimentally demonstrated [1]for the first time a recently proposed criterion [2] which is capable of detecting nonclassical behavior in the fluorescence emission of ensembles of single-photon emitters.
vs
Item 1
Item 2
-6 runs of 200 s
-excitation rate: 5 MHz.
-Red dot: stabilty test.
More robust to poissonian noise!
1- poissonian noise off,
2- 10000 counts/s due to noise,
3- 25000 counts/s due to noise.
bins
[1] E. Moreva et al., Phys. Rev. B 96, 195209 (2017)
[2] L. Lachman et al., Scientific Reports 6, 19760 (2016).

## Slide 18
Even states 1, 2, and 4 (outside the shaded area) show a non-classical component!
nome, date e luogo della conferenza
Dotted blu lines: constant g(4)(0).
Dashed purple lines: constant g(3)(0).
Solid cyan lines: constant g(2)(0).
Light blue shaded area: nominally non-classical states (g(2)(0) < 1) region.
Multi-mode states combination of poissonian, thermal and single-photon modes:
Mode reconstruction via multiphoton statistics
In collab. with:
BS
BS
BS
Phys. Rev. A 88, 013822 (2013)
ICASiPM 2018 - Schwetzingen

## Slide 19
Thank you for your attention!
Take-away
g(2)(t) function (and g(n)) is a fundamental tool (not only!) for characterizing optical fields
It can be directly sampled by non-PNR detectors (HBT, Grangier’s α)
Trade-off between low flux and SNR
Direct measurement exploiting PNR features of SiPM requires pre-characterization of the detector. Use SiPM like On/Off detectors!
Premiale Q-secGroundSpace
Funding:
ICASiPM 2018 - Schwetzingen

## Slide 20: BACKUP

## Slide 21
The source: NV center in ND
Final Meeting: May 2018 - INRIM
High photostability
Ambient temperature
Nanoscale magnetic sensor

## Slide 22
Model (II)
Final Meeting: May 2018 - INRIM
Including the effects of the background coincidences:
where:
We have developed a model accounting for the dead-time of the detectors effect and we observed that no significant events are lost.
Backflash peaks

## Slide 23
INRiM:
-fused 50:50 Beamsplitter;
-2 Excelitas SPCM-AQR SPADs;
-ID Quantuque “ID800” TDC.
Experimental set-up
Final Meeting: May 2018 - INRIM
NPL:
-fused 50:50 Beamsplitter;
-2 Excelitas SPCM-AQR SPADs;
PicoQuant “HydraHarp 400” TSPC module.
PTB:
-fused 50:50 Beamsplitter;
-2Excelitas SPCM-AQR SPADs;
-PicoQuant “HydraHarp 300” TSPC module.
Each measurement: 10 runs of 500 seconds Coincidence window: 16 ns
Coupling efficiency of system: ηTOT =1.76 ± 0.01%

## Slide 24
1550 nm HSPS joint measurement setup
Final Meeting: May 2018 - INRIM
10x1x10 mm
PPLN
810 nm
CW laser pump
532 nm
IF
Dichroic
mirror
1550 nm
FC
IF
FC
SMF
SMF
l/4
l/2
l/4
O
S
CH B
CH A
FBS
FPGA
Guest
HBT
INRiM
HBT
SPCM-AQR
Fast
Pulse
Generator
Coinc
FBS
MPD
InGaAs
MPD
InGaAs
Coinc
FBS
MPD
InGaAs
MPD
InGaAs
Coinc
FBS
InGaAs
SPAD
InGaAs
SPAD

## Slide 25
Experimental Results(I)
The algorithm is tuned in order to recover the mode structure of a field with just pseudo-thermal modes;
The fidelity of all the reconstructions shown is above 99%.
2 thermal + 1 «fake» poissonian mode
Pure thermal modes
Thermal + Poissonian modes

## Slide 26
EXL02 – SIQUTE Interim Meeting 13 – 14 November, CEA, Grenoble
Towards D1.1.4 - Higher order g-function as a tool for the investigation of ...
Experimental Results(II)
Reconstructed mode structure of the single photon state generated by our NHSPS (g(2)(0) < 0.05)
The mode structure of this state presents non-classical components, even if the state is nominally classical!
Occupation modes of a single photon state heavily polluted by a thermal field