Shape Measurements of Radiators
C.Schwarz, GSI
dy = +-0.5mm
--> dq = +- 30 mrad
all parts rest on three points
8420 mm

---
Principle
spots
yields information
about 900+di
second spot
yields information
about parallelism
check

---
Lithotec “L6”
B
F
Taking “front” spots (F) with respect
of their center of gravity ensures
sum %theta_i = 360^o newline sum 90^o+%delta_i = 360^o newline sum %delta_i = 0

---
Lithotec “L6”	“L1”
dq1 = 1.61	0.87 mrad
dq2 = -1.35	-0.36
dq3 = -3.07	0.66
dq4 = 2.81	-1.18
+- 0.03	+-0.05
Miass “R1”	“R2”
dq1 = 5.54	1.23
dq2 = -5.33	-1.12
dq3 = 5.54	1.12
dq4 = -5.75	-1.23
+- 0.03	+-0.05
Boeing “J1”
dq1 = -0.28
dq2 = 0.03
dq3 = -0.08
dq4 = 0.33
+- 0.05
q2
q3
q1
q1
q4
angles 100 times exaggerated
BaBar requirement:
<0.25mrad
in principle the full bar can be scanned....

---
Summary
Simple setup allows squareness measurements with angular resolution 25mrad (L=10m)
Radiator bars of three companies were measured
  - Squareness requirements need to be defined
Front side - back side reflections allow to measure parallelism of disks