## Slide 1: Stability and Availability Study Base on the 10-25 MeV Superconducting Proton Linac (CAFe)
Yuan He, Guirong Huang, Zheng Gao, Tiancai Jiang, Weiming Yue, Shenghu Zhang, Xingmeng Liu, Zhongzu Zhou, Weilong Chen, Jiangqiang Wu, Zhijun Wang, Liepeng Sun, Longbo Shi, Chenxing Li, etc.
On behalf of Linear Accelerator Center
Institute of Modern Physics, Chinese Academy of Sciences
Supported by “Strategic Priority Research Program” of the Chinese Academy of Sciences.
APEC2018, Dec. 10-12, 2018, Frankfurt

## Slide 2: Outlines
Introduction of Chinese ADS Project and CAFe
Operation Status of CAFe
Stability Issues
Conclusion

## Slide 3: Issues of Sustainable NP and Solution
Management and safe disposal of nuclear waste
  1GWe PWR ~25 ton/year;
  ~2200 ton/year in 2030 in China; ~10000 ton/year now in the world
  Total capacity of Yucca Mountain ~ 70000 ton;
“The ADS has the advantage that it can burn pure minor actinides while avoiding a deterioration of the core safety characteristics.”
⎯ ADS and FR in Advanced Nuclear Fuel Cycles – A Comparative Study, NEA/OECD, 2002
  China status: ~3% now, ~7% by 2020, ~10% by 2030, the total NP capacity will be the first position

## Slide 4: ADS/ADANES Roadmap in China
Inject I
Inject II
2014
~2.5 MeV
&10mA
2016
~25 MeV
&~10mA
<2030
~1.0 GeV
&<15mA
~203x
~1.0 GeV
&>15mA
10 MWt
>500 MWt
≥1 GWt
10 MeV
￥1.78 B
Phase I
2011--2016
Phase II
2017--2024
Key Tech. R&D : Acc., Target, Blanket… Prototypes
Initial Facility
Demo. Facility
Phase III
Phase IV
Indust. Facility
2024
~500 MeV
&~10mA
“strategic Priority Research Program” of the Chinese Academy of Sciences
CiADS

## Slide 5: CIADS Project (2018-2024)
Approved in Dec. 2015
Leading institute: IMP
Budget: >1.8B CNY (Gov. and Corp.)
Location: Huizhou, Guangdong Prov.
Contribution Partners: CIAE, CGN, IHEP, CASHIPS, etc.
HIAF & CiADS

## Slide 6: CiADS Project (2018-2024)
Design Particle | proton | 
Energy | 500 (250) | MeV
Beam current | 5 (10) | mA
Beam power | 2.5 | MW
Operation mode | CW&Pulse | 
Beam loss | ＜1 | W/m
Reactor power | 7.5 | MWt
CiADS - the Demonstration of ADS at MWs level
Broke ground
Beam trips goal:
<10s, -
10s～5min, 2500/y
>5min, 300/y
SARAF, D, 4MeV, 6kW
SPIRAL2, D, RFQ commissioning
IFMIF, D, RFQ commissioning
PXIE, P, 25MeV, RFQ commissioning

## Slide 7: Schedule of CiADS

## Slide 8: Chinese ADS Front-end Demo Linac (CAFe)
HEBT
DUMP
Beta=0.1
Injector II
IMP
IHEP
Beta=0.21
Beta=0.15
IMP
162.5 MHz Taper HWR
Goal: to demonstrate the technology of 10 mA CW beam of superconducting front-end Linac for CiADS.
Design: 25 MeV, 10 mA, CW, 4.5K
IMP collaboration with IHEP 2011 ~ 2017
Supported by “Strategic Priority Research Program” of the Chinese Academy of Sciences.

## Slide 9: Outlines
Introduction of Chinese ADS Project and CAFe
Operation Status of CAFe
Stability Issues
Conclusion

## Slide 10: Commissioning of Superconducting Linac
162.5 MHz HWR010
4
5
2014.06.06——2014.07.24, RFQ
2014.09.14——2015.02.13, TCM1
2015.03.26——2015.06.29, TCM6, beam accident, RFQ AMP and coupler broken 2015.10.28——2016.01.21, TCM6 commissioning
2016.05.01——2016.06.20, injector II, coupler broken 2016.09.01——2016.12.17, injector II high power
2017.04.28——2017.06.18, CAFe, current leads broken 2017.10.03——2018.01.23, CAFe, operation stability 2018.10.24—— 1 mA CW beam tuning and stability
Commission stage | First CW beam | Max Energy (MeV) | Beam time (hours) | CW beam time Total (hours) | CW Current Max(A) | CW Power Max(kW)
RFQ | Jun. 21, 2014 | 2.15 | 2036 | 90 | 11 | 23
TCM1 | Nov. 24, 2014 | 2.55 | 208 | 22.5 | 11 | 28
TCM6 | Jun. 24, 2015 | 5.3 | 400 | 20 | 4 | 21
Inject II | Sep. 24, 2016 | 10.2 | 327 | 11 | 2.7 | 26
CAfE | Jun. 7, 2017 | 26.1 | 334 | 27 | 0.3 | 5
3
162.5 MHz HWR010
2
162.5 MHz HWR010
1
162.5 MHz RFQ

## Slide 11: Chinese ADS Front-end Demo Linac
 | Ion source | RFQ/IMP | CM1/IMP | CM2/IMP | CM3/IMP | CM4/IHEP
frequency | DC | 162.5 MHz | 162.5 MHz | 162.5 MHz | 162.5 MHz | 325 MHz
output energy | 35 keV | 2.1 MeV | 5 MeV | 10 MeV | 18.5 MeV | 25 MeV
type | ECR | 4-vane | HWR010 | HWR010 | HWR015 | Spoke021
numbers | 1 | 1 | 6 | 6 | 5 | 6
RFQ
Couplers for RFQ and SRF
RF Amplifiers
Microphonics of SRF
EMC of PS
Beam loss due to halo or tails

## Slide 12: Stability of RFQ
Chart: Trips @ Usage of Solid-State Amplifier（108 times）
| Power Source Error | Cavity | Human error
 | 31 | 75 | 1
Chart: Trips @ Useage of Tetrode Amplifier（288 times）
| Power Source Error | Cavity | Interrruption of Power Supply | Human Error
 | 256 | 26 | 3 | 3
Chart: 
| 真空保护 | 腔体水冷 | 打火
 | 30 | 36 | 9
Vacuum
Cooling
Arc
3264 hours
2638 hours
MTBF:11.3 hours
MTBF:24.4 hours

## Slide 13: Stability of SRF
Chart: 
| 耦合器与腔真空 | 腔体温度 | 耦合器夹层真空 | Pt闪断 | 相位不稳脱环
CM1-CM3 脱环原因 | 28 | 2 | 8 | 28 | 419
Chart: 
| 耦合器与腔真空 | 腔体ARC | 腔体温度 | 耦合器夹层真空 | T型盒温度 | 失超快保护 | 氦压波动 | Pt闪断 | 相位不稳脱环
CM1-CM3 脱环原因 | 29 | 5 | 2 | 10 | 1 | 11 | 30 | 5 | 85
Trips during conditioning
Trips during beam commission
HWR010
HWR015
Spoke021

## Slide 14: Operation Reliability Test with low power beam
13
ECR
HV
RFQ AMP
PS
Diagnostics
test
Cryo-plant
Mag-quench
2017-12-19-00：00 ~ 2017-12-22-00：00；72 hours operation test
CW RF and Pulse beam (w/o MPS)
18MeV@1mA@1Hz@10uS & 18MeV@10mA@1Hz@10uS

## Slide 15: Preliminary RAMI analysis w/o active protection
Operation time | Beam time | Down time | Availability
4050 min | 3566 min | 484 min | 0.88
 | ECR HV | RFQ AMP | SRF (incl. LLRF) | Cryo-plant | Power supply
Beam trips | 6 | 2 | 21 | 1 | 1
Down time | 53 min | 77 min | 78 min | 183 min | 100 min
Beam trip required by ADS demo facility | 
Beam trips（10s-5min） | 2500/year
Beam trips（>5min） | 300/year
Availability | 80%
Mean time between failure MTBF (min) | Mean time to repair MTTR (min) | Beam trips (10s-5min) | Beam trips (>5min)
111.4 | 16.1 | 20 | 10
Some long time repair failures (> 5 min), such as HV, AMP, Cryo-plant, PS, have very clear reason, can be avoided in the nest stage.
10s-5min-trip number is less than the requirement. Root cause of trips of SRF are still under investigation.

## Slide 16: Preliminary RAMI analysis with active protection
Planned running time | Real running time | Total down time | Availability
1723 min | 1010 min | 713 min | 0.57
Mean time between failure | Mean time to repair | Beam trips (10s-5min) | Beam trips (>5min)
8.0 min | 5.7 min | 95 | 16
 | ECR | RFQ | SRF | Control system
Beam trips | 2 | 2 | 99 | 23
Down time | 7 min | 131 min | 419 min | 156 min

## Slide 17: MPS Trigs of phase-error during CW Beam
Statistics of MPS trig numbers
phase error trips（） beam: 0.2mA CW Operation time: 22 h
Chart: 
| cm1-1 | cm1-2 | cm1-3 | cm1-4 | cm1-5 | cm1-6 | cm2-1 | cm2-2 | cm2-3 | cm2-4 | cm2-5 | cm2-6 | cm3-1 | cm3-2 | cm3-3 | cm3-4 | cm3-5 | cm4
Phase Trips | 1 | 11 | 1 | 2 | 0 | 2 | 0 | 0 | 30 | 1 | 9 | 1 | 0 | 0 | 1 | 0 | 0 | 13
Ep(MV/m) | 18 | 18 | 20.09 | 27 | 22.44 | 24.74 | 29.94 | 28.64 | 30 | 30 | 22.14 | 18 | 12 | 12 | 20 | 20.07 | 13.95 | 23
Weakness FPC coupling of CM2-3, at least 1/3 of the others, means narrow bandwidth, might be the reason.

## Slide 18: Outlines
Introduction of Chinese ADS Project and CAFe
Operation Status of CAFe
Stability Issues
Conclusion

## Slide 19: Field emission issues
Pt port
FPC port
Trajectory of FE electrons
beam port
beam port
The coupler and Pt ports are located at the strong electric area of coaxial structure.
Highest surface field areas were designed not to face the pickup ports.
FE electrons can see the windows of FPC and Pt.
Electrons on ceramic discharge when accumulating to a certain value
L
H
0
E

## Slide 20: Windows broken due to FE
Broken windows in 2015, Operated for 6 months after broken
Broken windows in 2016
windows

## Slide 21: Pickup discharge due to FE
GDR
SEL
CM1-2
CM1-1
CM1-3
CM1-4
CM1-5
CM1-6
CM1-1：Epk= 18.94 MV/m Gam：355 uSv/h
CM1-2：Epk= 20.53 MV/m Gam：751 uSv/h
CM1-3 : Epk= 21.82 MV/m Gam : 236 uSv/h
CM1-4 : Epk= 27.36 MV/m Gam : 364 uSv/h
CM1-5 : Epk= 23.27 MV/m Gam : 394 uSv/h
CM1-6 : Epk= 24.52 MV/m Gam : 132 uSv/h

## Slide 22: Analysis of pickup
CM1-2
5~10 times
Fluorine

## Slide 23: Microphonics of SRF resonators in CM2
The CM2-3 waveguide support
The CM1-1 waveguide support

## Slide 24: Vibration Sources to CM2-3
Chart: 
Water pump for RFQ
Vacuum Pump for CM
Side bands cause phase error
Wat off + Vac off
Wat off + Vac on
Wat on + Vac on
Wat on + Vac isolation

## Slide 25: CM2-3 spectrum
Chart: 
Open loop
Close loop
155Hz side band is less than -90 dBm

## Slide 26: EMC of PS causes mis-trig of MPS
Main coil 120 A
Ripples p-p 4.1 V
Steering coils 50 A
Ripples p-p 3.4 V
Main coil 120 A
Ripples p-p 0.16 V
Steering coils 50 A
Ripples p-p 0.06 V
Before upgrading
After upgrading

## Slide 27: Beam loss issues
Operation in December 2017, ~18 MeV
Operate CW beam with 18 MeV / 0.2 mA
Current leads cooling trouble limit the transversal focus in CM3

## Slide 28: Beam loss study
The 6-dimensional ellipsoid gaussian is truncated at 3 RMS
1% of the total number of particles was defined as beam halo particles at the position of 10 times of RMS beam size in the horizontal and vertical RMS
 | Alpha X/Y/Z | Beta X/Y/Z m/rad | Emit-X/Y/Z (RMS) π.mm.mrad [ Norm. ] | Emit-X/Y /Z(99.99%) π.mm.mrad [ Norm. ]
Without beam halo | 0.25/-0.05/-0.076 | 0.226/0.096/0.611 | 0.112/0.097/0.094 | 2.06/2.07/2.14
With beam halo | 0.25/-0.05/-0.080 | 0.226/0.096/0.608 | 0.122/0.106/0.010 | 9.16/8.54/8.90
With beam halo

## Slide 29: Outlines
Introduction of Chinese ADS Project and CAFe
Operation Status of CAFe
Stability Issues
Conclusion

## Slide 30: Conclusion
CAFe is to demonstrate the superconducting front-end. The CW beam of 0.3 mA has been commissioned.
The issues of coupler, AMP, FE, EMC of PS have been realized and resolved partly.
The phase-error protection caused by microphonics is main trip source, we did not find the solution yet.
The beam loss in SCL is not understood yet. More simulation and experiments will be done to figure out it.
The goal will be to operate CW beam at 100 kW stably in 2019.

## Slide 31: Thanks for your attention