## Slide 1
Johann M. Heuser
GSI Helmholtz Center for Heavy Ion Research GmbH, Darmstadt, Germany
8th COSY Beamtime Advisory Committee Meeting, IKP FZ Jülich, 2 July 2018
CBM + HADES detector tests at COSY in Q1/2018, and outlook to Q1/2019

## Slide 2
Beamtime in calendar week #9 (26.2. – 5.3.) 2018
  with set-up of equipment in the preceding MD week
  JESSICA cave, protons of Ekin = 1 GeV
  detectors tested:
    CBM-STS:
      prototype modules with near-final integration of sensor, microcable, read-out ASIC
      relevance for Sensor Production Readiness Review in April 2018
    CBM-MUCH:
      had to be cancelled due to travel clearance issue of the VECC team
    HADES/CBM Start-Veto:
      first test of Ultra-Fast Silicon Detectors
  Outlook: further component tests considered in Q1/2019

## Slide 3: (1) CBM Silicon Tracking System
prototype STS module
STS-XYTERv2.0 on FEB-B
microcables
silicon microstrip sensor
285 µm thick
strips 4 cm long
2-sided, 7.5 deg stereo angle
128 channels/side read out
 triangular overlap area
read out with prototype free-streaming DAQ system
1 GeV protons
fiber Hodo1
fiber Hodo2
STS1
STS2
noise: 1090 150 e (n) 1350 200 e (p)
signal mean: 16720 e (n) 20300 e (p)
read-out threshold: 7000 e
signal-to-noise: 153
hit detection efficiency: > 95%
preliminary results:

## Slide 4: (2) Ultra-Fast Silicon Detectors for the HADES/CBM Start-Veto System
First test with 1 GeV proton beam @ COSY
A beam telescope made of 3 sensors:
  Two double-sided scCVD diamond sensors
  One UFSD with pad readout in between
  time precision and efficiency determination
Data analysis in progress
Expected time precision below 100 ps and high rate capability
Possible PID by ToF and dE/dx
4
beam direction
scCVD
diamond
scCVD
diamond
UFSD
sensor
UFSD sensor from Torino
N.Cartiglia, M.Ferrero, V.Sola
Diamond sensors prepared by GSI Detector Laboratory

## Slide 5: Outlook 2019
For further CBM component tests, we consider a further application at CBAC#9:
  beam-time in Q1/2019
  1 week
  component tests towards their production readiness, including e.g.
    read-out ASIC STS-XYTERv2.1
    TRD front-end electronics
    …

## Slide 6
Thanks for the support at IKP!