## Slide 1: CLOCK / SYNC Distribution mCBM
J.Frühauf
17. August 2018

## Slide 2: Needed Clocks
40MHz for AFCK Logic
120MHz for GBTx Logic
160MHz for TOF FEE
n x 40MHz CLK for STS/MUCH and TRD
  recovered from the optical link CLK of the GBTx
SYNC Pulse for AFCK and ToF-FEE
120MHz for GBTx needs to be phase locked to the 40MHz/160MHz for ToF to guarantee a synchronous data taking between subsystems

## Slide 3: SETUP 1: External CLKs
40MHz
120MHz
40MHz
160MHz
SYNC
Splitter
Splitter
AFCK
gDPB
ADDON
FM-S18
AFCK
gDPB
ADDON
FM-S18
AFCK
gDPB
ADDON
FM-S18
AFCK
gDPB
ADDON
FM-S18
...
TOF FEE
160MHz
TRD FEE
n x 40MHz
MUCH FEE
n x 40MHz
STS FEE
4 x 40MHz
CLOSY 1
CLOSY 2
Optic
160MHz
SYNC
SYNC

## Slide 4: CLK Relationship for ToF (SETUP 1)
CLOSY2
AFCK
(160MHz)
GBTx
GET4
SYNC
120MHz
160MHz
SYNC
Rx
Tx
Tx
Rx
CLOSY1: 120MHz & 40MHz phase locked
CLOSY2: 160MHz phase locked to 40MHz from CLOSY1
AFCK: 120MHz from CLOSY1 for GBTx and generate 160MHz for logic
GBTx: 120MHz from AFCK = Phase locked to CLOSY2 160MHz for GET4
GET4: 160MHz from CLOSY2 = Phase locked to 120MHz from CLOSY1 = Phase locked to 120MHz for GBTx
GET4 Rx use 4 times oversampling
GET4 Tx needs to be “phase controlled” on the GBTx side
tune here!
80Mbit
Only one point to tune!
All other relationships are given by cable delays and fix for a given setup
phase locked
CLOSY1
120MHz
40MHz
phase locked
be carful:
120MHz and 160MHz are phase locked to each other but the phase can change after each power cycle of
CLOSY
GBTx Core Reset (FPGA)

## Slide 5: AFCK ZOOM IN
External CLk from CLOSY
120MHz
120MHz
Switch
120MHz
LOGIC &
TIME CNT
SYNC
120MHz
GBTx
Core
120MHz
for GBTx
DATA
PLL
160MHz

## Slide 6: SETUP 1: External CLK generation
CLOSY1 Generate 120MHz and 40MHz
  120MHz for AFCK/GBTx
  40MHz for CLOSY 2
CLOSY2 generates phase locked to 40MHz from CLOSY1:
  160MHz for ToF FEE
  SYNC for AFCK and ToF FEE
AFCK generate phase locked 40MHz for logic out of 120MHz from GBTx Core
CLK for FEE (except ToF FEE) from GBTx

## Slide 7
40MHz
160MHz
SYNC
Splitter
Splitter
AFCK
RJ45
ADDON
FM-S18
AFCK
RJ45
ADDON
FM-S18
AFCK
RJ45
ADDON
FM-S18
AFCK
RJ45
ADDON
FM-S18
...
TOF FEE
160MHz
TRD FEE
n x 40MHz
MUCH FEE
n x 40MHz
STS FEE
n x 40MHz
SETUP 2:
External 40MHz CLK for AFCK
Internal 120MHz generation for GBTx
Optic
160MHz
SYNC
SYNC
40MHz
SYNC
40MHz

## Slide 8: CLK Relationship for ToF (SETUP 2)
CLOSY
AFCK
(160MHz)
GBTx
GET4
40MHz
SYNC
120MHz
160MHz
SYNC
Rx
Tx
Tx
Rx
CLOSY: 160MHz & 40MHz phase locked
AFCK: 40MHz from CLOSY to control 120MHz for GBTx and generate 160MHz for logic
GBTx: 120MHz from AFCK = Phase Controlled by 40MHz from CLOSY
GET4: 160MHz from CLOSY = Phase locked to 40MHz for AFCK = Phase locked to 120MHz for GBTx
GET4 Rx use 4 times oversampling
GET4 Tx needs to be “phase controlled” on the GBTx side
tune here!
80Mbit
Only one point to tune!
All other relationships are given by cable delays and fix for a given setup
controls
phase locked
be carful:
120MHz and 160MHz are phase locked to each other but the phase can change after each power cycle of
CLOSY
AFCK
GBTx Core Reset (FPGA)

## Slide 9: AFCK ZOOM IN
External CLk from CLOSY
40MHz
SYNC
120MHz
PLL
160MHz
LOGIC &
TIME CNT
SYNC
40MHz
SILAB
GBTx
Core
Phase
Tuner
40MHz
120MHz
for GBTx
120MHz
DATA
Phase locked

## Slide 10: SETUP 2: Internal 120MHz generation
synchronize Si570 on FM-S18 with PLL design as it's done in “White Rabbit 2”
external 40MHz from CLOSY will be the reference CLK for this solution
  (suggested by Adrian Byszuk)
CLK for FEE (except ToF FEE) from GBTx