## Slide 1: MIMOSIS,
the CMOS Pixel Sensor for the CBM Micro-Vertex Detector
Frédéric Morel on behalf of the
mIcPHC team of IPHC and
IKF team

## Slide 2: Outline
CBM
  Introduction
MVD
  Requirements
MIMOSIS
  Global architecture
MIMOSIS0
  Preliminary results
Conclusion

## Slide 3: CBM: experiment
Iouri Vassiliev | 2nd Heavy Flavor Meet| Kolkata (India)
Detector installation and commissioning: 2021–2024
First beam: 2025
30/08/2018

## Slide 4: CBM: detector
Joachim Stroth | 56th Winter Meeting on Nuclear Physics | Bormio (Italy)
Fixed Target experiment

## Slide 5: MVD: introduction
Beam
Beam
Vacuum
Beam
20 cm
#0
#1
#2
#3
Micro Vertex Detector (MVD) for the CBM experiment at GSI/FAIR:
Secondary vertex determination (~50 µm), background rejection in di-electron spectroscopy, reconstruction of weak decays
Vacuum/magnetic field operation
4 stations
~300 CMOS sensors
Power dissipation: 150 W
Radiation tolerance: >3 1013neq/cm2 & >3 Mrad
Quadrant (smallest functional unit):
CVD Diamond / TPG carrier for heat evacuation
CMOS pixel sensors: 50 µm thin, 150 mW/cm², ~10 µs read-out
Aluminum heat-sink (actively cooled)

## Slide 6: MVD: radiation
Au Au (1%) 12 AGeV
Non-ionizing
Ionizing
Stations at 5, 10, 15 and 20 cm
MIMOSIS benchmark
@ -20°C without safety margin
Michal Koziel| deutsche physikalische gesellschaft 2017| Münster (Germany)
p Au (1%) 30 GeV
Non-ionizing

## Slide 7: MVD: hit density
Michal Koziel| deutsche physikalische gesellschaft 2017| Münster (Germany)
Non uniform hit density in time and space

## Slide 8: MVD: sensor requirement
 | ALPIDE (demonstrated) | MIMOSIS (MVD design goal) | Factor
Ion. Rad. Tolerance | 2.7 Mrad | > 3 Mrad | 1
Non. Io. Tolerance | 1.7 1013 neq/cm² | > 3x1013 neq/cm² | 2
Heavy ion tolerance | N/A | 1 kHz / cm² | --
Time resolution | 5-10 μs | 5 μs | 2
Hit rate | > 12 kHz/mm² | 700 kHz/mm2 (peak) | 56
Data rate | 1 Gbps | 2.5 Gbps | 2.5
Data reduction | Trigger | Elastic buffer | --
Power consumption (depending on hit density) | 20-35 mW/cm² | 50-75 mW/cm² | 0.4
GBTx compatible | No | Yes | --
Joachim Stroth | 56th Winter Meeting on Nuclear Physics | Bormio (Italy)
ALPIDE is not sufficient to fulfil all the requirements of the MVD
Need a new architecture based on ALPIDE

## Slide 9: MIMOSIS
Matrix
x16
Region 1
504 x 2 x 8 pixels
Pixel
Pixel
Pixel
Pixel
Pixel
Analog FE
Dig
x8
Reg. 2
Reg. 3
Reg.4
Priority Encoder
Top Frame Generator
Region Readout Unit 1
SRAM
128 x 16 bit x 2
RRU 2
RRU 3
RRU 4
DACs
Super Region Readout Units
SRAM
64 x 32 bit x 8
Top Elastic Buffer
2048 x 128bit
Pixel Config
Management
Serializer
Slowcontrol
CLK: 40 MHz
320 MHz
10 bits @ 20 MHz
80 MHz
Registers
I2C
Digital Periphery
20 MHz
32 bits @ 40 MHz
256 bits @ 40 MHz
128 bits @ 80 MHz
N x 320 MHz (N = 1, 2, 4, 8)
Pad Ring
SLVS
x16
16 bits @ 20 MHz
Clock gen
40 MHz
320 MHz
SLVS Ref
32 bits @ 40 MHz
Sequencer
PLL
Data Generation for Multi-Frame Pattern Emulation
DGMFPE
DGMFPE
DGMFPE
Multi-Frame Pattern Emulation
PE Driving and Cluster Finding
16 bits @ 20 MHz
PEDCF
PEDCF
PEDCF
Matrix dimension: 1024 (col.) x 504 (row)
Pixel dimension: 26.88 µm (height) x 30.24 µm (width)
SEU hardened by design with TMR/Hamming (except for data)
Integration time: 5 µs
TowerJazz 180 nm

## Slide 10: MIMOSIS: Data Path
Super Region
Region
Pixel PE
•••
x8
Region U.
Super Region Unit
Pixel PE
•••
Region U.
•••
•••
Super Region Unit
x16
x4
Region PE
Elastic Buffer
Region PE
1,2,4,8 outputs @ 320 Mbps
Dual Port Memories for each block are (except elastic buffer):
filled in series with data from bin time N
emptied in parallel, the data from bin time N-1
8064 Pixels  1 Region through 2 Priority Encoder
4 Regions  1 Super Region through a common bus
16 Super Regions  1 Elastic buffer through a multiplexer
x1008
Pix.
Mux
Block with Dual Port Mem
Glue Logic Block

## Slide 11: MIMOSIS: Elastic buffer
Write speed is 4 times higher than read speed
Use time structure of beam fluctuations to average data frames
The buffer can store up to 9 maximal frames
HEADER
DATA
TRAILER
IDLE
Data Frame N-1
Data Frame N-2
Data Frame N-3
Time bin N+2 = 5µs
Time bin N+1 = 5µs
Time bin N = 5µs

## Slide 12: MIMOSIS: bandwidth
Component | Average | Maximum (3x average +2 sigma) | Available
Region | 10/14 | 55/70 | 100
Super region | 37/55 | 135/230 | 400
Elastic-Buffer input | 345/600 | 1120/1790 | 3200
Elastic Buffer output |  |  | 800
Au/Au 10 AGeV 100kHz
16 bits words during 5 µs
Beam fluctuations:
  Field: 100%/30%
Philipp Sitzmann| deutsche physikalische gesellschaft 2017| Münster (Germany)
Simulation
Simulation

## Slide 13: MIMOSIS: Pixel
2 versions of sensing part:
  DC coupled (similar than Alpide)
  AC with medium voltage bias
Small Area and Low power shaper amplifier:
  Different versions (1 closed to Alpide)
In-pixel Memory:
  New version with double counting removal
MV Bias1
Bias2
Comp
Amp
Dual Port
2 words of 1 bit
Charge inj.
160 aF
AC coupling
Amplification
Sensing part
In-pixel Memory
Full custom digital
Shaping time few µs
Bias1
Charge inj.
160 aF
DC coupling
Different pixel architecture tested with CE18 chips family
(see A. Dorokhov in Front End Electronics 2018)
Pixel output

## Slide 14: MIMOSIS: development plan
MIMOSIS0: portion of pixel array  may 2017
  2 regions wide prototype with AC and DC coupled pixels
MIMOSIS1: 1st full size sensor prototype  Q1 2019
MIMOSIS2: 2nd full size sensor prototype  End 2019
MIMOSIS3: final sensor pre-production  2020

## Slide 15: MIMOSIS0: test setup
Test setup developed by IKF with support of IPHC test team

## Slide 16: MIMOSIS0: preliminary results
S-curves density plot from all DC coupled pixels

## Slide 17: MIMOSIS0: preliminary results
Fe55 response for DC and AC coupled Pixel
Cluster size in function of threshold

## Slide 18: MIMOSIS0: preliminary results
Temporal Noise and Fixed Pattern Noise after Irradiation
Irradiated chips

## Slide 19: Conclusion
Close collaboration between IPHC and IKF for tests and design
Tests:
  Preliminary results of MIMOSIS0 are encouraging
    AC coupled pixels are promising
  Good accordance between tests from MIMOSIS0 and CE18 chips family
Design:
  MIMOSIS0 has validated a part of digital readout of MIMOSIS1
  Digital periphery is under development  no showstopper seen
Next steps:
  Continuing heavy testing (radiations) of MIMOSIS0 and CE18 chips family
  Finalize design of MIMOSIS1 which will be very closed to the final sensors