## Slide 1: Preliminary Results of CERN Testbeam 2018 for Endcap DISC DIRC Prototype
Simon Bodenschatz, Lisa Brück, Michael Düren, Erik Etzelmüller, Klaus Föhl, Avetik Hayrapetyan, Jan Hofmann, Sophie Kegel, İlknur Köseoğlu, Jhonatan Pereira de Lira, Mustafa Schmidt, Marc Strickert
PANDA CM 18/3 – PID-Cherenkov - 2018/11/06

## Slide 2
Testbeam 2018
Move in Y Direction
TOF1
TOF2
SiPM Boxes
Angle scan
Barrel DIRC

## Slide 3: EDD Prototype

## Slide 4: EDD Prototype-FEE connection from inside of the black box
EDD-Prototype
9 Focusing Elements (FEL)
3 Read-out Modules (ROM)
3 Photosensors (MCP-PMTs)
  Photonis Aqua
    3 Rows, 288 pixels
  Hamamatsu
    6 Rows, 384 pixels
  Photonis 2mm
    3 Rows, 288 pixels
  In total 960 connected channels
Focusing Elements
Photonis Aqua
Prototype

## Slide 5: EDD Prototype

## Slide 6
Front-end Electronics
18 ASICs
  15 ASICs are connected to one D-Board (EDD Prototype)
  3 ASICs are connected to second D-Board (SiPMs, MCP-TOFs, Laser)
First results are obtained from Photonis Aqua.
  4 and half ASICs, (288 Channels) are connected to Photonis Aqua.
Prototype-FEE connection from outside of the black box

## Slide 7: Offline analysis
Mapping between pixels of photonis aqua and ASIC channels
Time difference between laser and pixels of photonis aqua
  Time Difference between ASICs
      All MCP-PMTs are connected to ASICs with identical cables
Equalization of data
Y Scan, between 5mm to 379mm, step size 17mm
  p = 10 GeV/c
Angle Scan, 3º -18º with step size 1º
  p = 4 GeV/c
Current analysis only includes if events are between TOF1 & TOF2 time interval

## Slide 8: Laser trigger & photonis aqua for 3 FELs
Each focusing element (FEL) is connected to two different ASICs
ASIC 1
ASIC 16
Time_FEL2-Time_Laser [ps]
Pixel
FEL 2

## Slide 9: Equalization of data
Pixel 53 has the largest amount of events
xpeak is the reference time
Time_pixel-xpeak [ps]
#Entries
Time_Pixel53-Time_Laser [ps]
#Entries
xpeak
Time difference between all pixels and xpeak for FEL2

## Slide 10
Equalization of FEL2 data
FEL2
FEL2
Time_FEL2-Time_Laser [ps]
Before equalization
After equalization
Time_FEL2-Time_Laser [ps]
Pixel
Pixel

## Slide 11
Equalization for FEL1 & FEL3 data
Before equalization
After equalization
Time_FEL3-Time_LASER [ps]
Pixel
Time_FEL1-Time_LASER [ps]
Pixel
Time_FEL1-Time_LASER [ps]
Pixel
Time_FEL3-Time_LASER [ps]
Pixel
FEL1
FEL1
FEL3
FEL3

## Slide 12: Trigger selection
Time Interval for Triggers is between -34ns to -39ns was selected
p = 10GeV/c
[ps]
TOF1
TOF2
EDD
CBX
CBY
SiPM

## Slide 13
-39ns < Time_TOF1-Time_TOF2 < -34ns
Equalized data for FEL3
Time_TOF1-Time_FEL3 [ps]
Time_TOF1-Time_FEL3 [ps]
Pixel
Pixel
Pixel
Pixel
Y Position [mm]
Y Position [mm]
Time Cut: 40ns < Time_TOF1-Time_FEL2 < 44ns
y=141mm

## Slide 14
Time_TOF1-Time_FEL2 [ps]
Pixel
Time_TOF1-Time_FEL2 [ps]
Pixel
Time Cut: 38ns < Time_TOF1-Time_FEL2 < 45ns
Y Position [mm]
Pixel
Y Position [mm]
Pixel
-39ns < Time_TOF1-Time_TOF2 < -34ns
Equalized data for FEL2
y=141mm

## Slide 15
-39ns < Time_TOF1-Time_TOF2 < -34ns
Equalized data for FEL1
Time_TOF1-Time_FEL1 [ps]
Pixel
Time_TOF1-Time_FEL1 [ps]
Pixel
Time Cut: 41ns < Time_TOF1-Time_FEL1 < 45ns
Y Position [mm]
Pixel
Y Position [mm]
Pixel
y=226mm

## Slide 16: Trigger selection
pion: -38ns < Time_TOF1 - Time_TOF2 < -34ns
proton: -41ns < Time_TOF1 - Time_TOF2 < -38ns
p = 4GeV/c
proton
pion
TOF1
TOF2
EDD
CBX
CBY
SiPM

## Slide 17
Preliminary results of angle scan for pion
FEL1
FEL1
FEL 2
FEL 2
Time Cut: 41ns < Time_TOF1-Time_FEL1 < 45ns
-38ns < Time_TOF1-Time_TOF2 < -34ns
Time Cut: 41ns < Time_TOF1-Time_FEL2 < 45ns

## Slide 18
Preliminary results of angle scan for pion
FEL 3
FEL 3
Time Cut: 41ns < Time_TOF1-Time_FEL3 < 45ns
-38ns < Time_TOF1-Time_TOF2 < -34ns

## Slide 19: Channel 53 peak behavior during the days
Y Scan
Days in August
[ps]
Angle Scan
Blue dots: Gaus Fit
Red dots: Data

## Slide 20: Preliminary analysis
Equalization is done
Missing Channels are identified.
MCP-TOFs are used as triggers for
  p = 10 GeV/c -39ns < TOF1 - TOF2 < -34ns
  p = 4 GeV/c -38ns < TOF1 - TOF2 < -34ns for pion
      -41ns < TOF1 - TOF2 < -38ns for proton
Proper time cuts to reduce the background

## Slide 21: Future plans about analysis
MCP-TOF1 and SiPM boxes will be used as triggers
Reconstruct Cherenkov angle
SiPM boxes will be used to
  Eliminate background with spatial cut
  Improve Cherenkov angle resolution
All steps will be repeated for also Hamamatsu & Photonis 2mm
Time walk correction

## Slide 22: Thank you.

## Slide 23
Backup
SiPM bars
Photonis Aqua
Photonis 2mm
Photonis 2mm