Update on the Barrel DIRC Prototype Test @ CERN Jul-Aug, 2018
Prototype test at CERN
Observables
Reconstruction results
Summary
PANDA meeting
11.18
Roman Dzhygadlo,
PANDA Cherenkov Group

---
DIRC Prototype Test 2017
Goal:
evaluate performance of the 4x2 MCP-PMTs layout
test different optical couplings
4x2 MCP-PMTs layout
Highlights of the geometry:
33 degree prism as expansion volume
narrow bar as the radiators
3 layer spherical lens as focusing
4x2 MCP-PMTs (vs. 4x3 last year)
4x3 MCP-PMTs layout
Test conditions:
CERN PS/T9 area
beam type: protons and pions
beam momentum: 10, 9, 8, 7, 6, 5, 4, 3, 2 GeV/c
TOF PID
different configurations of the DIRC prototype
different DIRC prototype angles

---
CERN 2017 Prototype Test
Beam profiling
Trigger
TOF particle identification
π/p beam
DIRC
CERN PS/T9 area
TOF2
TOF1
T3
T2
T1
EDD
HODOSCOPE

---
Time Resolution
Improvements:
better power supply WIENER PL-506 for the 48V (TRB) and 4V (PADIWA)
improved calibration system (with two diffusers):

---
Time Resolution
Time resolution of all 512 channels:
2017 data (768 channels):
stable with time
Pilas laser + TRB time resolution ~190ps
TRB time resolution ~17ps

---
Geometry Calibration
Example for 20 deg:
separation [s.d.]
separation [s.d.]

---
Examples of the Hit Pattern
20 degree polar angle
pions and protons @ 7 GeV/c
bar + 3 layer spherical lens
beam data with proton tag
beam data with pion tag
geant simulation for pions

---
Comparison with 4x3 layout
20 degree polar angle
pions and protons @ 7 GeV/c
bar + 3 layer spherical lens
pions
4x3 MCP-PMTs
4x2 MCP-PMTs

---
Geometrical Reconstruction
π/p @ 7 GeV/c with a bar + 3LS lens
beam data @ 20O
beam data @ 20O
~72 photons
~97 photons
protons
4x2 layout
4x3 layout
30-40% less photons comparing to 4x3 layout

---
Geometrical Reconstruction
π/p @ 7 GeV/c with a bar + 3LS lens
beam data
protons
SPR = 8.6 mrad
 pions
 protons

---
Geometrical Reconstruction
π/p @ 7 GeV/c
with a bar + 3LS lens
beam data @ 20O
3.5 ± 0.3 s.d.

---
Bar with 3L Spherical Lens @ 7 GeV/c
π/p separation power (using time imaging reconstruction):
beam data @ 20O
4.8 s.d.
beam data @ 120O
2.7 s.d.

---
Azimuthal Scan
φ=10 deg
simulation for 4x3 layout
4x2 layout performs better for φ=0 while 4x3 performs good in all region

---
Bar-Prism X Step

---
Bar-Prism X Step

---
Momentum Scan for Bar with 3LS Lens
3.0 s.d.
@ 8 GeV/c
4.8 s.d.
@ 6 GeV/c
π/p / [GeV/c]	π/K / [GeV/c]	sep / [s.d.]	~ sep in PANDA / [s.d.]
3	1.5	8.2	13.4
5	2.6	6.3	7.4
6	3.1	4.8	6.5
7	3.6	3.8	5.6
8	4.1	3.0	4.5
10	5.1	1.8
7.7 s.d.
@ 4 GeV/c

---
Momentum scan with X Step
beam data

---
Summary and Outlook
Test beam was successful
Time resolution of the system was determined to be ~190 ps
(comparing to ~250 ps in 2017)
4x2 layout performs on the same level as 4x3
Good agreement between data and simulations
Momentum scan showed good performance
for different momenta
Ongoing studies:
optical grease vs. optical cookies
analytical PDF
     Thank you for your attention

---
Backup

---
DIRC Prototype Photos
Polar angle 90O
Azimuthal angle 0O
Polar angle 25O
Azimuthal angle 10O

---
Geometrical Reconstruction
Reconstruction: direction from LUT for hit pixels are combined with charge track direction
one pixel
charged track

---
Time Imaging Reconstruction. PDFs
beam data with plate @ 7 GeV/c @ 25 degree
detection time
proton candidate
pion candidate
PDFs of proton and pion
for given pixel