## Slide 1
NICA in heavy ion mode – status and plans

## Slide 2
Heavy ion colliding beams up to 197Au79+ + 197Au79+
at sNN = 4 ÷ 11 GeV , Laverage= 1x1027 cm-2s-1
Light-Heavy ion colliding beams of the same energy range and L
Polarized beams of protons and deuterons in collider mode:
pp spp = 12 ÷ 26 GeV Lmax ≈ 1x1032 cm-2s-1
dd sNN = 4 ÷ 13.8 GeV
NICA beams
Extracted beams of light ions and polarized p and d for fixed target experiments:
Li  Au = 1  4.5 GeV /u ion kinetic energy
p, p = 5 ÷ 12.6 GeV kinetic energy
d, d = 2 ÷ 5.9 GeV/u ion kinetic energy

## Slide 3
Stage I
Fixed target experiment with heavy ions
Stage II
Basic configuration of the collider and detector
Full configuration, heavy ion collisions
Collisions of heavy ions with light ions (protons)
Stage III
Spin physics program
Stages of the experimental program realization

## Slide 4
Injection complex: KRION, HILAc, LU20
Synchrotron Booster
BT Line Booster – Nuclotron
Nuclotron upgraded
BM@N Detector setup
Experiment
“The Baryonic Matter at Nuclotron”
Parameters:
Ebeam = 1-6 GeV/u; beams: from p to Au; Intensity~107 s-1 (Au)
NICA Stage I:
- fixed target experiment at the Nuclotron extracted beams
which main goals are investigations of strange / multi-strange hyperons, hypernuclei production and short range correlations

## Slide 5
12C BM@N SRC
40Ar 84Kr BM@N
Run 55: February – April 2018
Two tech runs @ 2016-2017
the first run with startup configuration of BM@N
experiment BM@N SRC
0,5
1,0
1,5
2,0
2,5
3,0
Kr26+
30/03/2018
s
03.04

## Slide 6
NICA-MPD heavy-ion program
The stage II is split in two phases:
Stage II-a: The basic configuration of the NICA complex
Stage II-b: The project (full) configuration of the NICA complex
NICA Stage II:

## Slide 7
Nuclotron (45 Tm)
injection of one bunch
of  2×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Linac LU-20
Ion sources
Fixed Target Area
Booster (25 Tm)
1(2-3) single-turn injection,
storage of (2  4)×109 ions,
acceleration up to 100 MeV/u,
electron cooling, acceleration
up to 600 MeV/u
Linac HILac
KRION
IP-1
IP-2
Stripping (80%) 197Au31+ => 197Au79+
KRION
Linac HILAc
Booster (25 Tm)
1(2-3) single-turn injection,
storage of (2  4)×109 ions,
acceleration up to 100 MeV/u,
electron cooling, acceleration
up to 600 MeV/u
Nuclotron (45 Tm)
injection of one bunch
of  2×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Linac LU-20
Ion sources
Fixed Target Area
Slow resonance extraction
Collider
L ≥ 1027 см-2с-1
2015-2018
work in progress
assembly
commissioned / existing
Facility components – status

## Slide 8
Nuclotron (45 Tm)
injection of one bunch
of  2×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Linac LU-20
Ion sources
Fixed Target Area
Booster (25 Tm)
1(2-3) single-turn injection,
storage of (2  4)×109 ions,
acceleration up to 100 MeV/u,
electron cooling, acceleration
up to 600 MeV/u
Linac HILac
KRION
IP-1
IP-2
Stripping (80%) 197Au31+ => 197Au79+
KRION
Linac HILac
Booster (25 Tm)
1(2-3) single-turn injection,
storage of (2  4)×109 ions,
acceleration up to 100 MeV/u,
electron cooling, acceleration
up to 578 MeV/u
Nuclotron (45 Tm)
injection of one bunch
of  2×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Linac LU-20
Ion sources
Fixed Target Area
Slow resonance extraction
Collider
L ≥ 1027 см-2с-1
2019
Facility components – status
work in progress
assembly
commissioned / existing

## Slide 9
Linac HILac
KRION
KRION
Linac HILAc
Booster (25 Tm)
up to 578 MeV/u
Nuclotron (45 Tm)
up to 4.5 GeV/u
Injection - chain
for heavy ions
Heavy ion source KRION ESIS type project up to 1.5·109 Au31+ particles per cycle (achived 5·108 Au31+ )
at repetition frequency up to 10 Hz
Overall commissioning
3.2 MeV/u, Au31+, 10.2016

## Slide 10
Linac HILac
KRION
KRION
Linac HILAc
Booster (25 Tm)
up to 578 MeV/u
Nuclotron (45 Tm)
up to 4.5 GeV/u
Injection - chain
for heavy ions
17.01.19
Booster - Nuclotron
channel contracted to BINP
commissioning at end of 2019
HiLac – Booster
channel
mounting started

## Slide 11
Linac LU-20
Ion sources
Nuclotron (45 Tm)
up to 4.5 GeV/u
Linac LU-20
Ion sources
Injection - chain
for light ions
New fore-injector for LU-20 with buncher + Source of Polarized Ions
 | Polarized deutrons | Polarized protons
Obtained beam current in 2017 (source) | 2 mA | 0.4 mA
Project beam current (source) | 5-6 mA | 5-6 mA
Obtained beam intensity in 2017 (Nuclotron) | 2.2x109 ppc | 1.8x108 ppc
Project beam intensity (Nuclotron) | 1-2x1010 ppc | 1-2x1010 ppc
3 runs in 2016-2017 (#52-54) with d↑, 1 run (#54) with stable p↑ beam
JINR, INR, ITEP, MEPHI,
Resonator is fabricated in Sneshinsk
1.8 E8
Polarized protons

## Slide 12
Time-schedule
Booster
Booster (25 Tm)
up to 578 MeV/u
Apr-May 2019 –
technological run
Oct-Nov 2019
- commissioning with the beam

## Slide 13
Booster dipoles
Leff. @ 9745 A
σrms = 2.3*10^(-4)
Leff. @ 625 A
σrms = 4*10^(-4)
Booster quadrupoles
Testing results

## Slide 14
Booster
Booster (25 Tm)
up to 578 MeV/u
17.01.19
20 dipoles’ units delivered to the tunnel

## Slide 15
Routine operation of SPI and new fore-injector
Polarized deuterons acceleration: Intensity up to 2*109 per cycle
8E8
Nuclotron: polarized deuterons and protons
12C+6 beam extraction (3,5 Gev/u) RUN #55 (05.02.18-05.04.18)
12C+6 5*108 Tspill = 4s, kdc= 99,5%
Nuclotron: slow extraction
Acceleration of 197Au79+ up to 4.5 GeV/u
Injection system for 197Au79+ from Booster at 578 MeV/u
Slow extraction system for 197Au79+ at 1  4.5 GeV/u
Nuclotron: tasks
for 2020

## Slide 16
Nuclotron (45 Tm)
up to
4.5 GeV/u max.
Lambertson magnets are based on existing spare yokes for slow extraction system of Nuclotron
Concept has been developed
Nuclotron high energy beam injection system
16
Design of a cold kickers is in progress
Warm prototype for mechanical tests has been manufactured
Nuclotron fast extraction system

## Slide 17
Magnetic element | Number | Effective length, m | Max. magnetic field (gradient), T (T/m)
Long dipole | 21 | 2 | 1.5
Short dipole | 6 | 1.2 | 1.5
Quadrupole Q10 | 22 | 0.353 | 31
Quadrupole Q15 | 6 | 0.519 | 31
Steerer | 33 | 0.466 | 0.114
Magnets of the Nuclotron-Collider channel are in development by SigmaPhi.
Nuclotron-Collider beam transport channel

## Slide 18
Developed at 1980-th…
“Nuclotron”-cable
SC-magnets for synchrotrons
SC-cable
“Nuclotron”- magnets
NICA Collider
Nuclotron magnets’ technology

## Slide 19
First Superconducting heavy ion accelerator
Nuclotron – Superconducting Synchrotron
operation since 1993

## Slide 20
NICA Collider
Nuclotron magnets’ technology
Racetrack of 503.04 m circumference
2 Interaction points
0.32 m vertical beam separation
double-aperture sc-magnets with 1.8 T max field
45 T·m magnetic rigidity
ion kinetic energy range from 1 GeV/u to 4.5 GeV/u for Au79+
vacuum: 10−9 Pa;
Average luminosity 1027 cm−2·s−1 for gold ion collisions at √sNN = 9 GeV.

## Slide 21
Collider
+ RF-2 systems in the project version
+ RF-3 systems in the project version
+ S-cooling (transverse)
+ E-cooling
1. Injector chain: KRION => Booster => BTL BN => Nuclotron
2. BTL Nuclotron => Collider
3. Collider equipped with
RF-1 (barrier voltage system) for ion storage
RF-2 in a reduced version: 2 cavities per ring instead 4 (50 kV RF amplitude instead 100 kV)
1 channel of S-cooling per ring (cooling of longitudinal deg. of freedom)
Result: 22 bunches of the length   2 m per collider ring that = 5e25 cm-2s-1.
NICA Stage II-a (basic configuration):
NICA Stage II-b (full configuration):
Result: 22 bunches of the length  = -star = 0.6 m per collider ring that = 1e27 cm-2s-1.

## Slide 22
Time-schedule
Collider
IP-1
IP-2
Collider
L ≥ 1027 см-2с-1

## Slide 23
Collider magnets’ system
Assembly and testing
Parameter | Dipole | Lens
Number of magnets | 80+8* | 78+12**
Max. magnetic field (gradient) | 1.8 T | 23.1 T/m
Effective magnetic length | 1.94 m | 0.47 m
Beam pipe aperture (h/v) | 120 mm / 70 mm | 
Distance between beams | 320 mm | 
Overall weight | 1670 kg | 240 kg
*- beams vertical elevation dipoles
**- final focus quadrupoles
178 structural sc-magnets to assemble and test

## Slide 24
SC-magnets to assembly and testing

## Slide 25
NICA Collider magnets testing
26 dipoles’ yokes delivered to JINR
5 dipoles’ successfully passed cryogenic tests
testing results

## Slide 26
RF-system
3D model of RF3 station
RF system for basic configuration is under construction at BINP – 2020
RF system for project configuration is under development at BINP – 2021
RF1 station: preparation for the tests

## Slide 27
Electron Cooling System of NICA Collider, Ions 197 Au79+
HV Electron Cooler for NICA Collider
Design and construction at BINP
Installation at NICA in 2021
together with 4 RF2 and 16 RF3 stations
Parameter | Value
Electron energy, MeV Energy instability, E/E | 0.2 – 2.5  110-4
Electron beam current, A | 0.1 – 1.0
Cooling section length, m | 6.0
Solenoid magnetic field, T Field inhomogeneity, B/B | 0.05 – 0.2  110-5

## Slide 28
Septum
Length, m | 2.5
Max magnetic field, T | 1
Aperture, mm×mm | 45×45
Septum thickness, mm | 3
Pulse shape | semisinusoidal
Pulse duration, μs | ~ 10
Technical design development is in progress.
Concept of power supply has been developed.
Injection-system

## Slide 29
Beam dump system – under designing
Kickers
Lambertson magnet
Septa
Beam-dump system

## Slide 30
How does NICA collider look like?
LHC
RHIC
NICA
…like others

## Slide 31
For round beams and head-on collisions
Number of bunches nb has to be as large as possible
but the inter-bunch distance is to be large enough
to avoid parasitic collisions inside detector
Train of bunches is prepared by injection chain
the bunch intensity Nb has to be maximal
the emittance  growth has to be minimized in all elements of injection chain
beta function in collision point * has to be as small as possible
but comparable with bunch length s
to avoid luminosity reduction due to “hour-glass” factor
Luminosity
Collider
Detector

## Slide 32
Synchrotrons
tune diagram
ideal if = const for all particles in the beam, but
self space charge effect
beam-beam effect
tunes vs dp/p:
  Major effects limiting the luminosity
  Space charge
  Luminosity lifetime
  IBS
  Instabilities

## Slide 33
The bunch brightness Nb/ is limited by two main space charge effects:
beam-beam parameter (linear part of the tune shift due to fields of opposite bunch)
incoherent shift of the betatron tune (Laslett tune shift)
- bunching factor
For NICA collider parameters
  Space charge

## Slide 34
The beam space charge creates the major luminosity limitation
Large luminosity requires
  Small circumference, C
  Short separation length, C/nb
  value of σs/* in 1-2
  Large emittance => large acceptance

## Slide 35
Beam Maintenance in Collider Rings with Cooling Technique
Beam Maintenance in Collider Rings with Cooling Technique
I.Meshkov Three stages of the NICA project COOL’2015 18 September 2015
Space charge dominated regime: Electron cooling is used to maintain
bunch 3D emittance.
E-Cooling
Two modes of the collider operation
1 1.5 2 2.5 3 3.5 4 4.5 5
E, GeV/u
Space charge dominated mode (ΔQ ≤0.05) | IBS dominated mode
ε and dp/p are optimized independently. The bunch relaxation? is suppressed by cooling. Luminosity is limited by space charge effects | ε and dp/p are “equi-partitioned”, either fast bunch relaxation. Luminosity can be obtained at small ΔQ<0.05
10000
1000
100
10
1
 e-cooling
|| e-cooling
IBS (3D equilibrium)
stoch (D.Möhl)
IBS dominated regime: Stochastic cooling is used to suppress beam
IBS influence.
Stochastic cooling
Time, s

## Slide 36
Ring + vertical beam separation
Ring symmetry =2
Two Beams  symmetric optics
Rings structure

## Slide 37
Two Beams  symmetric optics
Ring + vertical beam separation
Lattice

## Slide 38
Ring + vertical beam separation
Ring symmetry =2
Two Beams  symmetric optics
Lattice
Beta-IP = 0.6m
Beta-max=145m

## Slide 39
Collider scheme plan view

## Slide 40
Collider electrical power supply scheme
for 1 ring (2nd-blue-upper)
Индекс | Max Ток, А
2-PS-1 | 10500
2-PS-2 | 1000
2-PS-3 | 600
Индекс | Max Ток, А
2-APS-1… 2-APS-60 | 300
Main power supplies
Additional power supplies

## Slide 41
Structural quads’ feed currents

## Slide 42
Collider quads spec.

## Slide 43
Ring-10 –
quads lengths adjusted to power all magnets in series
Beta-functions
Linear optics
Beam Vertical separation magnets
MPD+ECool solenoids
RF-system
Corrector magnets:
Closed Orbit
Chromaticity
X-Y-coupling
Edge fields
Qx,y = 9.44
* = 0.6m

## Slide 44
sF1=43 T/m^2
sD1=173 T/m^2
sF2=43 T/m^2
sD2=173 T/m^2
Chromaticity correction

## Slide 45
Quadrupoles’ fringe field effect

## Slide 46
FF-quads fringe fields shrink DA
Beta_IP=0.35 m
S.A. Glukhov, E.B. Levichev,
RuPAC-2016

## Slide 47
Ring dynamic aperture
FF-quads fringe fields shrink DA
Beta_IP=0.35 m
Beta_IP=0.50 m
Beta_IP=0.60 m
25 % luminosity decrease
Beta_IP=0.35 m
Beta_IP=0.60 m
use octupoles to “correct” fringe field effect

## Slide 48
Correction magnets setup
Chromaticity correction
X-Y coupling correction
sF1=43 T/m^2
sD1=173 T/m^2
sF2=43 T/m^2
sD2=173 T/m^2
Bx=0.15 T
By=0.15 T
[T/m]: -2.48
0.18
0.57
0.64
sF1=48 T/m^2
sD1=185 T/m^2
sF2=48 T/m^2
sD2=185 T/m^2
Orbit correction
Fringe fields correction
oF1=150 T/m^3
oF2=60 T/m^2
oF1=150 T/m^3
oF2=60 T/m^2
[T/m]: -2.51
0.26
0.59
0.61
oF1=150 T/m^3
oF2=60 T/m^2
oF1=150 T/m^3
oF2=60 T/m^2
9.10
9.44
9.10
9.44
+

## Slide 49
Ring tune
9.10 9.44
3 % of focusing strength

## Slide 50
Ring tune
9.10 9.44

## Slide 51
Thank you

## Slide 52
NICA-MPD heavy-ion program
Main properties, EOS
- particle yields & spectra, ratios, femtoscopy, flow
In-Medium modification of hadron properties
- onset of low-mass dilepton enhancement
Deconfinement (chiral) phase transition at high rB
- enhanced strangeness production
QCD Critical Point
- event-by-event fluctuations & correlations
Y-N (hyperon-Nucleon) interactions in dense nuclear matter - hypernuclei

## Slide 53
Polarized beams
pp at spp = 12 - 27 GeV, Lav ≈ 1032 cm-2s-1
dd at sNN = 4 - 13 GeV
longitudinal and transverse polarization in SPD and MPD
Physics tasks
Nucleon spin structure studies
Drell-Yan pairs Direct photons J/ψ production
spin-dependent effects in elastic pp, pd and dd scattering;
spin effects in exclusive hadron production;
spin effects in production of hadrons with high pT
SPD/NICA will provide a unique opportunity not available at other facilities
to study all the eight nucleon PDF in one experiment
and obtain comprehensive information on the nucleon spin structure
at high statistical level and with minimal systematic uncertainties.
Timeline
open a project for the SPD design: Jan. 2019
preparation of CDR: 2019
preparation of TDR (+ prototyping); stage I: 2020 – 2022
stage II: 2023
construction of the detector: 2022 – 2025
first measurements: 2025
Spin Physics Detector (SPD)
Notes: Study of nucleon spin structure must prove the sum rule and to solve a puzzle of “spin deficit”. NICA collider will provide collisions of protons and deuterons with all combinations of polarization – transversal and longitudinal. It will allow to measure all 8 intrinsic-transverse-momentum PDFs at leading twists in one experiment. MMTDY mechanism and SIDIS processes are good tools for these measurements.

## Slide 54
Routine operation of SPI and new fore-injector
Polarized deuteron acceleration: Intensity up to 2*109 per cycle
Deuteron Spin Structure experiment, internal target
8E8
Nuclotron: polarized deuterons and protons
1.8 E8
Polarized protons

## Slide 55
55
12C+6 beam extraction (3,5 Gev/u) RUN #55
12C+6 5*108 Tspill = 4s, kdc= 99,5%
78Kr 2*105 Tspill = 10s, kdc= 99,3%
78Kr+26 beam extraction (2,8 Gev/u) RUN #55
Nuclotron: slow extraction

## Slide 56
Parameter | Project | Status (June 2018)
Max. magn. field, T | 2 | 2 (1.7 T routine)
B-field ramp, T/s | 1 | 0.8 (0.7 routine)
Accelerated particles | p–U, d | p, d, p – Xe
Max. energy, GeV/u | 12 (p), 5.8 (d) 4.5( 197Au79+) | 5.6 (d, 12C), 3.6 (40Ar16+)
Intensity, ions/cycle | 1E11(p,d), 2E9 (A > 100) | d 4*1010 (2*1010 routine), 7Li3+ 3*109 12C6+ 2*109 40Ar16+ 1*106 78Kr26+ 2*105 124Xe42+ 1*104
Nuclotron: status for 2018
 Acceleration of 197Au79+ up to 4.5 GeV/u
 Injection system for 197Au79+ from Booster at 578 MeV/u
 Slow extraction system for 197Au79+ at 1  4.5 GeV/u
 Upgrade of control system (synchronization)
Nuclotron: tasks

## Slide 57
Dy –correction
- skipped

## Slide 58
X-Y Coupling suppression
4 skew quads /
half ring [T/m]:
-2.48
0.18
0.57
0.64

## Slide 59
Ring tune
9.44 9.10
-300 А – to all quads (except FF) +0 А to D-quads in arcs

## Slide 60
Ring tune
9.10 9.44