## Slide 1
mCBM@SIS18
Christian Sturm, GSI
CBM @SIS100
2018 - 2022
2024 -
full system test-setup for high-rate A+A collisions
to test prototype detectors
to test front-end electronics (FEE)
to develop & test the data transport to DPB & FLIB (1st and 2nd FPGA)
to develop & test the data transport to FLES
to develop & test μ-slice + time-slice building
to test & develop data transport using a CRI
to develop & test a general timing + fast control system (TFC)
to develop & test the detector + experiment control system
to develop & test the online reconstruction + selection
to develop & test the software online framework
to develop & test the data analysis
2019
2020
+

## Slide 2: CBM DAQ upgrade (2019)
2 KINTEX-7 FPGA boards replaced by a ZYNQ Ultrascale+ FPGA board
Firmware functionality stays the same
CRI-12
DPB
FLIB
Pre-Processing
µS Tx
µS Rx
FLES PCI-E interface
10 Gb Optical link
Pre-Processing
FLES PCI-E interface
CRI = Common Readout Interface

## Slide 3: mCBM data taking 2019 & 2020
2018→ 2019 | development & commissioning data transport, data analysis, detector tests
2019→ 2020 | approaching full performance subsystems completed, high-rate data transport / processing → online reconstruction
requested beamtime
was fully granted
by GSI/FAIR G-PAC
2018 – Q1 2019:
1st tests during engineering runs Nov./Dec. 2018
4x weeks mCBM (parasitc) beam: March 4 – March 31, 2019
beam: 107Ag, 1.65 AGeV (top SIS18)
by G-PAC granted beam time for 2018 (→ 2019):
51 parasitic shifts → 41h / 28d ≈ 1 - 2h / d
fixed slots per day (i.e. 12:00 – 13:00 & 18:00 – 19:00)
new mCBM
control room

## Slide 4: mCBM data taking 2021 & 2022
proposal to be submitted in 2019/20
2020 → 2021 | 1st benchmark run Λ reconstruction production runs benchmark coll. systems: Ni+Ni 1.93AGeV & Au+Au 1.24AGeV
2021 → 2022 | 2nd benchmark run Λ reconstruction in Ni+Ni and Au+Au collisions at various projectile energies → Λ production excitation function
Λ - slope parameter:
smaller than proton
not explained by transport models
reason unclear:
  rescattering cross section ?
  repulsive potential ?

## Slide 5: Granted mCBM beam time 2019 - 2020
“For this task, we apply (1) for 30 shifts of parasitic beam time, distributed over
four development weeks. At the end of that year’s block of SIS18 beam
we apply (2) for 21 shifts (one full week) of parasitic beam time to perform
high-rate detector tests.” mCBM@SIS18 proposal, submitted on June 19, 2017

## Slide 6: Announcement for beam time request 2020 - 2021

## Slide 7: CBM Collaboration: 55 institutions, 470 members
China:
CCNU Wuhan
Tsinghua Univ.
USTC Hefei
CTGU Yichang
Chongqing Univ.
Czech Republic:
CAS, Rez
Techn. Univ. Prague
France:
IPHC Strasbourg
Germany:
Darmstadt TU
FAIR
Frankfurt Univ. IKF
Frankfurt Univ. FIAS Frankfurt Univ. ICS
GSI Darmstadt
Giessen Univ.
Heidelberg Univ. P.I.
Heidelberg Univ. ZITI
HZ Dresden-Rossendorf
KIT Karlsruhe
Münster Univ.
Tübingen Univ.
Wuppertal Univ.
ZIB Berlin
India:
Aligarh Muslim Univ.
Bose Inst. Kolkata
Panjab Univ.
Univ. of Jammu
Univ. of Kashmir
Univ. of Calcutta
B.H. Univ. Varanasi
VECC Kolkata
IOP Bhubaneswar
IIT Kharagpur
IIT Indore
Gauhati Univ.
Korea:
Pusan Nat. Univ.
Poland:
AGH Krakow
Jag. Univ. Krakow
Warsaw Univ.
Warsaw TU
Romania:
NIPNE Bucharest
Univ. Bucharest
Hungary:
KFKI Budapest
Eötvös Univ.
30th CBM Collaboration meeting in Wuhan
24-28 September 2017
CBM Scientists
Russia:
IHEP Protvino
INR Troitzk
ITEP Moscow
Kurchatov Inst., Moscow
VBLHEP, JINR Dubna
LIT, JINR Dubna
MEPHI Moscow
PNPI Gatchina
SINP MSU, Moscow
Ukraine:
T. Shevchenko Univ. Kiev
Kiev Inst. Nucl. Research
Chart: 
| China | Czech Republic | France | Germany | Hungary | India | Poland | Romania | Russia | Ukraine
 | 9.1912 | 2.2059 | 0.73529 | 35.2941 | 1.1029 | 13.6029 | 8.8235 | 5.8824 | 20.5882 | 2.2059

## Slide 8
Backup
mCBM

## Slide 9: To Do for 1st mCBM commissioning beam time, March 2019
hit rates
not fully understood,
T0 saturation ?
furthermore:
reconstruction of events, 4D data analysis
complete mSTS detector station-0, exchange mMUCH electronics parts
commissioning of new mCBM control room
prepare installation of mRICH and mPSD modules

## Slide 10: Present read-out chain of mSTS
STS modules 8 STS-XYTER v2.0 on FEB-8
copper link
optical link
FLES input node
with FLIB
boards
HTD cave, on detector
Green Cube
optical link
DAQ container
μTCA crate
with AFCK
boards
Common
GBTx
Readout Board

## Slide 11: mCBM read-out and data transport Start version

## Slide 12: mDAQ and mFLES 2018 (start version)
present design
 |  | Device | Function | Location
1 | 70x | GBTx | data concentrator | Cave, on detector
2 | 12x | AFCK | 1st layer FPGA board | DAQ container
3 | 96x | Optical fibers | Data transport | DAQ → Green IT Cube
4 | 4x | FLIB | 2nd layer FPGA board | Green IT Cube
5 | 2x | mFLES input node | Input stage | Green IT Cube
6 | 42x | mFLES compute nodes | Processing stage | Green IT Cube
1
2
3
4
5
6

## Slide 13: mCBM read-out, data transport and processing Final version

## Slide 14: mDAQ and mFLES 2019 (SIS100 version)
present design
 |  | Device | Function | Location
1 | 70x | GBTx | data concentrator | Cave, on detector
2 | 6x | CRI | FPGA board (1x layer only) | DAQ container
3 | 2x | mFLES input node | Input stage | DAQ container
4 | 96x | Optical fibers | Data transport | DAQ → Green IT Cube
5 | 42x | mFLES compute nodes | Processing stage | Green IT Cube
1
2
3
4
5

## Slide 15: mRICH
d
3x2 MAPMT
module(s)
Aerogel radiator (few cm thick)
New proposal by the RICH group:
Aerogel proximity focusing RICH
to be installed for phase II / 2019,
≈ 0.5m2 acceptance,
need 50 – 70 cm space behind mTOF
open issues:
read-out
DiRICH & TRBnet to be included
into the mCBM DAQ
→ synergy with mPSD
detector integration
integration into mCBM

## Slide 16: mCBM benchmark observable: Λ reconstruction
Λ→pπ-
Feasibility study using mSTS & mTOF (3x stations):
straight track candidates mTOF → mSTS (hit station-0, hit station-1) assuming primary vertex on (0,0,0)
proton and pion candidate by selection on transverse distance to primary vertex
momenta from time-of-flight assuming proton and pion mass → p, Minv

## Slide 17: Next steps - simulations
ROOT geometry:
sis18_mcbm_20deg_long
Au+Au 1.24 AGeV
Ni+Ni
1.93 AGeV
go back to 25° ?
→ sis18_mcbm_25deg_long
re-run Au+Au & Ni+Ni simulations
reproduce results of the feasibility study
for Λ reconstruction (proposal) with
“standard” CBM tools

## Slide 18: mCBM benchmark observable: Λ reconstruction
S/B = 8.4
S/B = 0.24
Simulation input: 108 UrQMD events, min. bias
Efficiency
Au+Au 1.24AGeV
Ni+Ni 1.93AGeV
Acceptance

## Slide 19: Λ production at SIS18 energies – mCBM reference data
M. Merschmeyer et al. (FOPI), PRC 76, 024906 (2007)
midrapidity
Ni + Ni 1.93 AGeV
Au + Au 1.23 AGeV
H. Schuldes et al. (HADES)
EPJ Web of Conferences 171, 01001 (2018), SQM2017

## Slide 20: Physics of the benchmark observable
Λ - slope parameter:
smaller than proton
not explained by transport models
reason unclear:
  rescattering cross section ?
  repulsive potential ?
Data:
HADES : Eur. Phys. J. A (2011) 47
FOPI : PRC 76, 024906 (2007)
IQMD transport calculation:
C.Hartnack et al., PR 510 (2012)

## Slide 21: CBM data types - up to event selection
N = Detector systems & “sectors” within
M = Number of microslices per timeslice
O = Number of overlap microslices needed to avoid edge losses in reconstruction
Typical size: microslices ~ 10-1000 µs, timeslices ~ 0.1-10 ms
FEE
DPB
FLES Input
Computing farm