## Slide 1: 20 Years of HSI-RFQ-Operation / Recent RFQ-Electrode Exchange Program
H. Vormann, GSI Darmstadt
„High Intensity RFQ meets Reality“
-Workshop Heidelberg April 2019

## Slide 2
Introduction:
  RFQ basic design parameters
  Design history
Third revision planned for 2019
  Upgrade for FAIR
Problems encountered in 2018
  Short term counter measures
Outlook
Outline

## Slide 3
≈ 115 m
UNIversal Linear Accelerator UNILAC
 | HSI RFQ | UNILAC | 
ion A/q | ≤ 59.5 (i.e. 238U4+) | ≤ 8.5 (i.e. 238U28+) | 
beam current (pulse) *A/q | nom. 0.25 (0.5% d.c.) | 1.76 (0.5% d.c.) | emA
input beam energy | 2.2 | (2.2 / 120IH / 1400Alv) | keV/u
output beam energy | 0.120 | 3.0 - 11.4 | MeV/u
normalized total output emittance | 0.4 | 0.8 hor. / 2.5 ver. | mm mrad
beam pulse duration | ≤ 5 | ≤ 5 | ms
beam repetition rate | ≤ 50 | ≤ 50 | Hz
operating frequency | 36.136 | 36.136 / 108.408 | MHz
length | 9.25 | ≈ 115 | m

## Slide 4: 20 Years....
1996 – 1999 design, fabrication (INITIAL DESIGN)
1999 commissioning
2004 RFQ IRM re-design (1st RE-DESIGN)
2008/2009 RFQ complete part. dyn. re-design (for larger acceptance) (2nd RE-DESIGN)
... 2012... performance loss
2015 August 5th: sudden performance improvement...
2015 November RF expert investigations (plungers 20...24% best)
2016 October: RF expert tests, best performance ever!
2017/2018 re-commissioning reveals performance loss
2018 Planning RFQ part.-dyn. re-design (for smaller emittance) (3rd RE-DESIGN)
2019 User beam time with reduced performance

## Slide 5: Design History – Initial Design from 1999
initial design from 1999 :
15 emA U4+ RFQ output beam current
input emittance 138 mm mrad assumed (0.3 norm.)
output emittance ≈ 19 mm mrad (0.3 norm.)
max. surface field strength 32 MV/m (=320 kV/cm)
acceptance ≈ 250 mm mrad
HSI-RFQ, during assembly work 2009 (DSCF3014,3088,3110)

## Slide 6: Design History – Initial Design from 1999
in operation from May 1999 to May 2004
achieved performance: 8.3 emA U4+ @RFQ output
(design 15 emA), Ar output emittance 20/22 mm mrad
re-designed because of low transmission and sparking problems at high rf-levels
Photograph: W. Barth et al, proc. EPAC2006

## Slide 7: Design History – First Revision in 2004 Input Radial Matcher
Changes w.r.t. previous design:
input radial matcher: new geometry (slightly (larger apertures, smoother matching to the RFQ, smaller beam angles)
rods (massive copper) additionally galvanic copper plated
Photograph: W. Barth et al, proc. EPAC2006

## Slide 8: Design History – First Revision in 2004 Operational Experiences
in operation from July 2004 to April 2009
transmission increased by 15% (9.5 emA @ exit) (in good agreement with simulations)
transmission still not sufficient for FAIR: → second re-design
rods after beam operation 2004-2009

## Slide 9: Microscopy of RFQ electrode surfaces
See talk P. Gerhard,
Tuesday Morning
2004, Cu-plated, used
1999, used
2019, polished, not used,
2004/2009?,
Cu-plated,
not used
1999, not used

## Slide 10: Design History – Second Revision 2009 New Beam Dynamics Design
changes w.r.t. previous design:
complete particle dynamics re-design with larger acceptance – large aperture, higher voltages, higher rf-input power (surface fields not increased)
correction of output energy
 | design 1999 | design 2009
voltage, kV | 125 | 155
max. field, kV/cm | 318 | 312
norm. transv. accep., mm mrad | 0.73 | 0.86
max. modul., min. aperture/mm | m ≤ 2.09 ; ap ≥ 4.02 | m ≤ 1.93; ap ≥ 4.09
transv. acceptance, mm mrad | ≈ 330 to 46 (input to output) | ≈ 390 to 54 (input to output)
A. Kolomiets et al, proc. LINAC2008

## Slide 11: Design History – Second Revision 2009 Operational Experience
in operation since July 2009 (except shutdowns in 2013 and 2017)
achieved performance: up to 8 emA U4+, corrected output energy
higher voltage & power made rf-conditioning harder
2014: just 93% of design voltage reached
transmission still not sufficient for FAIR, subsequent IH-DTL suffers from large RFQ output emittance → third re-design
rods after 3 years of operation (in 2012)
HSI beam envelopes R. Tiede / IAP 05/2008

## Slide 12: Third Revision Planned for FAIR
Strategy: moderate acceptance and voltage, match to new MEBT and IH-DTL
Planned design change:
  reduce design voltage
    observed in 2014: just 93% of design voltage achieved
    voltage reduction solved SARAF RFQ problems!
  new beam dynamics design:
    use realistic input emittance (Uranium beam measurements at North Terminal 2013)
    include new quadrupole-quartet for matching to RFQ
    optimize output matching to new MEBT and IH-DTL

## Slide 13: Third Revision Planned for 2019
re-design provided by A. Lombardi et al. (CERN)
TDR approved May 2018
presented to MAC 19 (June 2018)
transv. output distrib., C. Xiao
 | Design 2009 | CERN Design for FAIR
Strategy | Increased acceptance | Moderate acceptance and voltage, match to new MEBT and IH-DTL
design ion | 238 U4+ | 238 U4+
design voltage | 155 kV | 123 kV
maximum surface field strength | 31.2 MV/m | 32 MV/m
average aperture r0 in a cell | 6.0 mm | 5.1 to 6.0 mm (excl. IRM) (average all cells: 5.32 mm)
minimum aperture in a cell | 4.1 mm (excl. IRM) | 5.1 to 3.4 mm (excl. IRM)
maximum modulation | 1.93 | 2.00
number of cells | 394 | 372
input transv. emittance (20 mA) | 200 mm mrad, 50 mm mrad rms (0.11 mm mrad, rms norm.) | 200 mm mrad, 50 mm mrad rms (0.11 mm mrad, rms norm.)
output transv. emittance (20 mA) | 31.7/29.9 mm mrad (95%, hor./vert.) | 31.2 mm mrad (95%), (0.5 mm mrad 95% norm.)
transmission (accelerated) | ≈ 80% | 78% (TOUTATIS)

## Slide 14: Problems encountered in June 2018
June 2018 after 1.5 years of shutdown, test run: just 73% of design voltage reached
P / kW
2018
2016

## Slide 15: Conditions before Re-Commissioning Impact on HSI Cavities
  Shutdown 2017 conditions:
    RFQ, super lens, and IH-1 were vented with nitrogen
    RFQ was kept under atmospheric pressure for 11 months
    SL and IH-1 were disassembled for 15 months
DSCF8602
DSCF8502
IH-1/ section 4 SL IH-1/ section 1-3
    Impact on HSI Cavities:
    super lens (being a short version of the RFQ) and IH-1 show no issues
    RFQ behaves normal up to about 45% of design voltage (Q and Rs as usual)
    RFQ beyond 45%: exponential growth of required input power and of reflected power

## Slide 16: Investigations
  ... shutdown 2017
    voltage limit imposed by reflected power, not by sparking or vacuum
    classical “conditioning behavior” not observed; situation did not change for two weeks
    several tank temperatures and tuner positions tested
    residual gas spectrum does not reveal masses > 44, i.e., no hydro-carbonites
    independent dust probe indicates no oil
    visual inspection w/o special findings
photograph P. Gerhard, (August 2018)
RFQ-Upgrade (2009)
photograph P. Gerhard, (August 2018)

## Slide 17: Investigations
  ... shutdown 2017
    rf-power amplifier, power lines, rf-coupler ok
    position sensitive X-ray measurements: foreseen for 17th April 2019
    NWA-measurements of higher modes
    several external experts consulted: S. Ramberger, P. Chiggiato, S. Calatroni, W. Vinzenz, U. Ratzinger, M. Vretenar, ...
rf power line from RFQ transmitter to IH-1 cavity
NWA measurements of higher modes

## Slide 18: 2012...
Chart: Tank Voltage [V]
| 6.75 | 6.85 | 6.95 | 7.05 | 7.15 | 7.25 | 7.35 | 7.45 | 7.55 | 7.65 | 7.75 | 7.85
Fwd new | 450 | 475 | 505 | 555 | 610 | 670 | 730 | 810 | 900 | 1010 | 1120 | 1250
Rfl new | 16 | 18 | 21 | 25 | 30 | 38 | 49 | 67 | 88 | 117 | 152 | 200
Fwd 3 weeks | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200
Rfl 3 weeks | 2 | 3 | 4 | 7 | 14 | 23 | 36 | 54 | 73 | 95 | 119 | 145
Fwd 9 weeks | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400
Rfl 9 weeks | 1 | 2 | 3 | 4 | 8 | 15 | 27 | 42 | 62 | 80 | 105 | 132 | 158 | 184
Fwd 1 year | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400
Rfl 1 year | 25 | 38 | 54 | 73 | 96 | 120 | 148 | 177

## Slide 19: Third revision planned for FAIR suspended due to 2018 Problems
Most likely cause: after 9 years, rods exceeded lifetime
Short term solution, for beamtime 2020: re-production of rods with existing design (2009)
  decision to just re-produce rods (2009 design) instead of improved but not tested new design (CERN)
  → installation of new design suspended to minimize risks for operation in 2019/20
  fabrication of 2009 design rods finished in February 2019
  completion of electrode „baskets“ (with carrierr rings) finished 9th April 2019
Mid term: preparation to implement CERN design (FAIR)

## Slide 20: Outlook Mid Term Solution: FAIR Performance Gain
follow up the original strategy (CERN design)
postponed to 2020
material for rods and carrier rings ordered

## Slide 21: Summary
after two revisions the HSI RFQ has still not reached the required beam current performance --- a third revision is planned to meet FAIR
although design is completed, this third revision has been suspended due to latest cavity voltage performance losses
cause for performance loss is still not understood; most likely lifetime of rods is exceeded
user beam time Q1/2019 with limited amplitudes successsful
to cure the cavity performance loss, new electrodes are produced, applying the 2009 design
they will be mounted immediately after the beam time (ending 2019-04-16, 06:00 h)
additionally, new rods will be produced applying the CERN design for FAIR

## Slide 23: Conditioning 2009 - 2015
Notes from 2015...
5.8.15:
sxxx und vxxx in kantine: HSI-RFQ jetzt 7.9 V bei 450kW/20kWrück, faktor 2 besser als die beste kurve, Vacc14 mit 2.5Hz, während Au8+ mit 3.4V bei 50Hz und 3.2ms.
10.8.15:
HSI RFQ 8.0 V 500 kW 20 kW
12.8.15:
HSI-RFQ: Wenn der Warmhalter mit 6.42 Volt und 50 Hz mitläuft (ca. 1 ms HF), dann wirds dem tank wärmer, TK20%, und er braucht für die hohen vacc14 (8 V) mehr leistung (>500kW). Hxxx macht noch bis freitag tests, anweisung in mittagssitzung geschrieben.
7.10.15:
hsi rfq 7,60 V 600 kW 17Uhr
13.10.15:
HSI-RFQ 8,22 V bei 700 kW Vorlauf.
14.10.15:
HSI RFQ den U06er von 7.5V 2.5Hz auf 3.0 V 48 Hz 3ms Strahl (knapp 4 ms HF) geändert, so fällt der U15er (4.0 V) raus , Pxxx ändert frequenzregelung TK, schließlich TKs bei 15%, vorher bei 5%. U14 nun bei 8.21V 2 Hz nun 730 kW und 19 kW Rück.

## Slide 24: 2010...
Chart: Tank Voltage [V]
| 6.75 | 6.85 | 6.95 | 7.05 | 7.15 | 7.25 | 7.35 | 7.45 | 7.55 | 7.65 | 7.75 | 7.85
Fwd new | 450 | 475 | 505 | 555 | 610 | 670 | 730 | 810 | 900 | 1010 | 1120 | 1250
Rfl new | 16 | 18 | 21 | 25 | 30 | 38 | 49 | 67 | 88 | 117 | 152 | 200
Fwd 3 weeks | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200
Rfl 3 weeks | 2 | 3 | 4 | 7 | 14 | 23 | 36 | 54 | 73 | 95 | 119 | 145
Fwd 9 weeks | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400
Rfl 9 weeks | 1 | 2 | 3 | 4 | 8 | 15 | 27 | 42 | 62 | 80 | 105 | 132 | 158 | 184
Fwd 1 year | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400
Rfl 1 year | 25 | 38 | 54 | 73 | 96 | 120 | 148 | 177

## Slide 25: Impact on Beamtime 2018/2019
  limits deliverable A/q to 43.7;
  for intense uranium A/q = 59.5 is needed
  imposes considerable intensity limitations to all heavy ions
ion | mass | q_min | q_best | I_SIS18(q_best) [eµA] | I(q_min) / I(q_best) | I_SIS18(q_min) [eµA] | q(SIS18)
Pb | 208 | 5 | 4 | 411 | 0,01 | 4,11 | 65
Au | 197 | 5 | 4 | 262 | 1,00 | 262 | 25
Ag | 107 | 3 | 2 | 440 | 0,50 | 220 | 43
U | 238 | 6 | 4 | 2000 | 0,00 | 0 | 0
Fe | 56 | 2 | 1 | 44,7 | 1,00 | 44,7 | 25

## Slide 26: Outlook Mid Term Solution: FAIR Performance Gain
follow up the original strategy (CERN design)
postponed to 2020
material for rods and carrier rings ordered
test piece,
pre-milled pieces,
older example,
new milled rod.

## Slide 27: Work Package Description High Current RFQ / UNILAC
Scope
  Design, production, installation, and commissioning of the re-designed RFQ rods to meet FAIR requirements
System function
  First accelerating section of the heavy ion injector linac for FAIR
System requirements
  Ion energy 2.2 keV/u
  Maximum design current 0.34 mA* A/q (20 emA U4+)