## Slide 1
Very High Frequency Accelerators:
THz and IR
Nicholas H. Matlis
Center for Free-Electron Laser Science, DESY, Hamburg, Germany
Ultrafast Optics and X-Rays Group
KfB Strategie Workshop – September 5 - 6, 2019

## Slide 2
Technology | Wavelength | timing for 0.1% | Fabrication | bunch charge
Conventional | ~ 100 mm | ~ 300 fs | machining | ~ nC
THz-based | ~ 1 mm | ~ 3 fs | machining | ~ pC
Laser-plasma | ~ 0.01 mm | ~ 0.03 fs | wave excitation | ~ pC
Dielectric laser | ~ 0.001 mm | ~ 0.0003 fs | lithographic | ~ fC
Distance & Time scaling in High-Gradient Accelerators
All-optical approach ➞ intrinsic synchronization ➞ important for small scales
Gun
LINAC ~ km
Conventional Approach
E. Nanni et al., Nat. Comm. 6, 8486 (2015)
D. Zhang et al., Nature Photonics (2018)
Gun
LINAC
THz-Driven Approach
Direct Laser-Driven Approach

## Slide 3: Why explore higher frequencies?
Higher driving frequency allows:
higher acceleration fields: ➞ reduced accelerator size
lower pulse energy for same E-field in the cavity:
reduced pulsed heating: ➞ higher rep rates!
higher field gradients:
  stronger compression: ➞ shorter bunches
  quicker acceleration to relativistic energies ➞ reduce space charge effects
[1] Kilpatrick, W. D., Rev. Sci. Inst. 28, 824 (1957).
[2] Loew, G.A., et al., 13th Int. Symp. on Discharges and Electr. Insulation in Vacuum, Paris, France. 1988. [3] S. V. Dolgashev, et al. Appl. Phys. Lett. 97, 171501 2010.
[4] M. D. Forno, et al. PRAB. 19, 011301 (2016).
Reduced duration = larger field =
Notes: Smaller size, lower energy make accelerator more accessible
Reduced heating & higher rep-rate can compensate for lower charge
Higher gradients can lead to shorter bunches
don’t always want highest gradients
want to reach full compression when emittance is frozen: compression must occur with acceleration
grygorii: best emittance happens with lowest frequencies
true for sinusoidal drivers (with alternate waveforms, may not be true)
Rephrase: higher fields allows reaching relativistic energies sooner -> mitigates space charge effects

## Slide 4: Benefits of Compact Accelerators: Study scaling to shorter wavelength drivers
  lower energy required
    less heating
    smaller drivers -> more available
    higher repetition rates
  more compact
    more accessible
    less costly infrastructure
    allows accelerators to be brought to the problem instead of the problem to the accelerator
    allows diversification of accelerator science in general into new areas
  materials have different responses
    scaling of breakdown with driver duration & frequency
    use of new materials like dielectrics which can support much higher fields
  different manufacturing techniques can be used
    micromachining
    lithography
  shorter field scale lengths -> higher field gradients
    higher resolution streaking
    higher resolution beam manipulation
    stronger forcing on electron bunches
  new applications
    basic science
    conventional accelerator add-ons
  Use of laser drivers
    high field strengths
    inherent synchronization
  Development of new technologies
    New lasers
    high-power THz generation
    electrons on a chip
    compact UED
    compact X-ray light sources

## Slide 5: Attosecond X-ray Science – Imaging and Spec. (AXSIS)
FXK. et al., doi:10.1016/j.nima.2016.02.080
Undisturbed electronic structure
Damage-free structure
IR
or
Optical
Undulator
Laser driver
has its own science case
seeding of large scale FELs
 solve access to large facilities
20 mJ multicycle THz
1 mJ single-cycle THz
1 MeV THz Gun
20 MeV THz LINAC
5 keV X-ray source
THz-MeV UED source
Next Steps
2016 1st THz gun (1 keV)
1st THz acceleration (7 keV) 2015
kHz Joule laser 2018
AXSIS laboratory 2019
2018 0.6 mJ multicycle THz
Energy gain [keV]
0
0.2
0.4
0.6
0.8
Yield [a.u.]
65 keV
2008 1st THz practical device (65 keV)
2013 AXSIS project
0.2 mJ single-cycle THz 2017
structured photocathodes 2007
2019 multicycle staged acceleration
Previous Steps

## Slide 6: THz device Breakthrough: STEAM / Gun Devices
D. Zhang, et al. Nat. Photonics 12, 336 (2018)
65 keV
D. Zhang et al., Optica accepted
Electron acceleration & deflection

## Slide 7: STEAM Device manipulates electrons with high-gradient THz fields
focusing field
0.0 T
0.3 T
0.6 T
Beam Size
STEAM
focusing
0
2
-2
-4
4
Deflection (mrad)
Unstreaked
Streaked beam
Beam Spatial Mode
beam
STEAM
streaking
Delay(ps)
Retrieved temporal profile
Streaking gradient: 140 µrad/fs
Resolution: sub-10 fs
STEAM
compression
STEAM
compressor
STEAM
streaker
200 mm
From
DC gun
Compression
100 nJ
100 nJ
2 x 100 nJ
Notes: Velocity bunching
Terahertz-driven electron pulse focusing/defocusing. (A) and (B) The spatial profile of the electrons as a function of THz field at the relative focusing and defocusing phase respectively. (E) and (H) Initial 55 keV electron beam on the detector. (C) and (D) focusing and defocusing field spatial distribution . (E-G) and (H-J) are focused and defocused electron beam on the detector, respectively.
Terahertz-driven electron pulse compression. (A). Measured temporal profiles of the electron pulses as the THz field is increased (red arrow). (B) Measured electron pulse duration (FWHM) versus incident THz field strength (Black dots). The simulation is shown as red dotted line. (Inset) the electron beam spatial profile on the detector at the optimal compressed condition. (C) Simulated bunch length vs position. Inset: longitudinal phase space distribution (D) before the rebunching cavity, (E) after the rebunching cavity and (F) maximally compressed position marked with red dots respectively. This demonstration was performed in the low energy Yb:KYW laser system with three THz setups that generated ~2*0.1 µJ THz for rebunching and ~2 µJ THz for streaking.

## Slide 8
THz IFEL interaction @ Pegasus lab
Undulator Magnets
CPPWG
Walsh et al., Nature Comm. 8, 421 (2017)
THz sub-luminal free-space fields @ ASTeC in Daresbury
Kealhofer et al., Science 359, 459 (2016)
THz Compression @ LMU/MPQ
Phase-space control & characterization of electron pulses
12x compression from 930 to 75 fs
Avg 1 electron @ 70 keV per pulse
Beam Manipulation using 1μJ single-cycle 0.8 THz pulse:
150 keV energy modulation of 7 MeV beam using
Bunch compression by factor of two
Curry et al., New J. Phys. 18, 113045 (2016)
THz based electron manipulation takes up speed
Generation of sub-luminal propagating THz fields in free space
Tunable
Applicable for THz-based acceleration

## Slide 9
https://achip.stanford.edu/
Accelerator on a Chip (ACHIP)
ACHIP Collaboration
ACHIP Concept
Leverage Semiconductor Tech

## Slide 10: Research in ACHIP & Dielectric Laser Accelerators
2-sided pumping using a distributed Bragg reflector (dE/dz = 133 MeV/m, E0 = 28 keV, dE = 0.69 keV)
P. Yousefi et al, Opt. Lett. v44, p1520
2013
1st dielectric laser acceleration (250 MeV/m, E0 = 60 MeV, dE = 53 keV, E_opt = 92 uJ)
E.A. Peralta et al., Nature v503, p91
2015
acceleration of sub-relativistic electrons (dE/dz = 200 MV/m, E0 = 96 keV, dE = 1 keV)
K. Leedle et al., Optica v2, p158
2016
acceleration using fs pulses (dE/dz = 690 MV/m, dE = 29 keV)
K.P. Wootton et al., Opt. Lett. v41, p2696
2019

## Slide 11: ACHIP & DLA Development at TU Darmstadt
Accelerating structure
bunching
Alignment
Coupling of laser to structure
Development of structures for acceleration and control of electron properties

## Slide 12
END