## Slide 1
Status and Performance of the CBM Time-of-Flight system
Ingo Deppner1 and Norbert Herrmann1 for the CBM-Collaboration
1 Physikalisches Institut Uni Heidelberg, Heidelberg, Germany
Compressed Baryonic Matter experiment at FAIR
Exploring the QCD phase diagram at large baryon densities
Charged hadron PID for HI-collisions at kinetic beam energies Tbeam = 2 – 11 AGeV (for the heaviest system)
High granularity and rate capability for interaction rate R  10 MHz
Multi-gap Resistive Plate Chamber (MRPC) system with about 120000 timing channels and a system time resolution of   80 ps
Usage in STAR BESII campaign as part of the FAIR phase 0 program as eTOF system with acceptance range 1.0    1.5
MRPC1
MRPC2
MRPC3a
MRPC3b
MRPC4
CBM-ToF Requirements
Full system time resolution T ~ 80 ps
Efficiency > 95 %
Rate capability  30 kHz/cm2
Polar angular range 2.5° – 25°
Active area of 120 m2
Occupancy < 5 %
Low power electronics
(~120.000 channels)
Free streaming data acquisition
Anticipated rate
Phase space distribution
Summary: The CBM Time-of-Flight system is developed by 8 institutions from China, Germany, Romania and Russia. It comprises about 120000 channels and a rate capability up to 30 kHz/cm2. The targeted system time resolution is 80 ps at an efficiency above 95%. Test beam experiments have demonstrated counter resolutions in the order of 50 ps. CBM-TOF will participate as part of the FAIR phase 0 program in the BESII campaign of STAR@RHIC and miniCBM@GSI. The CBM-TOF wall will be ready to take beam at FAIR in 2024.
High net-baryon densities
The Compressed Baryonic Matter (CBM) experiment
The CBM Time-of-Flight wall
Electronic readout chain
Counter properties
Active area 300 – 864 cm2
Granularities 10 – 27 cm2
Low resistive glass
Rate capability > 30 kHz/cm2
Time resolution about 50 ps
Efficiencies above 95 %
Cluster size about 1.4 - 2
CBM MRPC prototypes and test performance
MRPC1/2
Cosmic stand setup
FAIR phase 0 program: eTOF at STAR/BNL
13
14
15
16
17
18
19
20
21
22
23
24
3 layers 12 sectors 36 modules
108 MRPCs 6912 channels
CBM “STAR” module
Installation of Sector 18 in Jan. 2018
Sector counting match the TPC sectors
Full installation in Nov. 2018
eTOF – barrel TOF correlation
MRPC3a/b
CBM TOF module M4_001
Upper setup
Lower setup
Beam
 = 3.5
 = 6
CERN SPS setup
TRD
TOF
ECAL
RICH
Dipole magnet
PSD
MVD & STS
MUCH
21
FAIR phase 0 program: mTOF at mCBM/GSI
Magnet pole tip on east side
mCBM@SIS18
mSTS
mMUCH
mTRD
mTOF
mTOF
Full eTOF wheel is currently in the commissioning phase
1st PID plot
TPC track matching
Event display of an Ag + Au event
1st “commissioning” beam-time in Dec. 18
Tracking acceptance: 2 < Lab < 25
Free streaming DAQ
Software based event selection
Rint = 10 MHz (Au + Au)
MRPC hit rate
Target: Au 10%
Diamond T0
3 mTOF modules with 5 MRPC3a each
Beam: Ag (42+) @ 0.95AGeV
MRPC3a (5 counters)
Active area 864 cm2
Dark rate 1 – 2 Hz/cm2
Flux up to 1 kHz/cm2
3 tracks