## Slide 1: Collaboration CERN – GSI/FAIR superconducting magnets
C. Roux for
Department of Superconducting Magnets
GSI Darmstadt, 02.07.2019

## Slide 2: overview
TITLE/SCOPE | Machine | Status | Addendum | Date
Magnetic-field measurement systems for the SIS100 superconducting dipoles | SIS100 | active | Annex to #2 #9, KR2984/TE | 2014 2016
Cryogenic testing of the superconducting magnets for the Super-FRS | Super-FRS | active | #2 #4 #5 #12, KR3912 | 2012 2014 2016 2018
CERN-GSI/FAIR collaborations: superconducting magnets
all collaborations in the framework of the 2010 agreement K1727/DG
Simulation of transient effects in the SIS100 main busbar system | SIS100 | in preparation
Superconducting high-field septa | Future accelerators | proposed

## Slide 3: SIS100: magnetic-field measurement system (dipoles)
purpose
Add. | GSI |  |  | CERN | 
#2 | Development of rotating feedthrough |  |  | Loan of measurement system | 
#9 | Design of the shaft Layout of the patch panel Procurement of MRUs mechanical components tooling Costs up to 55.000 CHF for personnel (calibration) up to 143.000 CHF for material (integrators, racks, …) | open |  | Expertise in coil design Drawing of coils and MRUs Procurement of integrators cabinets for controllers Winding and calibration of the coils Assembly of the segments | 15 segments delivered 10 expected in 09.2019
design and procurement of a magnetic field measurement system for the SIS100 series dipoles:
five shafts to be operated at 4 K in vacuum (first time), based on CERN design of tangential coils
contribution
K1727/DG (2010), Annex to addendum #2, Addendum #9: active collaboration
compensation of effort: three MRUs delivered to CERN in 2017
Responsible: S. Russenschuck | A. Szwangruber
five segments of rotating coils within dipole
MRU

## Slide 4: SIS100: magnetic-field measurement system (dipoles)
status: active, close to completion
three shafts at full operation at the series test facility for the SIS100 superconducting dipoles performing SAT.
at STF/GSI:
SAT results: magnetic-field properties
ΔBL/BL = 4.1 ×10-4
Excellent measurement system reveals excellent magnet properties
proof of principle for operation at cold + vacuum
K1727/DG (2010), Annex to addendum #2, Addendum #9: active collaboration
Responsible: S. Russenschuck | A. Szwangruber

## Slide 5: Super-FRS: testing of sc. magnets
K1727/DG (2010); Addendum #2 (2012), #4 (2014), #5 (2016) for infrastructure refurbishment + #12 (2018) for testing phase: active
purpose
Add. | GSI |  |  | CERN | 
#2 | 5.000.000 € |  |  | Refurbishment of test facility B180 | 
#4 | 1.860.000 CHF |  |  | Procurement of pre-cooler, QD-system, survey tooling | 
#5 | 210.000 CHF |  |  | Integration work, modification of cryo lines Implementation of preparation test bench and control room | 
#12 | Testing of the magnets 4 FTEs Further personnel if required Experts of survey at pre-series testing Cost-recovery for operational services | ongoing tbd ongoing ongoing |  | 1 FTE: test engineer to oversee functioning of test facility 0.4 FTE: support of equipment groups on best-effort basis Energy costs (no cryogenics) Office space and infrastructure | See kick-off See kick-off ongoing
testing of all superconducting magnets for the Super-FRS depicting the SAT for acceptance.
refurbishment and adaption of the cryogenic test facility at B180/CERN.
contribution
facility will be made available for similar testing after Super-FRS activities
32 multipletts
24 dipoles
Responsible: L. Van den Boogard/S. Russenschuck | K. Sugita

## Slide 6: Super-FRS: testing of sc. magnets
K1727/DG (2010); Addendum #2 (2012), #4 (2014), #5 (2016) for infrastructure refurbishment + #12 (2018) for testing phase: active
B180 refurbished and operational
Measurement systems available
GSI contributions on campus
status: test facility
test facility at B180:
infrastructure and measurement systems ready
for full commissioning/testing phase
32 multipletts
24 dipoles
Responsible: L. Van den Boogard/S. Russenschuck | K. Sugita

## Slide 7: Super-FRS: testing of sc. magnets
K1727/DG (2010); Addendum #2 (2012), #4 (2014), #5 (2016) for infrastructure refurbishment + #12 (2018) for testing phase: active
status: testing
first multiplett delivered
pre-series testing started
commissioning of the test facility (simultaneously)
FIRST cool down planned in week 27
Kick-off meeting at 03.07-04.07: organisation/personnel
delivery of pre-series multilplett
at test bench
testing phase in progress
(1.5 y for pre-series, 4 y for series magnets)
32 multipletts
24 dipoles
Responsible: L. Van den Boogard/S. Russenschuck | K. Sugita

## Slide 8: SIS100: transient effects in the main busbar system
purpose/benefit
Add. | GSI |  | CERN
#x | Input data of components and operation (magnet circuits, power converter, QD system, cycling details, 3D models) Delegation of GSI staff member (PhD student) Personell costs for CERN experts supervision first year: 0.35 FTE afterwards: 0.1 FTE |  | Simulation strategy and STEAM code Manpower for supervision and code adaption Guide and training of PhD student Cross-check of simulation results
simulation of transient effects in the SIS100 sc. magnet system with CERN software tools:
Reveal dynamical electrical behaviour at operation of complex cryomagnetic system.
contribution
in preparation: contract ready for signature (soon)
assumed effort: 3 years
fast power abort in LHC dipole
courtesy of CERN
dynamical and collective behaviour of SIS100 cryomagnets
use of STEAM in non-CERN application: valuable feedback
Responsible: A. Verwej | P. Szwangruber

## Slide 9: high-field superconducting septa: magnet development
purpose/benefit
Add. | GSI |  | CERN
#x | septa concept |  | Consine-theta expertise (Rutherford cable)
 | Design studies: electromagnetic, cryogenic, mechanical R&D of critical parts Prototyping and testing |  | 
conventional iron-dominated septa are limited to 2 T field strength. At GSI a cosine-theta septa magnet concept was developed enabling much higher field strength.
superconducting cosine-theta septa might be used at future accelerators (e.g. FCC, medical, …). For feasibility studies the concept must be transferred to an engineering design.
contribution
proposed
septa magnetic field
cosine-theta type coil
high interest from both sides (application in future projects)
benefit from complementary expertise
Responsible: J. Borburgh | K. Sugita

## Slide 10: Collaboration CERN-GSI/FAIR superconducting magnets
thank you

## Slide 11
bonus slides

## Slide 12: magnetic field measurements
System for magnetic field measurements
5 measuring heads – tangential coils
3 pick up coils per head, 600 mm length
effective surface 1.67 m2
Ti-alloy bellows – interconnection between segments and to align the heads along the beam axis
SiN ball bearings for rotation motion
ceramic supporting blocks for transverse positioning in the gap
Field measurements in vacuum @ 4.5K
measuring head
supporting block
620 mm
SiN ball bearing
Ti bellow
53.26 ±0.04
63.26
3600 mm
cross section of the measuring head (3 tangentinal coils)
rotated ferro fluidic feed througth
motor unit
24.18 -0.05
The measuring probe is designed and built in collaboration with CERN

## Slide 13: SIS100: magnetic-field measurement system (dipoles)
purpose
GSI | CERN
Design of the shaft Layout of the patch panel Procurement of MRUs mechanical components tooling Costs up to 55.000 CHF for personnel (calibration) up to 143.000 CHF for material (integrators, racks, …) | Expertise in coil design Drawing of Coils and MRUs Procurement of Integrators Cabinets for controllers Winding and calibration of the Coils Assebly and calibration of the segments
design and procurement of a magnetic field measurement system for the SIS100 series dipoles:
five shafts to be operated at 4 K, based on CERN design of tangential coils
status
GSI:
6 MRU‘s were produced at GSI during 2015 -2017
3 MRU‘s delivered to CERN in 2017
mechanical design of the measuring probe finalised in Q2/2017
all mechanical components for 5 measuring probes (5 shafts build up of 5 segments each) are procured and delivered to CERN
CERN:
3 electronic cabinets for control of the measuring system and DAQ delivered to GSI in 2017
fabrication of all coils (winding, calibration, sorting) is finished
15 out of 25 segments delivered ( 2017, 2018, 2019)
remaining 10 segments are under assembly and calibration. Expected delivery Sept. 2019
contribution
K1727/DG (2010), Addendum #9 + Annex to addendum #2
compensation of CERN’s effort: three MRUs

## Slide 14: SIS100: magnetic-field measurement system (dipoles)
2
1 – shaft of 5 rotating coils
2 – motor unit (MRU) for MFMS
3 – electronic cabinet for MFMS
4 – calibration magnet
5 – series dipole magnet for SIS100
1
5
5
1
2
3
4
series dipole magnet with installed MFMS at the test bench
installation of the shaft into the series dipole magnet
K1727/DG (2010), Addendum #9 + Annex to addendum #2

## Slide 16: Transient Effects in the SIS100 Main Bus Bar System
CERN simulation tools: Simulation of Transient Effects in Accelerator Magnets (STEAM)
Example of a fast power abort in LHC dipole circuit @ 10kA, 10A/s
Simulation
Measurements
courtesy of CERN
Simulations:
Electrical (netlist based)
Mechanical
Magnetic
Thermal
Quench

## Slide 17: SIS100: magnetic-field measurement system (dipoles)
purpose
design and procurement of a magnetic field measurement system for the SIS100 series dipoles:
five shafts to be operated at 4 K, based on CERN design of tangential coils
K1727/DG (2010), Annex to addendum #2, Addendum #9
SiN ball bearings
Ti bellows
SIS100 dipole with magnetic field measurement system
rotated ferro fluidic
feed througth
motor rotating
unit (MRU)
53.26 ±0.04
~ 3 m
600 mm
interconnections
measuring head with tangential coils
refurbishment and adaption of the cryogenic test facility at B180/CERN (add. #2, #4, #5).
refurbishment and adaption of the cryogenic test facility at B180/CERN (add. #2, #4, #5).

## Slide 18
Stray field / Main field
(Preliminary optimisation)
Iron yoke
Iron yoke
Conventional septum magnet
< 2T
SIS100
septum magnet
High field septum magnet with truncated cosine-theta concept

## Slide 19
Collaboration Meeting CERN - GSI/SCM | C. Roux for SCM
Medical machine
Heidelberg, Germany
Normal conducting gantry
600 ton
NIRS, Japan
Superconducting gantry
1st generation
  300 ton
2nd generation
  compact and light weight
Shorter straight section in the ring (injection, extraction) is important for further compact medical facility.
Therefore high field sc septum magnet is a key technology for further developments.
1st generation
2nd generation