## Slide 1: System Integration Issues with the Silicon Tracker of the CBM Experiment at FAIR
Johann M. Heuser GSI Helmholtz Center for Heavy Ion Research, Darmstadt, Germany for the CBM Collaboration
Forum on Tracking Detector Mechanics 2019, Cornell University, Ithaca NY, USA
CBM experiment at FAIR
Silicon Tracking System
Integration: status and issues

## Slide 2: Compressed Baryonic Matter
The phase diagram of strongly interacting matter
 focus on high-density matter:
Compressed Baryonic Matter
Au + Au collision
in the laboratory: nucleus-nucleus collisions
8 ρ0
model predictions, 10 GeV/u
cartoon
FAIR: the proper energy regime !
temperature T < 120 MeV density ρ > 8 ρ0 reaction time t ~ 10-23 s

## Slide 3: Compressed Baryonic Matter
high
net-baryon densities
Multiplicity × branching ratio
Particle yields in central Au+Au 4 A GeV
not measured with large statistics at high baryonic densities
rare probes:  high interaction rates

## Slide 4: Facility for Antiproton and Ion Research
new international research laboratory to explore the nature and evolution of matter in the Universe
under construction, Darmstadt, Germany
Helmholtz Center for Heavy Ion Research
current completion date, first beams: 2025
CBM beams at SIS100:
ions: 109/s, 2-14 GeV/u, sNN= 1.9 - 4.5 GeV
protons: 1011/s up to 29 GeV
  target: typically 1% I
100 m
CBM
(Compressed Baryonic Matter
experiment)
p-Linac
SIS18
SIS100/300
FAIR phase 1
FAIR phase 2

## Slide 5: Facility for Antiproton and Ion Research
https://fair-center.eu/

## Slide 6: Facility for Antiproton and Ion Research
https://fair-center.eu/

## Slide 7: Facility for Antiproton and Ion Research
https://fair-center.eu/

## Slide 8: Compressed Baryonic Matter Experiment
CBM cave + building

## Slide 9: Compressed Baryonic Matter Experiment
Beam
Dipole Magnet
RICH
Ring Imaging Cherenkov
TRD
Transition Radiation Detector
TOF
Resistive Plate Chambers
MVD
Micro Vertex Detector
STS
Silicon Tracking System
MUCH
Muon Detection System (parking pos.)
ECAL
Electro- Magnetic Calorimeter
PSD
Projectile Spectator Detector
Tracking acceptance:
Free streaming DAQ
Rint = 10 MHz (Au+Au)
with
Rint (MVD) = 0.1 MHz
Software based event selection
Target

## Slide 10: mCBM test experiment
mCBM@SIS18 - a CBM full system test-setup
for high-rate nucleus-nucleus collisions at GSI/FAIR
CBM prototype detector systems
free-streaming read-out and data transport to the mFLES
online event reconstruction and selection
up to 10 MHz collision rate
first successful commissioning with beam 12/2018 and 3/2019
mRICH
mTOF
mTRD
mMUCH
mSTS
T0
diamond

## Slide 11: mCBM test experiment
March 30, 2019 – run 175
(approx.) 108 Ag ions/s (1.58 GeV/u) + Au (2.5mm)
T0
March 30, 2019:
beam intensity ≈ 108 Ag ions / s
interaction rates 106 … 107 /s (preliminary)
x 106
T0 rate (Hz)
preliminary

## Slide 12: Silicon Tracking System
Approach:
8 tracking stations, 0.3 – 1.0 m downstream target
   4 m2 area,  3.5 m3 volume, 896 modules, 106 ladders, 1.8 M channels
double-sided silicon microstrip sensors
  hit spatial resolution  25 µm
  life time rad. tol. up to 1014 n/cm2 (1 MeV eq.)
  operation at T < -10C
self-triggering electronics
  time-stamp resolution  5 ns
  radiation tolerance > 30 Mrad
  power dissipation ~ 40 kW
low-mass detector modules/ladders:
  electronics/cooling outside physics aperture
  material budget per station:  0.3% – 2% X0
Central CBM detector: charged-particle tracking + momentum measurement
Requirements/challenges:
up to ~ 700 charged particles per heavy-ion collision  high granularity
105  107 heavy-ion collisions per second  radiation tolerant
pile-up free streaming of hit data to online computing  fast electronics
mechanical precision: transversal to beam  100 µm, less along beam

## Slide 13: Silicon Tracking System
field integral 1 Tm
field profile along beam
superconducting dipole magnet
distance from pole shoe center [mm]
distance from pole shoe center [mm]
[T]
[T]
144 cm

## Slide 14: Silicon Tracking System
central collision, Au-Au, 10 GeV/u
700 charged particles in aperture
track reconstruct. efficiency: > 96 %
momentum resolution: ~ 2%
momentum resolution
track reconstruction efficiency

## Slide 15: STS – composition
(18 variants)
(23 variants)

## Slide 16: System engineering
Global system aspects:
STS services, rail supports and details of
  Cabling, patch panels
  Cooling
  Positioning
  Safety / emergency systems
  Integration upstream and downstream
  vibrations / structural analysis
Thermal enclosure:
Sealing
Panel connections
Material budget rear panel
Overall stiffness
Service / support mechanics
Overall assembly procedure
Mechanical frames:
Material
Rail system
Positioning / adjustment
Cooling plate shape
Sensor cooling
Cabling
Consistent design being detailed. Current issues:
details on construction in: O. Vasylyev, FTDM 2017

## Slide 17: System engineering
full-scale mechanics demonstrator to be set-up

## Slide 18: System engineering
cooling concept:
liquid distribution for electronics cooling
gas flow for sensor cooling
thermal demonstrator under set-up
details in:
K. Agarwar, FTDM 2019

## Slide 19: System engineering
cooling concept:
liquid distribution for electronics cooling
gas flow for sensor cooling
thermal demonstrator under set-up
details in:
K. Agarwal, FTDM 2019

## Slide 20: Beam pipe
0.5 mm carbon fiber prepreg on a hub, foil embedded
window to target vacuum
pipe
first prototype made in industry
vacuum stability test failed
collapse in transition area to conical part
new trial pending
thicker carbon fiber layer for pipe: 0.8 mm

## Slide 21: Module assembly
double-sided microstrip sensors
1024 strips of 58 µm pitch
320 µm thick
4 variants/strip lengths
STS-XYTER v2.1
128 channels
self-triggering
5 bit ADC, time resolution < 5 ns
Front-end electronics board FEB-8
signal layer: 64 Al lines of 116 µm pitch, 30 µm wide, 14 µm thick on 10 µm polyimide
trace lengths 5 - 55 cm
trace capacitance 0.45 pF/cm
cable stack: with shielding, spacers thickness ~ 800 µm / 0.23% X0
TAB bonding
(Al width 45 µm) *)
*) alternative Cu cable/interconnect technology under study

## Slide 22: Module assembly
longest module variant for mSTS

## Slide 23: Ladder assembly
longest ladder, 970mm
shortest ladder, 480mm
FEE box, microcable routing, sensor attachment
transition-fits: pin to C-frame, pin to bearing
carbon fiber supports

## Slide 24: Ladder assembly
module #0 installed on ladder;
module #1 on transfer tool
application of glue onto L-legs
transfer of module #1 to ladder
module #1 transferred, fixed during curing of glue
half-ladder #0 for mSTS demonstrator
carbon fiber ladder with bearings

## Slide 25: Carbon fiber ladders
carbon tube, 1.5/0.7mm 
carbon fiber, Tenax, HTA40 E13, 3K, 200tex, three rovings, twisted
EP resin
winding core (prototype – Al, final – steel)
prototypes produced in company
length 120 cm, weight 14.8 g
derived from ALICE-ITS for production in a company

## Slide 26: Optical metrology
conceived for silicon microstrip QA,
adapted to ladder metrology:
mSTS mechanical dummy half-ladder
demonstration of assembly technique
sensor warp and other effects
module placement achieved within target ± 200 µm (z), 100 µm rms (xy)
fiducial marks on sensors
fiducial mark survey
focus: surface height
edge detection
10 µm position resolution

## Slide 27: Survey of carbon fiber ladders
ladder shapes – 16 prototypes
ladder sag under load
vibrational analysis ?
quality uniform, slightly larger tolerances needed – longer L-legs
300 µm*
* at simultaneous load; with module mounting
starting from center of ladder: expect  100 µm
enlargement

## Slide 28: Central ladders
Concepts of modification to the carbon fiber ladders for the beam pipe intersection:
Hollow carbon fiber cone added to a ladder (ALICE-ITS style frame).
Turned out presenting too much material in CBM-STS geometrical arrangement.
Low-mass ribs in the cut-out. To be prototyped.

## Slide 29: mSTS demonstrator
station #0: C-frames #0 and #1
station #0 area 12 x 12 cm2
mSTS – demonstration of:
C-frame and ladder mounting mechanics
module and ladder assembly
LV + HV powering
liquid cooling of electronics (water)
module performance, data streaming
no sensor cooling, operation at ``room’’ temperature

## Slide 30: Issues seen with modules
module assembly yield
all tested components
microcable attachment yield high
FEB 8 assembly/operation yield too low on the first prototypes
  under systematic study
  new FEB design, custom designed rad. tol. LDO, …
P-side, Vbias = 100V
N-side, Vbias = 100V
noise in longest modules too high
in test box:  1300 e OK
in mSTS:  3000 e  S/N  8-12 threshold high
  under systematic study
  powering scheme, filtering
(preliminary)

## Slide 31: Issues with STS system integration summarized
modules:
understand and improve FEB assembly yield
improve with respect to final noise in system
ladders:
full length assembly to be done
central ladders to be prototyped
vibration analysis:
how to identify sources? cooling: N2 stream, liquid pump, …
apply to which components, measure? ladders, pipes, C-frames, …
beam pipe:
prototype based on carbon fiber, not yet approved
system integration:
optimization of FEB box design with respect to cooling properties and space/cabling requirements

## Slide 32: CBM-STS project teams
Germany
Helmholtz Center (GSI), Darmstadt
Karlsruhe Institute of Technology (KIT), Karlsruhe
Eberhard Karls University (EKU), Tübingen
Poland
University of Science and Technology (AGH), Krakow
Jagiellonian University (JU), Krakow
Warsaw University of Technology (WUT), Warsaw
Russia
Joint Institute for Nuclear Research (JINR), Dubna
Ukraine
Institute for Nuclear Research (KINR), Kiev
Japan
High Energy Accelerator Research Organization (KEK), Tsukuba (associate member)
STS timeline:
Construction: 2019 – 2024
Installation: 2025
First beams: in 2025

## Slide 33: Backup

## Slide 34: Module microcable stack
cable stack:
thickness  800 µm, 0.23% X0
trace capacitance 0.45 pF/cm
trace lengths 5 - 55 cm
N-side read-out
P-side read-out

## Slide 35: Read-out chain Front-end electronics

## Slide 36: mSTS powering scheme
Floating LV supplies are referenced to the P- and N-side potentials.
Microcable shields are connected to the respective FEB grounds.
HV common return is not connected to the mSTS enclosure.
Enclosure is grounded at all times; electrically insulated from the mounting table

## Slide 37: Detector signal path
Return path capacitor must be placed close to the FEBs.
Blocking resistors prevent signal “escape” into the filter and HV power supply.