## Slide 1: Compression and noise reduction of field maps
Xiaonan Du (PSU Department)
Phys. Rev. Accel. Beams 21 084601 (2018)

## Slide 2: Outline
Introduction, eigen-values, transformation of base
Method of High Order Singular Value Decomposition
Example: 5D E-field map of 1st new Alvarez cavity
Benchmark: box-cavity solved analytically

## Slide 3: Why field data can be compressed?
symmetry planes
smoothness (differentiable)
repeated patterns
continuity
lots of zeros
unwanted mesh noise
-120
-120
y
z
simulated E-field distribution of one DTL cell
-120
120
0

## Slide 4: Application for transformation of data
=[0.41,0.91]
=[0.91,-0.41]
with matrix decomposition,
we find a better coordinate system.
and are orthonormal basis
: statistical linear relation between human height and weight
: offset from average for specific person
: height of specific person
: weight of specific person
height weight
Tom
Alice
Bob
…
x
y
body
scale
Tom
Alice
Bob
...
body
type
Temperature
Total
volume
Hot water
volume
Cold water
volume
Time domain:
amplitude, time
Signal Fourier Transform
preferred
coordinates
Frequency domain:
amplitude, frequency
preferred coordinates, remove high frequencies could achieve noise reduction

## Slide 5
High Order Tensor Singular Value Decomposition
(HOSVD)
A Multilinear Singular Value Decomposition
Lieven De Lathauwer, Bart De Moor, and Joos Vandewalle.
SIAM J. Matrix Anal. & Appl. 21-4 (2000), pp. 1253-1278
1st order tensor (vector)
2nd order tensor (matrix)
3rd order tensor
(stack of matrices)
4th order tensor
(hard to draw ..)
SVD:
train a set of orthonormal basis with original data (bunch of vectors or discrete 1D distributions), and project the data to them. Those basis are sorted according to it singular value. Elimination of bases with low singular-values can provide compression and noise reduction w/o loss of data essentials
SVD | Eigen decomposition | Fourier expansion
Singular values | Eigen values | Coefficients, spectral
Singular vectors | Eigen vector | Fourier basis
Sorted according to singular value | Sorted according to Eigen value | Sorted according to its wave length
HOSVD:
generalization of SVD, commonly applied to the extraction of relevant information from multi-way arrays (high order tensor).
Tensor:

## Slide 6
2D heat map (matrix)
90 mesh
steps
100 mesh steps
(90,100)
(100,100)
(90,90)
(90,100)
S
(90,100)
(100,100) a set of new bases
(90,100)
(90,90)
(90,100)
Finally,
More familiar expressions:
heat map on
mesh grid (90,100):
2D SVD, step by step:
original data
Example of 2nd order data SVD
2nd tensor,
matrix
: treat row (1st dim) as vector to .......calculate inner product
: treat column (2nd dim) as vector …….to calculate inner product
: treat name? (3rd dim) as vector …….to calculate inner product

## Slide 7
The operator:
discrete 3D distribution, e.g potential map, heat map, density map...
2X2 matrix is transformed to 4X3 matrix.
The process could be reversed if basis are orthonormal.

## Slide 8
finally, we get compressed data, a tensor with shape (2,3,4) and 3 sets of basis
Reduce
3D heat map, with mesh grid 20*30*40 (**)
core tensor with shape (20,30,40)
3 sets of singular vectors (square matrices)
(40,40)
(30,30)
(20,20)
HOSVD
(20,30,40)
(20,30,40)
A
S
s
: compressed & recovered data
Example of 3rd order data SVD and compress
here: (2,3,4) components from new base were kept
new core tensor
singular vectors with largest eigen-values
(i, j, k)
(j, n)
(i, m)
(k, p)
dumped, because of too
small singular value
s

## Slide 9: Generalize to tensor with order
Original data A is pre-stacked Nth-order tensor with shape(), decomposition by HOSVD is
where ,
data is represented by coefficient tensor S and basis (, 1≤n≤N), then are cut to according to its singular value:
where , , ,
=
basis with high singular values (data essence) are preserved!
s and is compressed data, is de-noised data.
≈

## Slide 10: Data recovery /de-compress/ inquire
extract data value on specific mesh node :
where is the th column of
new core tensor
(i, j, k)
(j, n)
(i, m)
(k, p)
s
use one column of each set of basis, the result will be scalar field value on specific mesh node.
Use complete basis that preserved, the result will be entire field map.
42

## Slide 11: Advantage of transformed data
Much less data volume
Practically noise-free
High efficient data extraction: the extraction of de-noised data is done through multi-linear mapping rather than through time consuming memory search. The efficiency of beam dynamic simulation codes can by improved accordingly, if such compressed field map are used

## Slide 12: E-field map data of 1st cavity of new Alvarez-DTL
original field map is a 5th order tensor with shape (55, 201, 41, 41, 3), i.e.,
it comprises 55*201*41*41*3 = 5.5*107 entries
To each cell 201*41*41(long.*hor.*ver.)
mesh nodes are assigned.
3 field components on each mesh node.
tank1 comprises 55 cells
55 DTL cells
201 z-nodes per cell
41 x-nodes per cell
41 y-nodes per cell
3 field components per node: Ex,Ey,Ez
to “address“ a single field value, 5 infos needed, i.e., which:
cell, z-node, x-node, y-node, component
→

## Slide 13
after HOSVD and reduction:
(55, 201, 41, 41, 3)
shape of s: (3,8,4,4,3)
shape of : (3,55)
shape of : (8,201)
shape of : (4,41)
shape of : (4,41)
shape of : (3,3) as no field component shall be lost !
total file size : 20 KB
Field map data set size after compression
dimension of original data -> fixed
from desired amount of compression ->
(to be shown later …)
compression factor ≈ 10000

## Slide 14
distribution along z axis is linear
combination of . The 1st singular vector is very similar to
distribution along x axis is
linear combination of
What the singular vectors looks like
high value singular vectors
low value singular vectors
noise-like, no physical meaning, should be cut
noise-like, no physical meaning, should be cut
z-node
x-node
z-node
x-node

## Slide 15
Determine number of base components to be kept, i.e., the compression factor
original: (55, 201, 41, 41, 3)
choice made as (3,8,4,4,3)
why not (5,15,8,8,3) or (3,3,3,3,3)?
change third index:
Threshold is set to 1/10000 of the largest singular value, which is beyond expected accuracy of field map.
too much useless
data
loss of essential data
too much useless
data
loss of essential data
change second index:
15

## Slide 16
comparing original data (55,201,41,41,3)
with compressed & recovered data (3,8,4,4,3)
CR: compressed and recovered
maybe CR data is worse because some “true information” is dumped
maybe CR data is better, because noise is dumped
check of quality ...
z
x
y
Quality of compressed field map data

## Slide 17
z
y
x
a = 100 mm; b = 130 mm; l = 200 mm;
m = 1; n = 1; p = 1
good mesh
poor mesh
typical DT mesh
rf gap
Example box cavity:
simulated and analytical field map

## Slide 18
x
z
y
Check field distribution at arbitrary 2D slice :
Comparisons of originally simulated field map and of de-noised (RC) field map reveals that the algorithm reduces the amount of noise for both mesh types, and the analytical field values are reproduced. Additionally, the data volume to be stored is significantly reduced during field extraction
deviation from “analytical“

## Slide 19
check field distribution at arbitrary off-axis position :
and along z axis, x=10, y=10 (node)
smoothness of Ez and Ey distribution is hard to see directly
smoothness of their derivatives d/dz is easy to see
CR-data is much smoother, hence with physical meaning (it is in fact much closer to analytical solution)
Analyzing field smoothness inside DTL gap
un-physical field ripples give kicks to particles in beam dynamics simulations
these kicks are not real and lead to artificial beam heating
this is of concern for circular machines (many passages through noisy field maps)

## Slide 20
Data volume of the field map is compressed dramatically by four orders of magnitude
Compression also reduces field map noise caused by finite element method
Applicable to any kind of field maps
Paves way to develop a high efficiency particle simulation code that uses compressed field map
Details in
Summary
Thank you!
one more slide below for a frequently asked question.

## Slide 21: Shortcut for calculation of n-mode SVD
several ways to get right side singular vectors numerically.
Original way:
Eigen decomposition on to get singular vectors.
it is announced that calculation of is time consuming.
poor accuracy for low singular value part.
improved numerical methods:
iterative, save the effort of calculating , more precise.
a bunch of 41-dimensional vectors, is one of it’s elements
is mentioned as square-sum matrix C in the paper.
we already have pre-stacked data, not necessary to unfold to huge matrix B