## Slide 1: Particle Tracking Challenges: The CBM Silicon Tracking Station at FAIR
Christian J. Schmidt,
GSI Darmstadt
at Gauhati University, Assam, India

## Slide 2: FAIR - Facility for Anti-Proton and Ion Research, Darmstadt
GSI Helmholtz Center for Heavy Ion Research GmbH, Darmstadt, Germany
p to U beams,
2 – 45 GeV/nucleon
highest intensities
1 km circumference
CBM
The GSI-future project under construction, operative in 2024

## Slide 3: FAIR - Facility for Anti-Proton and Ion Research, Darmstadt
Spring 2017

## Slide 4
August 2018

## Slide 7: FAIR - Facility for Anti-Proton and Ion Research, Darmstadt
GSI Helmholtz Center for Heavy Ion Research GmbH, Darmstadt, Germany
p to U beams,
2 – 45 GeV/nucleon
highest intensities
1 km circumference
CBM
The GSI-future project under construction

## Slide 8: CBM
Compressed Baryonic Matter
  About 500 members
Collide Au heavy ions onto Au nuclei
in a fixed target configuration at ~ 10 GeV/nucleus
CBM

## Slide 9: CBM Detector
Dipol
magnet
Ring Imaging
Cherenkov
Detector
Transition
Radiation
Detectors
Resistive
Plate
Chambers
(TOF)
Electro-
magnetic
Calorimeter
Silicon
Tracking
Stations
Tracking
Detector
MUCH
Muon
detection
System
Projectile
Spectator
Detector
(Calorimeter)
Vertex
Detector

## Slide 11
Diagnostic probes

## Slide 12
 10 MHz  6 billion tracks per second
 determination of (displaced) vertices (σ  50 m)
 identification of leptons and hadrons
 fast and radiation hard detectors
 free-streaming readout electronics
high speed data acquisition and high performance
computer farm for online event selection
 4-D event reconstruction
CBM technological challenges
fixed target configuration makes 10MHz Au+Au interaction rate feasible at FAIR
Notes: 12
12
12

## Slide 13: Detector Laboratory at GSI: 600 m2 Clean-Room
22 m
36 m
Machinery:
Laser Lithography
PVD
Bonding Automates
Probestation and Chip Handling
Automated Wire Winding
Digital Microscope
Thin Foils Handling and Processing
Gaseous Detector Ageing Teststands
Large Prototyping CNC Milling Machine
Competences:
Micro Patterned Gaseous Detector Technology
Silicon Strip Detector Integration
ASIC Handling and Integration
Diamond Detectors
PSL APD-characterization lab

## Slide 14: ISO 3 Clean Room for Laser Lithography 1µ
5 x 5 mm2 SCDiamond
5 x 5 mm2 SCDiamond

## Slide 15: Work at GSI Detectorlab

## Slide 16: Precision fibre composite milling from very small to very large
100cm x 160cm
fibre composits
= 3D-mold manufacturing
Hades MDC
CBM-STS sensor clips

## Slide 17: CBM Silicon Tracking System STS
to be fit into magnet yoke (1,4m)
Fixed Target Tracker, Acceptance 2,5°< q < 25°
Double Sided Silicon Strips in 8 Layers, 58µm
2 Mio. readout channels, ~ 3 m2
Event rate 10 MHz, freely streaming r/o
less than 1% radiation length per layer
x/X0 [%]
material budget per station
Central Au on Au Collision at 8 AGeV

## Slide 18: Mechanical Integration in Fixed Target Configuration
Thermal enclosure, operation at -5°C
Minimize mat. budget in acceptance
Electronics outside acceptance, 40kW
Module
Ladder
of 10 modules
Half-Station
140cm

## Slide 19
Silicon-Doublesided-Microstrip-Sensors
6 x 2 cm2
6 x 4 cm2
6 x 6 cm2
6 x 12 cm2
Sizes
300 µm thick, n-type silicon
double-sided segmentation
2nd metal routing lines
1024 strips of 58 µm pitch
rad. tol. up to 1014 neq/cm2

## Slide 20: CBM-STS-module-assembly
Numbers:
1000 Modules
32 cables per module
2048 ch per module
Tab bonding
Micro cables: 10µ Polyimide 14µ Al traces

## Slide 21: Micro Cable Technology with TAB-Bonding
double cable layer bonded onto chip

## Slide 22: 32.000 read-out cables cooperation with LTU, Ukraine
cable stack: thickness 0.230 % X0
spacer layer
signal layer: 64 Al lines of 116 µm pitch, 14 µm thick on 10 µm polyimide, lengths up to 55 cm

## Slide 23
Assembly Jigs
jig for TAB-bonding 1st and 2nd micro-cable layer to ASIC
jig for TAB-bonding 1st microcable layer to ASIC
jig for TAB-bonding micro-cables to sensor with micro-positioners for
x-, y- and rotation

## Slide 24
Tab-Bonding Chip-Cables to Silicon Sensor
fixing of the microcables with vacuum and alignment
TAB-bonding of 16 microcables to the sensor (two rows at 8 microcables)
protection of the TAB-bonds with Globtop after QA-measurements
wire-bonding of the STS-YTER-ASIC´s
Wire Bonding Chip-Cables
to Readout Board
... and then the other side...

## Slide 25
STS-XYTER: Dedicated AGH-ASIC Development for CBM
128 ch, self-triggered, dynamics 15 or 75 fC, ~ 1000ENC
power < 10mW/ch, GBTx-compatible output
1024 ch Front End Board (FEB)
Operation: floating at bias potential
256 Mhit/s ~ 10 Gbit/s bandwidth
30,6 mm

## Slide 26: ZIF 500V-AC-Coupling Connector Part
40-pin 0.5mm pitch ZIF
Compatible to 40-line commercial shielded flat cable
Height to be optimized
good for up to 18 up-links
Mounted device sensitive to shear forces: need to add glue for robustness.

## Slide 27: Digital Interfacing: Bridging Signals to Gnd – 3D arrangement
first tombstone tests
...after optimization

## Slide 28: 128ch Readout ASIC serves as STS-XYTER and Much-XYTER r/o
Moderate Time (~5ns) and Energy res. (5bit)
1000 electrons noise
Switchable Gain, Identical Readout Logic
GBTx-based DAQ, 32 Mhit/s each chip
Power optimized, radiation tolerant
Microchip ASIC developed at AGH Krakow,
Design internationally reviewed,
Detector Integration by international groups
1024 ch CBM-STS readout board

## Slide 29: STS-XYTER Readout Microchip Analog Front End
Switchable
(90ns – 280ns)
in 4 steps
Switchable gain
(5x smaller for MUCH)
+ trimming 2 bit
Krzysztof Kasinski and Robert Szczygiel of AGH
Krakow, Poland

## Slide 30: Skimming LDOs: Development at SCL Chandigarh
Output noise (100kHz to 100MHz) < 70µV RMS
1/3 of STS-XYTER power-pin related signal noise (210 µV RMS),
1/10 noise power contribution
Final size: 5.7mm x 6.2mm
Two versions: 1.8V/1.6A and 1.2V/1.6A
Ripple rejection up to 100kHz
Junction temp up to 100°C
No self-restart upon overcurrent
Output enable
5 external parts (R, 4 Caps)
pre prototype
5.7mm
6.2mm

## Slide 31: Power distribution in harsh environments Towards Rad Hard LDOs Cooperation with SCL Chandigarh
STS-XYTER needs on power quality
Three LDO chips survived 4x1013/cm2
2 GeV protons, no SEU observed
P. Koczon, S. Loechner, P. Wieczorek
V2/Hz

## Slide 32
Final STS-Module:

## Slide 33: Concept inherited from ALICE ITS: Carbon fiber ladders
11g for 1m long ladder
mount 10 silicon modules onto one ladder

## Slide 34
Assembly Tests : Modules onto Prototype Ladder
S.Mehta , University of Tübingen and GSI, Darmstadt
Dummy module - I
Dummy module - II
Dummy module - III
Dummy module - IV
Dummy module - V
6

## Slide 35
Cable stack is thick and stiff
Need precise lengths of cables so they won´t fold up
While mounting on frame, handling difficulty.
Ladder assembly imposes mechanical challenges during assembly of modules onto ladder

## Slide 36: Mini-CBM @ FAIR Phase 0: fully assemble and operate small functional CBM subset
Currently: pre-series modules employed in the miniSTS of mCBM@SIS18
13 modules, arranged on 5 ladders, forming 2 tracking stations
mCBM run 02/2019: mCBM run scheduled May 2020: 4 modules on 2 ladders further 9 modules on 3 ladders

## Slide 37
Chart: CBM Collaboration (511 scientists)
| Germany | Russia | India | Poland | China | Romania | Ukraine | France | Czech Republic | Hungary | Croatia | Korea
 | 159 | 135 | 62 | 44 | 24 | 23 | 11 | 9 | 7 | 6 | 6 | 4
The CBM Collaboration
First physics beam targeted in 2024

## Slide 39: Time Projection Chamber, the Queen of Trackers
100 m3 gas
Currently engagement in mayor fraction of GEM based ALICE TPC upgrade
None-triggered continuous TPC readout

## Slide 40: HADES- The GSI Dilepton Spectrometer
Detector lab engagement in HADES Drift
Chamber design and production