## Slide 1: WQ Magnet for CR. CDR/FDR Review.
D. Gurov, A.Utkin for CR team
BINP, Novosibirsk
November 28, 2019
3rd FAIR-BINP Workshop, Novosibirsk, Russia

## Slide 2: Contents
CDR documentation
Project management structure
Base principles and Concept
WQ quadrupoles in CR
Calculations and simulations
Assembling
Production plan

## Slide 3: FDR Documentations
The 3D-models (in EDMS): https://edms.cern.ch/document/2146941/1
Mechanics - 2D drawings anhttps://edms.cern.ch/document/2245832/1

## Slide 4: Project management
Name: Anatoly Utkin
Position: Research Scientist Email: A.V.Utkin@inp.nsk.su
Tel.: +7383329-4684
The Deputy is responsible for:
Follow-up of production activities;
Magnetic measurements to ensure the required field and field quality;
Factory Acceptance Test (FAT) to verify the given specifications of the components;
Name: Denis Gurov
Position: Research Scientist Email: D.S.Gurov@inp.nsk.su
Tel.: +7383329-4684
The Deputy is responsible for:
Preliminary magnet design, final magnet design (development, simulation);
Magnetic field calculation;
More Details in “Quality Plan”
The Project Manager
Name: Alexandr Starostenko
Position: Head of BINP Division № 5-11 Email: A.A.Starostenko@inp.nsk.su
Tel.: +7383329-4940
The Project Manager is responsible for:
Development of the technical documentation and manufacturing drawings for the deliverables;
Ensuring that the production of the magnets is according to the technical specifications and time schedule;
Follow-up of production activities;
Transportation, delivery of the equipment to the FAIR site;
Regular and timely reporting on progress and problems;
Timely conduction/participation of reviews and provisions of feedback;
Scientific Design Department
Name: Vladimir Korchagin
Position: Principal Design Engineer Email: V.Ya.Korchagin@inp.nsk.su
Tel.: + 7383329-4953
The Principal Design Engineer is responsible for:
Magnet design (3D-models, production drawings);

## Slide 5: Construction of WQ magnet

## Slide 6: Construction of WQ magnet
Profile for laminas stamping
Quarter of yoke

## Slide 7: Construction of WQ magnet
35 turns coil
WQ magnet coil construction

## Slide 8: WQ Quadrupole and stand for quadrupole only

## Slide 9: WQ Quadrupole and stand for one sextupole

## Slide 10: WQ Quadrupole and stand for two sextupoles

## Slide 11: WQ calculations
3D Magneto-static calculations in “Mermaid” code
Pole profile coordinates (mm)
Chart: 
| 44 | 44 | 49.512 | 51.661000000000001 | 53.720999999999997 | 56.193999999999996 | 58.571999999999996 | 61.772999999999996 | 63.106999999999999 | 64.855000000000004 | 66.573000000000008 | 68.682999999999993 | 71.167999999999992 | 73.611999999999995 | 76.421999999999997 | 79.591999999999999 | 83.908000000000001 | 88.204999999999984 | 93.699999999999989 | 100.09299999999999 | 106.28 | 113.19184 | 120.55115000000001 | 127.99754999999999 | 136.71746000000002 | 145.21485000000001 | 152.62771000000001 | 160.86552999999998 | 167.49808000000002 | 173.84040999999999 | 179.75010999999998 | 186.17273999999998 | 191.98039 | 196.96889999999999 | 202.30238 | 206.55512999999999 | 217.45334 | 226.22135 | 235.97920999999999 | 244.62136999999998 | 254.12518 | 265 | 290
 | 290 | 265 | 254.1252 | 244.6214 | 235.9792 | 226.2214 | 217.4533 | 206.5551 | 202.3024 | 196.9689 | 191.9804 | 186.1727 | 179.7501 | 173.8404 | 167.4981 | 160.8655 | 152.6277 | 145.2149 | 136.7175 | 127.9975 | 120.5512 | 113.1918 | 106.28 | 100.093 | 93.7 | 88.205 | 83.908 | 79.592 | 76.422 | 73.612 | 71.168 | 68.683 | 66.573 | 64.855 | 63.107 | 61.773 | 58.572 | 56.194 | 53.721 | 51.661 | 49.512 | 44 | 44
X (mm) | Y (mm)
113.192 | 113.192
120.551 | 106.28
127.998 | 100.093
136.717 | 93.7
145.215 | 88.205
152.628 | 83.908
160.866 | 79.592
167.498 | 76.422
173.84 | 73.612
179.75 | 71.168
186.173 | 68.683
191.98 | 66.573
196.969 | 64.855
202.302 | 63.107
206.555 | 61.773
217.453 | 58.572
226.221 | 56.194
235.979 | 53.721
244.621 | 51.661
254.125 | 49.512
265 | 44
290 | 44
Pole profile
Chamfer 17.5 mm depth 35 mm height, side cut outs 20 mm depth 20 mm width

## Slide 12: Field in yoke
Field in yoke (kGs) at maximal gradient value
Permeability in yoke at maximal gradient value

## Slide 13: Field quality
Longitudinal gradient distribution at maximal gradient value.
Integral contributions of 6th and 10th multipoles at 136 mm radius.
Chart: Integral contribution of 6 and 10 harmonics at different gradient magnitudes
| 0.69134720000000005 | 2.7707313999999998 | 4.8260665999999999 | 5.7308066000000002 | 6.3797357999999997
A6/A2 | 0.00016576 | 0.00011022 | -2.4533e-05 | -0.00016211 | -0.00034114
A10/A2 | 8.968e-05 | 7.7597e-05 | 4.3679e-05 | 2.066e-05 | 5.925e-06

## Slide 14: Field quality
H - Integral Homogeneity
H=
Chart: Integral inhomogeneity on horizontal plane
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 15 | 16 | 17 | 18 | 19 | 20
0.47 T | -0.00088252 | -0.00084488 | -0.0008094 | -0.00076413 | -0.00069951 | -0.00060339 | -0.00045489 | -0.00034869 | -0.00020994 | -2.616e-05 | 0.00021882 | 0.00054622 | 0.00098427
4.7 T | 0.00067026 | 0.00070494 | 0.00072549 | 0.00072833 | 0.00070049 | 0.0006164 | 0.000439 | 0.00030152 | 0.00012522 | -9.1773e-05 | -0.00034711 | -0.0006297 | -0.00091357
3.3 T | -0.00012069 | -8.9831e-05 | -5.8512e-05 | -2.8839e-05 | 0 | 2.4271e-05 | 3.7963e-05 | 3.9319e-05 | 3.7802e-05 | 3.7897e-05 | 4.6135e-05 | 7.7382e-05 | 0.00015985
4 T | -8.4932e-05 | -4.8311e-05 | -2.1952e-05 | -3.503e-06 | 0 | -2.3672e-05 | -9.7741e-05 | -0.0001618 | -0.00024521 | -0.0003486 | -0.00046775 | -0.00058778 | -0.00068347
1.88 T | -0.0006656 | -0.00062832 | -0.00059458 | -0.00055395 | -0.00049975 | -0.00042452 | -0.00031612 | -0.0002419 | -0.00014691 | -2.2553e-05 | 0.00014312 | 0.00036774 | 0.00067842

## Slide 15: Calculation of attraction force
I=1490 A
Distance between SWQ yoke and Yoke of the sextupole magnet is 350 mm.
3D model in FEM “Mermaid” of ¼ of construction

## Slide 16: Calculation of attraction force
Field magnitude (kGs) near surface of sextupole yoke
Longitudinal distribution of magnetic field (kGs) along line from SWQ quadrupole yoke to sextupole yoke
1
2
3
4
5
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310 | 320 | 330 | 340 | 350
1 | 4.6076 | 4.4691 | 4.34 | 4.2056 | 4.0555 | 3.8698 | 3.6392 | 3.383 | 3.1109 | 2.8256 | 2.528 | 2.2649 | 2.0416 | 1.844 | 1.6669 | 1.5069 | 1.3556 | 1.2266 | 1.1084 | 1.0026 | 0.90781 | 0.82251 | 0.74691 | 0.67968 | 0.61974 | 0.56725 | 0.52127 | 0.48119 | 0.44719 | 0.41879 | 0.39573 | 0.37826 | 0.36613 | 0.35815 | 0.35433 | 0.35465
2 | 2.6647 | 2.6455 | 2.6404 | 2.6419 | 2.6411 | 2.5327 | 2.4168 | 2.3009 | 2.1941 | 2.1087 | 2.0601 | 1.9973 | 1.9025 | 1.7885 | 1.6581 | 1.5136 | 1.3252 | 1.1803 | 1.0577 | 0.95559 | 0.86637 | 0.78749 | 0.71941 | 0.65978 | 0.60725 | 0.56204 | 0.52294 | 0.48916 | 0.46086 | 0.4373 | 0.41794 | 0.40292 | 0.39165 | 0.38373 | 0.37914 | 0.37791
3 | 1.1356 | 1.1668 | 1.2162 | 1.2798 | 1.3524 | 1.2436 | 1.1374 | 1.0379 | 0.9486 | 0.87412 | 0.81921 | 0.78919 | 0.7887 | 0.81998 | 0.8831 | 0.97592 | 0.88518 | 0.80388 | 0.73127 | 0.66674 | 0.60952 | 0.5588 | 0.51405 | 0.47459 | 0.4399 | 0.40963 | 0.3834 | 0.36111 | 0.34257 | 0.32779 | 0.31778 | 0.31215 | 0.31271 | 0.32348 | 0.34346 | 0.37408
4 | 9.0155 | 7.9786 | 6.9305 | 6.0212 | 5.2238 | 4.539 | 3.9542 | 3.4548 | 3.0268 | 2.6586 | 2.3411 | 2.0666 | 1.8284 | 1.6205 | 1.4383 | 1.278 | 1.1378 | 1.0132 | 0.90259 | 0.80428 | 0.7165 | 0.6376 | 0.56681 | 0.50293 | 0.44487 | 0.3921 | 0.34374 | 0.299 | 0.25748 | 0.21846 | 0.18134 | 0.14585 | 0.11163 | 0.078894 | 0.049914 | 0.035424
5 | 2.7412 | 2.582 | 2.4147 | 2.2434 | 2.0696 | 1.8961 | 1.7263 | 1.5633 | 1.4101 | 1.2686 | 1.14 | 1.0243 | 0.92061 | 0.8278 | 0.74461 | 0.67 | 0.60346 | 0.54338 | 0.48925 | 0.44047 | 0.39628 | 0.35602 | 0.31939 | 0.28583 | 0.2549 | 0.22635 | 0.1998 | 0.17489 | 0.15147 | 0.12922 | 0.10788 | 0.08733 | 0.067384 | 0.048132 | 0.030841 | 0.022533

## Slide 17: Calculation of attraction force
Stored energy (J)
F(N)= dE/dX =3.26/0.04= 81.4 N
Chart: Energy, stored in system at different distances between magnets
| 330 | 350 | 370
 | 26881.155 | 26882.985 | 26884.413
Distance (mm)
Energy (J)

## Slide 18: Assembling of the magnet
1. Fasten alignment feet 1 (3 pcs.) to the lower half of the yoke 2 (1 pcs.), using bolts 3 (18 pcs.);
2. Install the lower half of the yoke of WQ quadrupole on stand 4 (1 pcs.) (alignment feet must be properly fastened to a stand using bolts 5 (12 pcs.)to prevent any fall);
3. Install the lower half of the sextupole yoke on stand (when quadrupole shares same stand as sextupole, sextupole alignment feet must be properly fastened to a stand to prevent any fall);
4. Install vacuum chamber on lower half of WQ quadrupole (and sextupole)
5. Install the upper half of the yoke of WQ quadrupole 6 (1 pcs.) on lower half WQ quadrupole and fasten to each other using bolts 7 (16 pcs.)
6. Install the upper half of the sextupole yoke on lower half sextupole (when quadrupole shares same stand as sextupole) and fasten to each other using bolts
7. Install the manifolds 8 (2 pcs.) on the side of the magnet on the brackets 9 (2 pcs.) using the mounting blocks 10 (4 pcs.) with the bolts 11 (8 pcs.);

## Slide 19: Assembling of the magnet
8. Connect lower and upper half of manifolds, using bolts 28 (4 pcs.);
9. Install the connection boxes 12 (2 pcs.);
10. Assemble the connection boxes 12:
10.1. Install the cable connection plates 13 (2 pcs.) using the mounting blocks 14 using the fastening plates 15 with the bolts 16 (4 pcs.);
10.2. Connect the upper and lower windings using the midpoint connection plate 17 (1 pcs.) with the bolts 18 (8 pcs.);
10.3. Connect the cable connection plates 13 (2 pcs.) with the beginning and end of the upper and lower windings with the bolts 20 (8 pcs.);
10.4. Fix the outlets of the sections of the windings using the mounting blocks 21 using the fastening plates 22 with the bolts 23 (4 pcs.);
11. Connect the water hoses 24 (8 pcs.) to fittings 25, fix with the clamps 26 (16 pcs.).

## Slide 20: Production Plan
Month | Activity | Begin | End
0 | Contract is signed | 26.06.2018 | 26.06.2018
6 | Tecnological design, Equipment design | 27.12.2018 | 30.09.2019
11 | Conceptual Design Review | 23.05.2019 | 23.05.2019
12 | Design in detail | 26.06.2019 | 28.06.2019
16 | Final Design Review | 07.11.2019 | 07.11.2019
17 | Material procurement | 20.11.2019 | 30.01.2020
17 | Tooling manufacturing | 20.11.2019 | 29.03.2020
21 | Manufacturing of pre-series | 01.04.2020 | 01.06.2020
23 | FAT of pre-series | 01.06.2020 | 30.07.2020
25 | Shipment of pre-series to FAIR | 04.08.2020 | 26.08.2020
26 | SAT A of pre-series | 09.09.2020 | 21.10.2020
28 | Manufacturing of series | 22.10.2020 | 23.05.2023
28 | Prepare series production | 22.10.2020 | 22.02.2021
32 | Series production started | 22.02.2021 | 22.02.2021
34 | FAT accepted | 22.04.2021 | 23.05.2023
37 | Site Assembling series | 23.07.2021 | 27.06.2023
38 | SAT Series | 23.08.2021 | 04.07.2023
38 | SAT accepted | 23.08.2021 | 04.07.2023