## Slide 1: Octupole Corrector for CR. CDR Review.
D. Gurov, A.Utkin for CR team
BINP, Novosibirsk
November 27, 2019
3rd FAIR-BINP Workshop, Novosibirsk, Russia

## Slide 2: Contents
CDR documentation
Project management structure
Base principles and Concept
OC octupoles in CR
Calculations and simulations
Assembling
Production plan

## Slide 3: CDR Documentations
Risk analysis and hazard analysis https://edms.cern.ch/document/2245853/1
Operating manual / user manual https://edms.cern.ch/document/2245855/1
Test plan
https://edms.cern.ch/document/2245857/1
Mechanics - 3D model
https://edms.cern.ch/document/2245861/1

## Slide 4: Project management
Name: Denis Gurov
Position: Research Scientist Email: D.S.Gurov@inp.nsk.su
Tel.: +7383329-4684
The Deputy is responsible for:
Follow-up of production activities;
Magnetic measurements to ensure the required field and field quality;
Factory Acceptance Test (FAT) to verify the given specifications of the components;
Name: Anatoly Utkin
Position: Research Scientist Email: A.V.Utkin@inp.nsk.su
Tel.: +7383329-4684
The Deputy is responsible for:
Preliminary magnet design, final magnet design (development, simulation);
Magnetic field calculation;
More Details in “Quality Plan”
The Project Manager
Name: Alexandr Starostenko
Position: Head of BINP Division № 5-11 Email: A.A.Starostenko@inp.nsk.su
Tel.: +7383329-4940
The Project Manager is responsible for:
Development of the technical documentation and manufacturing drawings for the deliverables;
Ensuring that the production of the magnets is according to the technical specifications and time schedule;
Follow-up of production activities;
Transportation, delivery of the equipment to the FAIR site;
Regular and timely reporting on progress and problems;
Timely conduction/participation of reviews and provisions of feedback;
Scientific Design Department
Name: Vladimir Korchagin
Position: Principal Design Engineer Email: V.Ya.Korchagin@inp.nsk.su
Tel.: + 7383329-4953
The Principal Design Engineer is responsible for:
Magnet design (3D-models, production drawings);

## Slide 5: Construction of OC magnet

## Slide 6: Construction of OC magnet
Quarter of SWQ yoke with quadrupole and octupole coils
Quarter of SWQ yoke

## Slide 7: OC Octupole parameters
Parameter | Value
Water consumption | 2.7 l/min
Dimensions of wire for coils | 4.5x4.5 mm
Number of OC magnets | 12
Overall weight | 124 kg
Coil current | 42 A
Number of coil turns | 33
Coil resistance | 930 m
Coil inductance | 68 mH
Maximum DC power loss | 1.65 kW

## Slide 8: Various constructions of octupole coils
Chart: Longitudinal distribution of field in octupole in different constructions at same current
1
3

## Slide 9: OC magnet calculations
3D Magneto-static calculations in “Mermaid” code
Coil coordinates (mm)
Longitudinal distribution of magnetic field (Gs) in octupole corrector at total current 1 kA per coil at 10 cm. radius (green and red lines are showing the edge of yoke and octupole coils correspondently).
X (mm) | Y (mm)
107.4 | 96.9
109.3 | 101.1
274.7 | 21.4
276.5 | 25.5
412.8 | 8.1
409.7 | 11.4
539.4 | 141.4
542.6 | 138.1
96.9 | 107.4
101.1 | 109.3
21.4 | 274.7
25.5 | 276.5
8.1 | 412.8
11.4 | 409.7
138.1 | 542.6
141.4 | 539.4
Chart: Longitudinal distribution of magnetic field
 | 0 | 16
 | 0 | 16

## Slide 10: Field in yoke
Field in yoke (kGs) at maximal octupole gradient value
Flux lines

## Slide 11: Field quality
Integral contributions of 8th 12th and 16th multipoles at 120 mm radius.
The integral harmonic contribution of the field at the 120 mm radius.
n | An (T/m**2) | Bn (T/m**2)
1 | 2.31E-05 | 0
2 | -1.16E-05 | 0
3 | 8.10E-05 | 0
4 | 1.53 | 0
5 | 1.85E-04 | 0
6 | 0.00 | 0
7 | -2.55E-04 | 0
8 | -8.16E-03 | 0
9 | -2.43E-04 | 0
10 | 0.00 | 0
11 | 1.97E-04 | 0
12 | -1.01E-02 | 0
13 | 1.62E-04 | 0
14 | -1.16E-05 | 0
15 | -1.27E-04 | 0
16 | 6.60E-03 | 0
17 | -1.04E-04 | 0
18 | 0.00 | 0
Chart: G*L (T/m**2)
| 1.1054745370370371 | 0.55274305555555558 | 0.11054398148148149
A8/A4 | -0.0053501 | -0.0053605 | -0.0053398
A12/A4 | -0.0066274 | -0.0066378 | -0.0065962
A16/A4 | 0.004324 | 0.0043344 | 0.0042927
Chart: Integral inhomogeneity on horizontal plane
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0.96309 | 0.066356 | 0.013878 | 0.0047268 | 0.0019179 | 0.00076895 | -3.2177e-05 | -0.00083892 | -0.0019068 | -0.0034739 | -0.0057551 | -0.0089581 | -0.013265 | -0.018778 | -0.025535 | -0.033498 | -0.042574 | -0.052587 | -0.063288 | -0.074361

## Slide 12: Assembling of the magnet
1. Fasten the Octupole Corrector coils to the quarters of SWQ yoke using bolts 37 (16 pcs.);
2. Fasten the quarters of SWQ yoke to each other to create upper and lower half of SWQ yoke, using bolts 38 (12 pcs.);
3. Fasten the alignment feet 1 (3 pcs.) to the lower half of the yoke 2 (1 pcs.), using bolts 3 (18 pcs.);
4. Install the lower half of the yoke of the SWQ quadrupole on the stand 4 (1 pcs.) (alignment feet must be properly fastened to a stand using bolts 5 (12 pcs.) to prevent any fall);
5. Install the lower half of the sextupole yoke on the stand (sextupole alignment feet must be properly fastened to a stand to prevent any fall);
6. Install the vacuum chamber on the lower half of the SWQ quadrupole and sextupole;
7. Install the upper half of the yoke of the SWQ quadrupole 6 (1 pcs.) on the lower half of the SWQ quadrupole and fasten to each other using bolts 7 (12 pcs.);
8. Install the upper half of the sextupole yoke on the lower half of the sextupole and fasten to each other using bolts;
9. Install the manifolds 8 (2 pcs.) on the side of the magnet on the brackets 9 (2 pcs.) using the mounting blocks 10 (4 pcs.) with the bolts 11 (8 pcs.);
10. Connect the lower and upper half of the manifolds using bolts 28 (4 pcs.);
11. Install the connection boxes for quadrupole coils 12 (2 pcs.) and octupole coils 27 (2 pcs.);

## Slide 13: Assembling of the magnet
12. Assemble the quadrupole coils connection boxes 12:
12.1. Install the cable connection plates 13 (2 pcs.) using the mounting blocks 14 using the fastening plates 15 with the bolts 16 (4 pcs.);
12.2. Connect the upper and lower windings using the midpoint connection plate 17 (1 pcs.) with the bolts 18 (8 pcs.);
12.3. Connect the cable connection plates 13 (2 pcs.) with the beginning and end of the upper and lower windings with the bolts 20 (8 pcs.);
12.4. Fix the outlets of the sections of the windings using the mounting blocks 21 using the fastening plates 22 with the bolts 23 (4 pcs.);
13. Connect the water hoses 24 (8 pcs.) to the fittings 25, fix with the clamps 26 (16 pcs.) ;
14. Assemble the octupole coils connection boxes 27:
14.1. Connect the water hoses 30 (16 pcs.) to the fittings 29, fix with the clamps 31,32 (32 pcs.);
14.2. Connect the upper and lower windings using the midpoint connection plate 35 (1 pcs.) with the bolts 34 (2 pcs.);
14.3. Connect power supply to the current outlets 33,36 .

## Slide 14: Production Plan
OC production plan
Month | Activity | Begin | End
0 | Contract is signed | 26.06.2018 | 26.06.2018
7 | Tecnological design, Equipment design | 05.02.2019 | 09.11.2019
12 | Conceptual Design Review | 02.07.2019 | 02.07.2019
13 | Design in detail | 05.08.2019 | 26.09.2019
16 | Final Design Review | 07.11.2019 | 07.11.2019
17 | Material procurement | 20.11.2019 | 30.01.2020
19 | Tooling manufacturing | 19.01.2020 | 17.06.2020
25 | Manufacturing of pre-series | 20.07.2020 | 19.09.2020
27 | FAT of pre-series | 19.09.2020 | 17.11.2020
29 | Shipment of pre-series to FAIR | 22.11.2020 | 14.12.2020
30 | SAT A of pre-series | 28.12.2020 | 08.02.2021
36 | Manufacturing of series | 09.07.2021 | 23.05.2023
32 | Prepare series production | 11.03.2021 | 12.07.2021
36 | Series production started | 12.07.2021 | 12.07.2021
38 | FAT accepted | 09.09.2021 | 23.05.2023
39 | Site Assembling series | 21.09.2021 | 27.06.2023
40 | SAT Series | 22.10.2021 | 04.07.2023
40 | SAT accepted | 22.10.2021 | 04.07.2023