## Slide 1: NSQ Magnet for CR. CDR Review.
D. Gurov, A.Utkin for CR team
BINP, Novosibirsk
November 27, 2019
3rd FAIR-BINP Workshop, Novosibirsk, Russia

## Slide 2: Contents
CDR documentation
Project management structure
Base principles and Concept
NSQ quadrupoles in CR
Calculations and simulations
Assembling
Production plan

## Slide 3: CDR Documentations
Test plan
https://edms.cern.ch/document/2245947/1
Mechanics - 3D model
https://edms.cern.ch/document/2245951/1
Operating manual / user manual https://edms.cern.ch/document/2245945/1
Risk analysis and hazard analysis [AID:0002663]
https://edms.cern.ch/document/2245943/1

## Slide 4: Project management
Name: Denis Gurov
Position: Research Scientist Email: D.S.Gurov@inp.nsk.su
Tel.: +7383329-4684
The Deputy is responsible for:
Follow-up of production activities;
Magnetic measurements to ensure the required field and field quality;
Factory Acceptance Test (FAT) to verify the given specifications of the components;
Name: Anatoly Utkin
Position: Research Scientist Email: A.V.Utkin@inp.nsk.su
Tel.: +7383329-4684
The Deputy is responsible for:
Preliminary magnet design, final magnet design (development, simulation);
Magnetic field calculation;
More Details in “Quality Plan”
The Project Manager
Name: Alexandr Starostenko
Position: Head of BINP Division № 5-11 Email: A.A.Starostenko@inp.nsk.su
Tel.: +7383329-4940
The Project Manager is responsible for:
Development of the technical documentation and manufacturing drawings for the deliverables;
Ensuring that the production of the magnets is according to the technical specifications and time schedule;
Follow-up of production activities;
Transportation, delivery of the equipment to the FAIR site;
Regular and timely reporting on progress and problems;
Timely conduction/participation of reviews and provisions of feedback;
Scientific Design Department
Name: Vladimir Korchagin
Position: Principal Design Engineer Email: V.Ya.Korchagin@inp.nsk.su
Tel.: + 7383329-4953
The Principal Design Engineer is responsible for:
Magnet design (3D-models, production drawings);

## Slide 5: Construction of NSQ magnet

## Slide 6: Construction of NSQ magnet
19 turns coil 17x17 mm. wire
7 mm. hole
Quarter of yoke

## Slide 7: NQ Quadrupole and stand for quadrupole
Parameter | Value
Lamination thickness | 1 mm
Dimensions of wire for coils | 17x17 mm
Number of NSQ magnets | 1
Overall weight | 2.0 t
Coil current | 1210 A
Number of coil turns | 19
Coil resistance | 10.1 m
Coil inductance | 9 mH
Maximum DC power loss | 14.8 kW

## Slide 8: NSQ Quadrupole top wiew and yoke

## Slide 9: NQ magnet calculations
3D Magneto-static calculations in “Mermaid” code
Pole profile coordinates (mm)
Pole profile
Chamfer 12 mm depth 12 mm height, side cut outs 15 mm depth 10 mm width
Chart: 
| 69.86 | 32 | 32 | 39.369999999999997 | 39.459973494245581 | 40.746250258394497 | 42.119210160709855 | 43.587921211903975 | 45.16276193919817 | 46.855667006823374 | 48.680430229696626 | 50.65308126026418 | 52.792357729040191 | 55.120302302885605 | 57.663024998582166 | 60.451686695484717 | 63.523782535104097 | 66.924837598971465 | 70.710678118654741 | 74.710678118654741 | 78.710678118654741 | 82.710678118654741 | 86.710678118654741 | 90.710678118654741 | 94.710678118654741 | 98.710678118654741 | 102.71067811865474 | 106.71067811865474 | 110.71067811865474 | 114.71067811865474 | 118.71067811865474 | 122.71067811865474 | 126.71067811865474 | 127 | 141.6 | 145.6 | 211.28
 | 211.28 | 145.6 | 141.6 | 127 | 126.7107 | 122.7107 | 118.7107 | 114.7107 | 110.7107 | 106.7107 | 102.7107 | 98.7107 | 94.7107 | 90.7107 | 86.7107 | 82.7107 | 78.7107 | 74.7107 | 70.7107 | 66.9248 | 63.5238 | 60.4517 | 57.663 | 55.1203 | 52.7924 | 50.6531 | 48.6804 | 46.8557 | 45.1628 | 43.5879 | 42.1192 | 40.7463 | 39.46 | 39.37 | 32 | 32 | 69.86
Y (mm) | X (mm)
287.16 | 145.74
211.28 | 69.86
145.6 | 32
141.6 | 32
127 | 39.37
Hyperbola: | X*Y=5000
39.37 | 127
32 | 141.6
32 | 145.6
69.86 | 211.28
145.74 | 287.16

## Slide 10: Field in yoke
Field in yoke (kGs) at maximal gradient value
Flux lines in yoke at maximal gradient value

## Slide 11: Field quality
kGs/cm
Integral contributions of 6th and 10th multipoles at 136 mm radius.
Longitudinal gradient distribution at maximal gradient value.
cm
Chart: 6 and 10 harmonics at diferent gradient magnitudes
| 3.2069928141176471 | 2.5145325935294118 | 1.8177560770588237 | 1.1168831135294117 | 0.4158513317647059
A6/A2 | -0.00014331 | 7.9341e-05 | 0.00021633 | 0.00026411 | 0.00025016
A10/A2 | -6.9274e-05 | -4.0912e-05 | -2.0221e-05 | -1.4075e-05 | -1.3342e-05

## Slide 12: Assembling of the magnet
1. Fasten the alignment feet 1 (3 pcs.) to the lower half of the yoke 2 (1 pcs.), using bolts 3 (18 pcs.);
2. Fasten stainless steel spacers 29 (2 pcs.) to the lower half of the yoke 2 using bolts 7 (12 pcs.);
3. Install the lower half of the yoke of the NSQ quadrupole on the stand 4 (1 pcs.) (alignment feet must be properly fastened to a stand using bolts 5 (12 pcs.) to prevent any fall);
4. Install the vacuum chamber on the lower half of the NSQ quadrupole;
5. Install the upper half of the yoke of the NSQ quadrupole 6 (1 pcs.) on the lower half of the NSQ quadrupole and fasten to each other using bolts 7 (12 pcs.);
6. Fasten stainless steel brackets 30 (4 pcs.) using bolts 31 (24 pcs.) to increase mechanical rigidity;
7. Install the manifolds 8 (2 pcs.) on the side of the magnet on the brackets 9 (2 pcs.) using the mounting blocks 10 (4 pcs.) with the bolts 11 (8 pcs.);
8. Connect the lower and upper half of the manifolds using bolts 28 (4 pcs.);
9. Install the connection boxes 12 (2 pcs.);

## Slide 13: Assembling of the magnet
10. Assemble the connection boxes 12:
10.1. Install the cable connection plates 13 (2 pcs.) using the mounting blocks 14 using the fastening plates 15 with the bolts 16 (4 pcs.);
10.2. Connect the upper and lower windings using the midpoint connection plate 17 (1 pcs.) with the bolts 18 (8 pcs.);
10.3. Connect the cable connection plates 13 (2 pcs.) with the beginning and end of the upper and lower windings with the bolts 20 (8 pcs.);
10.4. Fix the outlets of the sections of the windings using the mounting blocks 21 using the fastening plates 22 with the bolts 23 (4 pcs.);
11. Connect the water hoses 24 (8 pcs.) to the fittings 25, fix with the clamps 26 (16 pcs.).

## Slide 14: Production Plan
NSQ production plan
Month | Activity | Begin | End
0 | Contract is signed | 26.06.2018 | 26.06.2018
8 | Tecnological design, Equipment design | 25.02.2019 | 29.11.2019
14 | Conceptual Design Review | 16.08.2019 | 16.08.2019
15 | Design in detail | 19.09.2019 | 21.09.2019
16 | Final Design Review | 07.11.2019 | 07.11.2019
17 | Material procurement | 20.11.2019 | 30.01.2020
24 | Tooling manufacturing | 17.06.2020 | 25.10.2020
28 | Manufacturing of pre-series | 28.10.2020 | 28.12.2020
30 | FAT of pre-series | 28.12.2020 | 25.02.2021
32 | Shipment of pre-series to FAIR | 02.03.2021 | 24.03.2021
33 | SAT A of pre-series | 07.04.2021 | 19.05.2021
33 | Manufacturing of series | none | none
33 | Prepare series production | none | none
33 | Series production started | none | none
33 | FAT accepted | none | none
41 | Site Assembling series | 20.11.2021 | 03.04.2022
42 | SAT Series | 21.12.2021 | 30.05.2022
43 | SAT accepted | 20.01.2022 | 08.08.2022