## Slide 1
Installation procedure of the Magnet into the Iron Yoke

## Slide 2
Magnet assembly procedure
For installation of the Magnet into the Yoke it is possible to use an I-beam steel 70B2 (697 x 260 mm) GOST 26020-83. The length of the beam is L = 9 m.
To roll inside, we can use rollers that are used to open doors (Roller skate Boerkey model AM-H)
Rail

## Slide 3
Installation procedure of the Magnet into the Iron Yoke
Tooling for installation of the Magnet into the Iron Yoke.
Removable Support
Fixed Support
Beam (1.6t)
Central removable Support
Support for Magnet
Rollers system

## Slide 4
Installation procedure of the Magnet into the Iron Yoke
Preparation of the tooling for moving of the magnet: installation of fixed and removable support, support for magnet and beam.
RAMAZI RAMAZI
Yoke
(the doors are opened)
Magnet on the transport frame

## Slide 5
Installation procedure of the Magnet into the Iron Yoke
Remove left support and install the magnet with transport frame on the support of magnet.
Central removable Support
Support for Magnet
Magnet on the transport frame

## Slide 6
Installation procedure of the Magnet into the Iron Yoke
Insert removable support and install the rollers system for moving magnet.
Removable Support
Rollers system

## Slide 7
Installation procedure of the Magnet into the Iron Yoke
Remove the magnet fixation on the transport frame and move the support of magnet with transport frame down.
Support for Magnet

## Slide 8
Installation procedure of the Magnet into the Iron Yoke
Front view
Gap 15…20 mm

## Slide 9
Installation procedure of the Magnet into the Iron Yoke
Remove the central support, install and align of the Magnet into the yoke.

## Slide 10
Installation of the Control Dewar.
Install and connect of the Control Dewar with the magnet by a transfer line.

## Slide 11
Installation of the Control Dewar.
Magnet with Control Dewar.

## Slide 12
Power supply of PANDA Magnet.
Сonnection of the Control Dewar with the Power supply system.

## Slide 13: Thank you for your attention!