## Slide 1: STT BEAmdata analysis and inputs to simulation
06.11.19 I Gabriela pérez andrade
Panda collaboration meeting
Tracking session

## Slide 2: Outline
Calibration/tracking
Global calibration
Investigation of straws efficiency
Inputs to simulation
1

## Slide 3: CALIBRATION AND TRACKING
  Isochrone parametrization
  Track Pre-fit from wire positions of straws with hits
  calculation for each hit
  Residual definition:
  Use of 2- MINUIT function to reduce distance from isochrones
  to fitted track.
  Single outliers rejection:
        Condition in , (e.g. > 900 µm).
Radial distance (mm)
Straw channel no.
All channels drift time (ns)
Beam
Drift time (ns)
2

## Slide 4
TRACKING RESOLUTION
Expected residual distribution around .
Shifted mean indicates systematic error caused by wire misplacement i.e. channel dependent.
Correction through :
= + , where refers to tracks above and below the wire respectively
Re-fit with (iterative procedure).
Hit resolution given by fit to residuals distribution (σ).
Protons 2.5 Gev/c initial
Protons 2.5 Gev/c iteration 10
σ = 121 µm
µ = -1 µm
= 191 µm
µ = -60 µm
Residuals [µm]
Residuals [µm]
Channel number
Channel number
3

## Slide 5
TRACKING RESOLUTION
At ~ 6 iterations, the resolution value stabilizes.
After value stabilizes, the resolution value difference is of ~2 µm between iterations
Final resolution in general is < 130 µm
Hit resolution better than design goal (i.e. 150 µm) after a few iterations.
Systematic error correction further improves hit resolution.
4

## Slide 6: rEMARKS
Calibration and tracking (iterations) are performed for each dataset :
  Results are slightly biased.
  Isochrone parametrization and systematic error correction should be performed only once.
  Information such as particle momenta will not be available in the experiment i.e. method should be dE/dx independet.
  An approach for a global calibration has been tested in 3 proton and 3 deuteron beam datasets at different beam momenta.
5

## Slide 7: Global calibration
A global dataset is chosen based on uniform illumination.
Parameters from calibration and giving optimal hit resolution are obtained, i.e.
    Isochrone parametrization
    correction
Output parameters from calibration and tracking are used as input for other datasets of same particle specie.
Compare hit resolution and residual shift correction.
6

## Slide 8: Preliminary results
Global calibration, hit resolution
Global calibration/tracking parameters result on a difference of < 5 µm with own calibration/tracking parameters.
7

## Slide 9: Channel RESIDUAL comparison
Proton beam 2.5 GeV/c
Mean residual stay mostly within a window of 30 µm for tracks above the wire.
Difference in mean residuals can be attributed to hit-map differences.
Mean residual, tracks below the wire
Mean residual, tracks above the wire
8

## Slide 10
Global isochrone parametrization.
Perform tracking using specific straw areas.
Test tracking performance in blocked straws:
    Obtain hit resolution
    Retrieve straw radii.
    Obtain wire misplacement information from
Investigation of Straws efficiency (un-biased)
Time [ns]
[m]
9

## Slide 11: Inputs to Simulation (hit digitization)
Information extracted from experimental data can be used to benefit some simulation features for tracking:
Driftime-Isochrone:
    Isochrone uncertainity.
    Hit resolution.
Time over Threshold (ToT) characterization to:
    Obtain information about hit multiplicity.
    Use as criterion for hit filtering (δ-electrons).
    Use as PID observable.
Drift time [ns]
ToT [ns]
Straw signals
10

## Slide 12: Summary and outlook
Calibration and tracking iterations introduce a slight bias in hit resolution and systematic error correction.
Hit resolution using global calibration and tracking parameters show a difference of < 5 µm from own calibration/tracking (preliminary tests). Residual shift stay mostly within a window of 30 µm (preliminary tests).
Straw properties (e.g. radius, wire misplacement) can be investigated if tracking is performed using a reduced amount of straws.
Available data could provide with useful information for simulation parameters.
11

## Slide 13
THANK YOU!

## Slide 14: Channel RESIDUAL comparison
Mean residual, tracks above the wire
Mean residual, tracks below the wire
Proton beam 0.55 GeV/c
Residual shift stay mostly within a window of 30 µm

## Slide 15: Channel RESIDUAL comparison
Mean residual, tracks below wire
Mean residual, tracks above wire
Deuteron beam 0.60 GeV/c
Hits per channel, Deuterons 1.5 GeV/c (Global sample)