## Slide 1: and HITRAP
Frank Herfurth
CRYRING@ESR
December-17, 2019
CRYRING@ESR
  ECooler
    leak in isolation vacuum
    next test fill after the fix in Jan.
  Major vacuum incident on Nov-23 vented 7 out of 8 sections
    Post mortem report (link), later found that the cryopump at the E Gun is broken (due to the vent or the bake out) – to be fixed in Jan.
    UHV + Ring operation reestablished by Dec-10. Ready for ESR beam
  Ring Operation/Test
    stored D+ @ 5 MeV/u for 1000 s (with only little losses) – life time beyond 6000 s
    injection kicker tested successfully with beam
    extraction kicker tested, beam disappears, extraction section BI not available
HITRAP
  EBIT run for B3+ laser spectroscopy conducted by TUDA colleagues ended
  started removing the faulty MPS (multi passage spectrometer/ beam switch)
1000 s

## Slide 2: and HITRAP
Frank Herfurth
CRYRING@ESR
Januar-07, 2020
CRYRING@ESR
  Summary of engineering run and Status for Experiments
    stored Ar18+ @ 13 MeV/u – life time about 600 s
    required 14 shift with ESR beam (Machine Meeting in June)
      got less than 2 shifts
    did not measure life time for heavier, highly charged ions
    we have almost no control on the beam setup quality (tuning/optimization)
      To set one new value for the coupled ESR – CRYRING pattern requires at least 1 min, but usually 3 to 6 min.
      this yields less than 10 different values per hour
  Experiments at CRYRING@ESR will be extremely challenging
1000 s
PAC Experiments in 2020 expect:
  136Xe50+, 238U88+ and 238U91+ @ about 10 MeV/u, 107 (/ minute)
  cooled!