## Slide 1: The Linac Coherent Light Source (LCLS) Free Electron Laser (FEL) Performance Program
William S. Colocho, WAO, October 2014
With focus on Reproducibility.

## Slide 2: Outline
  LCLS FEL at a glance.
  Time Accounting
  FEL Performance program
  Reproducibility issues
  Future Work
  Questions

## Slide 3: Linac Coherent Light Source – Free Electron Laser
The LCLS is the world’s most powerful X-ray laser. Its highly focused beam, which arrives in bursts a few to ~120 femtoseconds long, allows researchers to probe complex, ultra-small structures and freeze atomic motions, thus shedding light on fundamental processes of chemistry, materials and energy science, technology and life itself.

## Slide 4: The LCLS Operation Strategy
Capacity
  Increase the experimental capacity of LCLS by performing simultaneous experiments via beam splitting and sharing methods
Capability
  Develop new capabilities such as pulse control and
  characterization, detection and control systems, sample environment and delivery
Efficiency
  Transition LCLS operations from the “start-up” phase to a more efficient sustainable mode that is scalable to LCLS-II
Uwe Bergmann

## Slide 5
Capacity is the Major Limitation for LCLS
Chart: # of Proposals Received
| Run 1 2088 hrs | Run 2 2256 hrs | Run 3 2184 hrs | Run 4 2256 hrs | Run 5 2772 hrs | Run 6 2388 hrs | Run 7 3120 hrs | Run 8 2700 hrs | Run 9 2280 hrs
Proposals Received | 28 | 62 | 107 | 116 | 114 | 134 | 152 | 175 | 194
% Propsals Scheduled | 0.39286 | 0.37097 | 0.23364 | 0.22414 | 0.25439 | 0.24627 | 0.26974 | 0.2 | 0.18557
October 2009 August 2014
Uwe Bergmann

## Slide 6: Increase LCLS Capacity by Beam Sharing
  Successful demonstration of two simultaneous experiments XPP/CXI during in-house research
  3 user experiment performed in Run 8, first one at XPP/MEC
  7 user experiments performed in Run 9 resulting in 20% more user time
  Second set of diamond crystals for the XCS mono underway
  Work underway at CXI to use the beam for two back-to-back experiments
  In the process to attract funding for a new Hutch
100 µm thick diamond crystal
Mirror for MEC

## Slide 7: Time accounting
Chart: 
| Users | Machine Dev. | Photon MD | Off
Scheduled | 0.54606 | 0.23276 | 0.03593 | 0.18525
Chart: 
| Users | Machine Dev. | Photon MD
Availability | 0.94965 | 0.88435 | 0.90532
Reliability | 0.96386 | 0.91954 | 0.93805
LCLS User runs are planned for 10/12 months each calendar year.
Each week of a run includes on average 5 days for User experiments and 2 days for Non-User time.
Time spent tuning is counted an un-available to Users.
MD Reliability is lower by 4.4%! We shift maintenance tasking risk to Machine Development periods.

## Slide 8: Non-User Time Scheduling
Setup: Setup FEL for User specified parameters (Wavelength, pulse intensity, bunch length, etc.)
Maintenance: tune-up of energized equipment, injector laser tuning and software releases.
Performance Programs:
Capability: Develop new FEL capabilities that align with changing user interests and future needs.
Stability: Improve jitter.
Reproducibility: Reduce setup and tuning time
Quality: Achieve higher FEL beam parameter values
Photon: Develop or commission common x-ray beam lines.
https://portal.slac.stanford.edu/sites/lclscore_public/Pages/FEL-Performance-Programs.aspx

## Slide 9: Reproducibility
Pulse intensity reproducibility target is to achieve 75% of previously attained performance by restoring control devise configuration.
Pulse intensity is dependent on many other configuration factors including photon wavelength (e- energy) and photon bunch length (e- peak current).

## Slide 10: Reproducibility topics
Injector Laser profile on VCC
Laser heater 3D overlap
Gun Amplitude
L1X orbit offset
L2/L3 RF gain stability
BC2 dispersion
LTU emittance growth
Lateral drift motion of LTU QUAD(s).
Undulator launch orbit
Undulator K degradation.
SASE gain disturbances across undulator chicanes.
UND chicane phase.
Injector QUADs BBA.
Operations – Physicist communication.
Large parameter optimization space.
Large number of configurations
Opportunistic measurements.
4:15 meeting requests seems late.
Multiple optimization algorithms.
Lattice and orbit control.
Orbit control and feedback
Magnetic filed reproducibility. (LTU PS)
Coupling

## Slide 11: Reproducibility examples – Injector Laser Profile
Operators on shift identified FEL pulse intensity to be extremely sensitive to injector laser profile
Save profile and try to visually reproduce.
Ways to quantify, track, correlate and monitor profile needed.
Zernike polynomials may help.
Use symmetric/anti-symmetric coefficient (2 values).
R&D to use adaptive optics.
Individual coefficients change with time

## Slide 12: Machine Characterization.
Each operating point includes parameters selected by Users: 280 eV to 11.2 KeV, 20 pC to 180pC, 10 fs to ~120 fs).
This leads to a large number of different configurations with different intrinsic performance.
Machine characterization takes time. Must work hard at automating and speeding up measurements – Fast wire scanners.
Expert only measurements adapted for operator use.
Develop non invasive ways to monitor parameters.

## Slide 13: Machine Characterization
Opportunistic during hutch access
Users and hutch scientists may be suspicious of “Non-Invasive” measurements
Hutch access time may not be known or predictable
Operators may prefer to tune or keep beam stable rather than to embark in measurement program
Measurement procedure(s) not well documented.
No value added to current shift.

## Slide 14: Multiple Optimization Algorithms
Large number of knobs leads to individual optimization approaches.
Physics based “By the book” tune up algorithm has proven to work BUT not all the time.
Minimizing beam emittance is a necessary but not sufficient condition for good performance.
Multiple iterations needed
Pulse I vs emit

## Slide 15: Operations – Physicist communication.
Operations find improved performance from changing parameters that Physicist would expect to set once. (XCAV transverse offset, Hard X-Ray Self Seeding chicane delay)
Easy to get lost in parameter space.
Parameter drift may be caused by hardware issue (Gun Solenoid tweaks due to Gun Amplitude probe issues).
Two logbook systems, multiple programs lead to information overflow
Other activities in the control room require operator attention. (Multi-program operation: FACET, ESTB, SSRL)

## Slide 16: Other tuning aids, ideas and issues
“Tunagedon” Operator written GUI to automate common tuning tasks
Jitter interferes with tuning efficiency.
Drift interferes with tuning efficiency.
Robust Conjugate Direction Search (RCDS)* has been explored.

## Slide 17: RCDS
Each evaluation took 10.5 seconds on average (mostly waiting for undulator).
* X. Huang, et al, NIMA 726 (2013) 77-83

## Slide 18: Summary
Accurate time accounting identifies areas of improvement.
New FEL performance program guides schedule.
Reproducibility is tracked at multiple levels and is a key performance indicator for an FEL X-Ray source
A strong parameter characterization program is needed
Good coumnication between Operators and Physicists is a requirement for Reproducibility issues.
Improving machine Reproducibility will decrease setup time and increase machine’s Capacity and Efficiency.

## Slide 19: Questions

## Slide 20: Back up slides: Optimization knobs
Injector laser profile
Injector phase scans
Injector orbit steering
Laser Heater timing, transverse profile, intensity (mJ).
Orbit at X-Cavity linearizer.
Undulator Taper
SXRSS and HXRSS phase delay.
Undulator orbit launch
Linac betatron matching quads
LTU betatron matching quads
Linac energy gain configuration
Linac steering
LTU steering
Gun solenoid
BC1/BC2/BL2 dispersion correction
Collimator positions
Bunch compression BC1/BC2
L3 Vernier
L3 chirp
electron charge
Undulator pointing

## Slide 21: Room Temperature Structure of GPCRs
  - Human serotonin receptor refined to 2.8 Å
  - Average crystal size
    LCLS 5x5x5 mm3
    Synchrotron 80x20x10 mm3
    Only 0.3 mg of protein used at LCLS
  - RT structure displays a unique distribution of
  thermal motions and conformations of residues
   More accurate receptor structure and
  dynamics in a cellular environment
  -
Lipidic Cubic Phase Jet
Weierstall et al. (2014)
Liu et al. Science (2013)
Team led by Cherezov
LCLS (red) vs Synchrotron (blue)

## Slide 22: FEL Performance Program Examples
Quality: Seeding Lines, Optics Studies
Capability: Soft X-Ray Self Seeding.
Photon: LODCM for beam sharing
Stability: Jitter diagnostics