## Slide 1: THE DIGITAL REVOLUTION
Notes: The Digital or 3rd industrial revolution started in the 50th of the last century with the invention of digital logic circuits. Moor's law predicted, that the performance of these circuits doubles every 18 month. That turned out to be fairly accurate and by the turn of the century digital circuits were replacing analogue electronics everywhere, and of course as well in accelerators: the SLS was commissioned in 2001 with a distributed control system, a digital beam position monitor system and Fast Orbit Feedback and even with digital regulated magnet power supplies.
Why? Because it was cheaper to develop and build this high performance equipment with digital circuit technology, and it promised much short development cycles, higher flexibility and better reproducibility. But at the very same time we still had analogue cables going from the accelerator into the control room, to be used there with Oscilloscopes and Spectrum Analysers, and with patch panels in the machine hall to connect them to different signal sources. And we are talking about expensive cables here: if you want to transport high bandwidth signals over 50 to 100 m, then you have to pay good for that.
Wasn’t that already old-fashioned then? Well, it was mainly argued, that we would need these cables for flexibility: you can connect whatever you want and investigate the signal in the control room, once you figured out what you need to investigate. In my personal opinion the main reason was, that in case of uncertainties you prefer to stick to proven technology from your own past.
Just a few years after the successful commissioning of the SLS we merged the operation groups and the control rooms of the three PSI accelerator facilities: the high intensity proton accelerator, the medical proton cyclotron PROSCAN and the Swiss Light Source.
The common control room was 500 m away from the SLS: suddenly analogue cables were no option anymore.

## Slide 2: Paul Scherrer Institut
PSI,
The fully digital PSI accelerator control room
Andreas Luedeke
Notes: Today I'll talk about the new common PSI accelerator control room, in operation since 2007.
I'm convinced that analogue cables in the control did had their time, but this time is really over.

## Slide 3: Paul Scherrer Institut
SLS
HIPA
Proscan
Control
Room
SwissFEL

## Slide 4: The original Control Room of the SLS (2000)

## Slide 5: The SLS Corner in the HIPA Control Room (2003)

## Slide 6: The new PSI Common Control Room (2007)
SLS
HIPA
SwissFEL
Proscan

## Slide 7: Combined Control Room → Combined Operation Crew
Each operator knows all accelerators!
  Easier roster
  Saves staff costs
Risks:
  Loss of knowledge
  Less dedication
  New demands on operator interfaces
  Operation must become simpler

## Slide 8: How to train one operators on three facilities?
Formal training
Dedicated beam time for hands-on training
Presentation tomorrow:
  How to get to best practices for operator training?

## Slide 9: SLS Video and Analogue Signals
Analogue Cameras
  Fluorescence Screens
  Synchrotron Radiation Monitors
  In old control room: video multiplexer
  Add remote control
  Add “Keyboard-Video-Mouse” (KVM) extender for two monitors
  Optical fibres to new control room
Analogue signals
  Rarely used
  Old patch panel moved
    Local Oscilloscope
    Local Spectrum Analyser
    KVM extender again

## Slide 10: What you should do instead…
Use digital cameras + dedicated network → SwissFEL
Embed control system on Oscilloscopes → SwissFEL & SLS Beamlines
or even better: use fast ADCs instead with dedicated applications
System is rarely ever used
  Fluorescence screens or sync. rad. monitors rarely used
  Oscilloscope and Spectrum Analyser rarely used
  New synchrotron monitors have digital cameras
Newer diagnostics all use digital signal processing

## Slide 11: Conclusion
PSI,
Our control room is based on 9 year old solutions.
Meanwhile digital circuits got 64 times more powerful!
Today: digitize at the source.
Andreas Lüdeke at the ARW13 in Melbourne