## Slide 1
M.Pont, ALBA-CELLS
WAO’2014
26-31/10/2014
A Common Operation Metrics for
3rd Generation Light Sources

## Slide 2: Comparison of Light Sources
80%
90%
100%
110%
Beam Availability
2005
2006
2007
2008
2009
2010
Year
A. Luedeke, ‘Do you believe in Operation Statistics?, ARW11, Cape Town

## Slide 3: Survey on Failure Analysis at Light Sources
How do you exactly define “beam downtime”?
How do you exactly define “beam availability”?
Result of the survey:
No two facilities were calculating “beam availability” in the same way!
Some examples:
  Downtime: often defined in common sense rules
  Short up-time: some did count every up-time, some dismiss up-times up to 1 hour
  Compensation time: some subtract it from downtime, some not
“Beam availability”: shows reliability of one facility over time; BUT
comparison of numbers from different facilities is meaningless!!!
A. Luedeke, Phys. Rev. ST Accel. Beams 12, 024701 (2009)
Previous experience

## Slide 4: Starting point: “Beam availability”
Talk of Andreas Lüdeke: Find your "Happy User Index“
Every type of machine has it’s own figure of merit.
Common metrics to compare facilities (Beam availability, MTBF, MTTR)
Specific metrics to optimize your facility (quantify user demands)
Open Discussion:
Do we have a common way to calculate beam availability?
There were 12 representatives from different light sources present.
Conclusion: No, we don’t!

## Slide 5: Starting point: “Beam availability”
Examples:
When does a downtime start?
  < 99% of nominal beam current (e.g. SPEAR3)
  < 50% of nominal beam current (e.g. ELETTRA, Diamond)
  no beam (e.g. ALBA)
When does a downtime end?
  Nominal beam current is restored (e.g. Australian Synchrotron)
  Beam is given to the users (e.g. ALBA, SLS)
  Penalty time added after beam is back (e.g. ELETTRA: +15min, PETRA III: +1h)

## Slide 6
Starting point: “Beam availability”
Conclusion:
We need a world wide common standard on accelerator reliability!
We’ve started the initiative for:
A Common Operation Metrics for 3rd Generation Light Sources

## Slide 7: How to define this Standard?
Redefine “downtime” and “beam availability”?
No, that would not work:
  Risk of ambiguity (old and new definitions)
  Risk of resistance (Availability numbers can be part of contracts)
  Too simple to be meaningful (Downtime has many modes)
Instead start with a list of common failure modes

## Slide 8: Primary Failure Modes
Time
Beam-
current
“No-beam”
“Low-beam-current”
I(nom)
20% I(nom)
I(min)
99.5% I(min)
No-beam
Low-beam-current

## Slide 9: Secondary Failure Modes
Define a set of secondary failure modes
Low lifetime
Beam blow-up
Distorted Orbit
Distorted Bunch Timing
Bunch Impurity
Beam Feedback Outages
Short Uptime
Beam unrelated Outages (Network,…)
…
Number and total duration of failure modes answers:
Is our orbit feedback system as reliable as those of other facilities?
How reliable is our top-up mode compared to other light sources?
Is our beam size fluctuation normal?
…

## Slide 10: User Time
Scheduled User Experiment Time (users scheduled > 1 month ago)
Scheduled User Reserve Time (user re-scheduled ≥ 1 month ago)
Spontaneous User Compensation Time (user re-scheduled < 1 month ago)
The sum of all the above is the User Time
Example: Vacuum leak, 5 days lost
  Management decision:
    5 days shutdown for repair,
    next service week shortened by 5 days,
    these 5 days given to users
  Accounting:
    “No beam” event of 5 days
    5 days “Spontaneous User Compensation Time”
    This adds 5 days to the “User Time”

## Slide 11: Failure Mode Statistics: what to publish?
Publish for each failure mode:
  Failure count
  Total duration
Publish user schedule statistics:
  𝑇𝑆𝑐ℎ𝑒𝑑𝑢𝑙𝑒𝑑
  𝑇𝑅𝑒𝑠𝑒𝑟𝑣𝑒
  𝑇𝐶𝑜𝑚𝑝𝑒𝑛𝑠𝑎𝑡𝑖𝑜𝑛
  𝑇𝑈𝑠𝑒𝑟= 𝑇𝑆𝑐ℎ𝑒𝑑𝑢𝑙𝑒𝑑 + 𝑇𝑅𝑒𝑠𝑒𝑟𝑣𝑒 + 𝑇𝐶𝑜𝑚𝑝𝑒𝑛𝑠𝑎𝑡𝑖𝑜n

## Slide 12: Failure Mode Statistics: how to use it?
Simple beam availability:
Compensated beam availability:
Mean Time Between Distortions:

## Slide 13: Example
In the operations calendar for 2014:
Tscheduled: 4800 h Treserve: 72 h Tcompensation: 0 h
At the end of the year
Toutages: 80 h + 3 full days due to a main PS failure Toutages: 152 h
Treserve is fully used
In addition Management decides to extend the last run for 1d, that is Tcompensation: 24 h

## Slide 14: Example
To compare to other facilities
Internal use: Did all users get their beamtime?

## Slide 15: Summary
We propose a simple, distinct and standardized operation metrics:
  Primary failure modes: clearly defined, easy to measure
  Secondary failure modes: work-in-progress
  Defined accounting for user schedule statistics
Only such a standard allows a meaningful comparison
of the reliability of 3rd generation light sources!

## Slide 16: Acknowledgements
Many thanks for input to this talk go to:
Michael Bieler, Petra III at DESY
Jean-François Lamarre, SOLEIL
Andreas Lüdeke, SLS at PSI

## Slide 17: Contacts
Michael Bieler for PETRA 3 at DESY,
Ruy Hanazaki do Amaral Farias for Sirius at LNLS,
Laurent Hardy for the ESRF,
Stefano Krecic for Elettra,
Jean-François Lamarre for SOLEIL,
Andreas Lüdeke for the SLS at PSI,
Roland Müller for BESSY2 at HZB
Montse Pont for ALBA at CELLS
Mailing List of this initiative:

## Slide 18
Visit us at http://sites.google.com/site/comi3gls
Contacts