## Slide 1: Operation Progress and Upgrade in SSRF
Qinglei ZHANG
On behalf of Wenzhi ZHANG
Oct. 27, 2014
Mainz/Germany

## Slide 2
Brief Introduction
Operation Statistics
Accelerator Improvement
New Beamlines Commissioning
Summary
Outline

## Slide 3: Outline
Brief Introduction
Operation Statistics
Accelerator Improvement
New Beamlines Commissioning
Summary

## Slide 4
Dec. 2004 Ground break
Oct. 2007 Commission
May 2009 Open to users
Dec. 2012 Top up operation
Beam lines in Operation
  7 Beamlines have been open to users since May 2009
  6 Beamlines are ready to users
  1 Dreamline is under commissioning
History

## Slide 5: Overview

## Slide 6: Beam Parameters
Parameter / unit | Design value | Operation
Beam energy / GeV | 3.50 | 3.50±0.02
Beam current / mA | 200~300 | 240 (operation current) 300 (achievable)
Tune (H, V) | 22.22, 11.29 | 22.220, 11.290 (±0.002)
Natural emittance / nm.rad | 3.89 | 3.8±0.2
Coupling | 1% | 0.6% (0.1%)
Natural chromaticity (H, V) | -55.7, -17.9 | -50, -15 (direct measurement)
Corrected chromaticity (H, V) | --------- | 1.5, 0.5
RMS energy spread | 9.845×10-4 | 0.001
Energy loss per turn / MeV | 1.435 | ~1.45 (without ID, from RF power)
Momentum compaction factor | 4.27×10-4 | (4.2±0.2)×10-4
RF voltage / MV | 4.0 | 1.51, 1.55, 1.54 (Three cavities)
RF frequency / MHz | 499.654 | 499.654 (depend on machine conditions)
Synchrotron frequency | 0.0072 (VRF=4.0MV) | 0.0075±0.0002
Natural bunch length / ps | 13 | 14±2
Injection efficiency | --------- | >95% (from BS DCCT to SR DCCT)
Beam lifetime / hrs | >10 | ~20 (0.6% coupling, 240mA)

## Slide 7: Website http://159.226.222.249/ssrf/beam/

## Slide 8
Brief Introduction
Operation Statistics
Accelerator Improvement
New Beamlines Commissioning
Summary
Outline

## Slide 9: Operation time schedule
Year | Total | User | Beamline | AP | Maintenance
2010 | 7319 | 4003 | 1702 | 1330 | 284
2011 | 7356 | 4476 | 1130 | 1280 | 470
2012 | 6696 | 4610 | 856 | 960 | 270
2013 | 7272 | 4608 | 1488 | 912 | 264
Total | 28643 | 17697 | 5176 | 4482 | 1288
Chart: 
| user | beamline | AP | maintenance
 | 17697 | 5176 | 4482 | 1288

## Slide 10
Chart: 
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 - H1
Availability | 0.9456 | 0.9569 | 0.976 | 0.9836 | 0.9813 | 0.99



MTBF(hrs) | 28.3 | 42.1 | 55.3 | 69.8 | 70.28 | 78.71
MDT(hrs) | 1.65 | 1.89 | 1.37 | 1.19 | 1.36 | 0.82
Reliability performance

## Slide 11: New record of continuous light delivery
light delivery
without break
for 312hr
Maintenance
Maintenance
trip
trip
light delivery
without trip
for 551hr

## Slide 12: Hardware faults distribution
Chart: Hours distribution of machine breakdown in SSRF (2009.5-2013.11)
Chart: Hours distribution of machine breakdown in SSRF (2009.5-2013.11)
| RF | power supply | linac | beam diagnosis | timing | control | injection | vaccum | utility | beamline | operation | cryogenic | technology | safty | magnet | others
 | 308.29 | 83.46 | 24.4 | 30.32 | 3 | 13.02 | 70.86 | 18.25 | 73.15 | 43.39 | 30.47 | 23.6 | 13.85 | 17.73 | 0 | 62.28

## Slide 13: Hardware faults trend
Chart: Hours distribution of machine breakdown in SSRF (2009.5-2013.11)
Chart: Hours distribution of machine breakdown in SSRF (2009.5-2013.11)
Chart: Trend of breakdown hours
| 2009.9 -2010.7 | 2010.9 -2011.7 | 2011.9 -2012.7 | 2012.9 -2013.7 | 2013.9 -2014.7
RF | 95.6 | 102.4 | 24.37 | 92.56 | 40.36
PS | 26.1 | 11.85 | 41.41 | 12.7 | 27.76
Inj. | 5.6 | 37.05 | 3.3 | 11.81 | 3.6
Cryo. | 29.6 | 37.85 | 42.35 | 8 | 0
Chart: Trend of breakdown times
| 2009.9 -2010.7 | 2010.9 -2011.7 | 2011.9 -2012.7 | 2012.9 -2013.7 | 2013.9 -2014.7
RF | 120 | 82 | 27 | 56 | 45
PS | 15 | 6 | 25 | 5 | 12
Inj. | 1 | 5 | 1 | 3 | 2
Cryo. | 3 | 2 | 7 | 1 | 0

## Slide 14: RF improvement
The 3 items above have a proportion of 66% in hours and 75% in times in all RF failure from 2009 to 2011.
Improved by conditioning, about once(several hrs) per 2weeks
1st half of 2011: more than 6 times failure per month
2nd half of 2011: less than 3 times failure per month
Item | Times | Hours
Pr/Pf | 16 | 11.54
Readychain | 14 | 8.12
Quench | 6 | 2.83

## Slide 15: Experience of cryogenics
Signal amplifier failure,
recover delayed for lack of spare part
Cable terminal burned down,
32hrs to restart compressor
Solutions:
All systems reviewed, necessary spare parts were managed.
Maintenance procedure were reviewed to avoid neglect.

## Slide 16
Brief Introduction
Operation Statistics
Accelerator Improvement
New Beamlines Commissioning
Summary
Outline

## Slide 17
1. Top up Operation
To provide more stable beam for users
  Electron orbit stability, which we have already taken a lot of methods to keep the beam stabilized within 2~5 microns
  Heating stabililty of beamline monochromator, which must be solved by keeping beam current as stable as possible, i.e. top-up injection
Beam current will oscillate within less than ±0.5% level during top-up operation, that means the injection process will running frequently, mostly once per several minutes, and the users can still do experiment during this period.
Safety is the most important in any case

## Slide 18: Interlock interface

## Slide 19: Before top up
Delivery time = 12 hours
Filling time ~ 5min
∆I / I ~ 30%

## Slide 20
After top up
Delivery time ~ 10min
Filling time = 10s
∆I / I ~ 0.5%

## Slide 21
2. Fast Orbit Feed Back
Steady orbit is always an essential requirement for users. As slow orbit feedback (SOFB) works with a period of ten seconds, the RMS of closed orbit deviation is kept in several microns in both horizontal and vertical plan. To further improve the stability of closed orbit, FOFB has been put into operation, and the RMS of closed orbit deviation is kept about 0.26um/0.25um in horizontal/vertical plan respectively.

## Slide 22: 3. Beam Current Improved Step by Step
Nov. 2013, beam current improved to 230mA
Mar. 2014, beam current improved to 240mA

## Slide 23
4. Hybrid Filling Pattern
Hybrid filling pattern combines the multibunch and single-bunch together to satisfy different user’s needs. Machine study and beamline commissioning has been carried out with 500 bunches of 225mA and 1 bunch of 5mA.

## Slide 24
5. Others
Timing system has been renewed, and the injecting time is reduced, as well as the trigger missing issue is now resolved.
LLRF control of storage ring superconducting cavity is upgraded to enhance its reliability.
Digital LLRF for booster RF cavity is on-going.
Single bunch study is progressing.
Coupling is optimized.

## Slide 25
Brief Introduction
Operation Statistics
Accelerator Improvement
New Beamlines Commissioning
Summary
Outline

## Slide 26: ID commissioning
There are 7 beamlines opened to users, and another 8 are under commissioning. Insertion devices are used for most of the beamlines, which had brought some problems in operation. The IVUs have small impact on beam dynamics, the main difficulty comes from the DEPU for dreamline.
DEPU not only causes COD, but also impact on the working point, coupling, and dynamic aperture.
COD: dipole error
Tune shift: quadrupole error
Coupling(vertical emittance): skew quadrupole field
Dynamic aperture (beam life time/Injection efficiency) : non-linear effects

## Slide 27
U148
U58
COD caused by DEPU
Frame

## Slide 28
EPU 58 Gap
Coupling:
0.1%  0.8% (max)
Beta beating:
~0.4% @ small gap
Coupling
Longitudinal position
Longitudinal position
Horizontal Betabeating
Vertical Betabeating
Coupling & Beta Beating with DEPU

## Slide 29: Compensation of DEPU
  EPU58
    10 quadrupoles feed-forward for tune compensation: Δ＜0.001
    6 Sextupoles feed-forward for coupling compensation: Δ＜ 0.2%
    Optimization to increase the injection efficiency: ~80%
    feed-forward for closed orbit distortion:
    gap: Δ＜4/2μm (H/V), shift: Δ＜2/2μm (H/V)
  EPU148
    feed-forward for closed orbit distortion:
    gap: Δ＜2/1μm (H/V), shift: Δ＜2/2μm (H/V)
  Frame
    feed-forward for closed orbit distortion: Δ＜2/1μm (H/V)

## Slide 30: Compensation of DEPU
Test of closed orbit feed forward for new beamlines:

## Slide 31: Filling Pattern Optimization
500 bunches in 1 train
( 125 bunches + 50 empty buckets ) 4 sub-trains
The beam went unstable with small gap of IDs. Filling pattern had been optimized, and the mode of 4 sub-trains with 125 bunches in each train is finally adopted

## Slide 32
Brief Introduction
Operation Statistics
Accelerator Improvement
New Beamlines Commissioning
Summary
Outline

## Slide 33: Summary
SSRF had a very stable user’s operation during last more than four years.
Beam parameters and machine performance had been improved gradually.
Orbit stability and brightness had been improved dramatically after top up operation.
There are still a lot of works to do in order to satisfy the user: brightness, reliability, etc.
Challenges are waiting for us when more and more beamlines will be built, as well as new insertion devices introduced.

## Slide 34
Thank you ！