## Slide 1: Automation at the CERN Super Proton Synchrotron Automation without losing skills
WAO 2014
James RIDEWOOD - CERN

## Slide 2: Overview
Introduction to the SPS (Super Proton Synchrotron)
Evolution of the SPS
Automation in the SPS
Maintaining skills and motivation
Operator feedback
The future
Conclusions

## Slide 3: Super Proton Synchrotron
LHC 450GeV via TI2
…and TI8 transfer lines
North experimental area - 400GeV
HiRadMat - High-Radiation to Materials 440GeV
AWAKE - Advanced Wakefield Experiment – 400GeV – 2016
  Ex CNGS – CERN Neutrinos to Gran Sasso – 2006-2012
450GeV

## Slide 4: Evolution of the SPS
The LHC requires good quality beam quickly
Reducing time from dump to reinjection is critical for physics
SPS (and the entire injector complex) needs to be ready as soon as LHC requires beam
…..whilst still satisfying our other users
Sometimes a juggling act

## Slide 5: Evolution of the SPS
When I arrived at CERN the SPS was a very different machine
Machine user configuration was rarely changed – usually one single cycle
With multiple cycles, multiple users and the advent of the LHC era these changes can be several times per shift!
Several clients expecting beam simultaneously
We had to automate to keep our heads above water!
2000
2010
Notes: Not only do we have more cycles and users but the configuration changes frequently too

## Slide 6: Automation tools in the SPS
Beam trajectory steering application
Auto tune and chromaticity measurement and correction
Task sequencer

## Slide 7: Beam trajectory steering application
Automated injection oscillation corrections
Automated steering on targets
Closed orbit corrections
Transfer line trajectory corrections
Benefits:
Reliable
Fast
  ….but its use is not trivial
Notes: Trivial, foolproof

## Slide 8: Beam trajectory steering application
Our automation tools are not always simple
Require a certain understanding to get best results
Notes: This perhaps demonstrates that a minimum of understanding is still essential.
These aren’t set and forget tools

## Slide 9: Beam trajectory steering application
Horizontal plane
Vertical plane
Injection line trajectory
Difference of first turn wrt closed orbit for sextants 1 and 2
Corrections converge cycle by cycle to minimise injection oscillations
*

## Slide 10: Beam trajectory steering application
Horizontal plane
Vertical plane
Corrections converge cycle by cycle to minimise injection oscillations
Injection oscillation corrections:
2000 ~20-30 mins
2014 ~3-4 mins
Notes: Another advantage is the possibility of parallel operations so we can be optimising steering on targets for the north area fixed target program whilst correcting injection oscillations for the cycle destined for the LHC

## Slide 11: Beam trajectory steering application
Horizontal plane
Vertical plane
Corrections converge cycle by cycle to minimise injection oscillations
Parallel optimisation is also possible.
e.g. re-steer all 3 north area targets whilst correcting injection oscillations on the cycle destined for the LHC
Notes: Another advantage is the possibility of parallel operations so we can be optimising steering on targets for the north area fixed target program whilst correcting injection oscillations for the cycle destined for the LHC

## Slide 12: Auto tune and chromaticity measurement and correction
Measurement of tune throughout cycle
  Previously only point by point - laborious
Non destructive. Excitation not always necessary
Benefits
  Fast …gets us quickly up and running
  …but again not foolproof! Need to understand what’s behind to be able to take advantage of its labour saving potential
  …and invariably needs fine tuning the old fashioned way after

## Slide 13
Cycle time
Tune value
(Decimal part)
Horizontal tune
Vertical tune
0.62
0.58

## Slide 14
Difference between measured tune and theoretical tune
current tune function
Proposed correction
Proposed correction often requires manual adjustment by an experienced hand before sending to hardware

## Slide 15
Difference between measured tune and theoretical tune
current tune function
Proposed correction
Proposed correction often requires manual adjustment by an experienced hand before sending to hardware
Tune measurement and correction throughout cycle at 10ms intervals:
2000 ~1-2 hours
2014 ~10 mins

## Slide 16: Task sequencer
Good for repetitive tasks such as:
  Preparation of zones for personnel access
  Change of machine configuration e.g. cycling to coast beam
  Switch to economy settings in temporarily unused areas
  With more sequences currently under development
Benefits:
  Same sequence every time – can avoid unnecessary written, manual procedures
  Same results regardless of operator – no variations
    Avoids the necessity that everyone is informed of and remembers changes!

## Slide 17: Task sequencer
A sequencer has existed in one form or another for many years in the SPS
New sequencer inherited from LHC with greater functionality and flexibility
The sequencer is still in its infancy in the SPS but is gaining ground rapidly
Increased use of the sequencer is encouraged by management

## Slide 18: Task sequencer
Functionalities:
Controls middleware – set and get values to and from equipment
Function database – Can revert to a function saved in history
Power converter controls – Change of state: ON, OFF, ECONOMY
Timing events – enable, disable, adjust delays
Software interlocks – mask, unmask, unlatch

## Slide 19
  Typical access sequence

## Slide 20
Run: Execute all tasks sequentially
Suspend: Pause a running sequence
Step: Execute a single task
Skip: skip a task
Stop: Stop a running sequence
In addition, sequence details remain visible and (in rare cases) editable if the need arises
A well designed sequence will execute all tasks as foreseen…but the sequencer gives us the option to:

## Slide 21: Losing skills?
The operator’s skill set has evolved along with the machine
Today’s operators perhaps would not be as immediately adept in performing the tasks that were day-to-day jobs 10-15 years ago
…but the focus has moved and the management of priorities now plays a large part in a multi-cycling machine
  Evaluating and changing machine user configuration to optimise beam availability to users
Operations has not become “easier” despite the advent of automation
Notes: The requirements from operators has moved with the evolution of the machine

## Slide 22: Maintaining skills and motivation
  Each operator is given a specialisation
  This is Diego, a young operator responsible for managing, maintaining and implementing new sequences
  He and fellow operators on the front line identify areas where automation could be of interest
  Operations conceive, create and edit sequences
    Good way for newer operators to understand the underlying processes

## Slide 23: Maintaining skills and motivation
To maintain skill levels operators are actively involved with:
  Machine re-commissioning
  Set-up of new beams
  Machine development sessions
All are examples of when automation may not be ideally suited or easily applied
Notes: Machine re-commissioning –
Since the LHC now more or less imposes shutdowns machines are stopped for greater periods with more work executed in the tunnel
Setting up of new beams –
new multi turn extraction schemes from the PS
Ion beams Argon – Lead in the past, Xenon in the future
Coasting beams
Doublet beams for scrubbing
etc

## Slide 24: Operator feedback
Operators have pride in the good functioning of their machine and are motivated to improve efficiency and performance
  Automation is often seen as an effective means to do so
Automation can mean less time is spent on “mundane” tasks
  Meaning greater availability for more rewarding and stimulating work
Operators do not currently feel threatened by automation
  …as long as operations are involved in how it’s implemented

## Slide 25: The future?
A large amount of our time is spent for measurement and fine tuning of LHC beams
  Bunch intensity and structure
  Longitudinal parameters
  Transverse emittance
    Critical for LHC luminosity!

## Slide 26: Conclusions
Some level of automation is essential for modern accelerator operations
Automation tools are not necessarily straightforward and often require a well-trained operator to get best results
Operator’s skillset has evolved in line with the machine
Despite the assistance of automation operation is not easier today than it was 10-15 years ago
Operators should continue to be implicated in it’s implementation

## Slide 27: Thank you for your attention
http://xkcd.com/1319/